## Slide 1: Design for Testability
CSE 244A
Monday November 18, 2019

## Slide 2: Outline
What is Design-for-Test?
Scan Flop
Scan Chain
Applying Tests through Scan Chains
Cost of Scan Testing
Partial Scan

## Slide 3: What is Design-for-Test?
Up to now, we’ve been looking at how to effectively test existing designs…
But what if we could alter/enhance our design to improve the testability of our designs?
  Testability:
    Controllability – how well can we drive stimulus to design
    Observability – how well can we observe the effects of that stimulus
Design-for-Test is designed to improve testability to either:
  Enhance coverage
  Reduce test cost

## Slide 4: Scan Flip Flop – Base Element of DFT
D
Q
SEL
0
1
CLK
Q
TC
SCANIN
D
CLK
Scan Flip Flops (SFF) give alternate non-functional method for loading data into Flip Flop
Functional Flip Flops can be converted to Scan Flip Flop by adding a Scan MUX
Two new input signals:
  TC – Test Control
    TC = 0: Scan Mode
    TC = 1: Functional Mode
  SCANIN – Scan Input is alternate input for loading data

## Slide 5: Scan Chains linking Scan Cells
Primary Inputs
D
Q
Primary Outputs
D
Q
D
Q
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
CLOCK
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q

## Slide 6: Scan Chains linking Scan Cells
Primary Inputs
Primary Outputs
D
Q
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK

## Slide 7: Scan Chains linking Scan Cells
Primary Inputs
Primary Outputs
TC
D
Q
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK

## Slide 8: Scan Chains linking Scan Cells
Primary Inputs
Primary Outputs
SCANIN
D
Q
SCANOUT
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK

## Slide 9: Scan Chains linking Scan Cells
Primary Inputs
Primary Outputs
SCANIN
TC
D
Q
SCANOUT
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK

## Slide 10: Scan Chains linking Scan Cells
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Scan Flops+Scan Chains can turn Sequential Test into Combination Test
CLOCK

## Slide 11: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK

## Slide 12: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1
1
0
X
P
Shift (Load Pattern 1)
A1
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus

## Slide 13: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1
1 2
0 0
X X
P P
Shift (Load Pattern 1)
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
A1
B1

## Slide 14: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1
1 2 3
0 0 0
X X X
P P P
Shift (Load Pattern 1)
A1
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
B1
C1

## Slide 15: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1
1 2 3 4
0 0 0 0
X X X X
P P P P
Shift (Load Pattern 1)
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
A1
B1
C1
D1

## Slide 16: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1
1 2 3 4 5
0 0 0 0 0
X X X X X
P P P P P
Shift (Load Pattern 1)
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
B1
A1
C1
D1
E1

## Slide 17: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1
1 2 3 4 5 6
0 0 0 0 0 0
X X X X X X
P P P P P P
Shift (Load Pattern 1)
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
C1
B1
A1
D1
E1
F1

## Slide 18: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1
1 2 3 4 5 6 7
0 0 0 0 0 0 0
X X X X X X X
P P P P P P P
Shift (Load Pattern 1)
A1
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
B1
C1
F1
E1
D1
G1

## Slide 19: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1
1 2 3 4 5 6 7 8
0 0 0 0 0 0 0 0
X X X X X X X X
P P P P P P P P
Shift (Load Pattern 1)
A1
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
B1
C1
F1
E1
D1
G1
H1

## Slide 20: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
A1
Pattern 1, Step 1: Enable Test Mode, Scan Chains Load Test Stimulus
B1
C1
F1
E1
D1
G1
H1
I1

## Slide 21: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
P
-
X
1
10
Shift (Load Pattern 1)
Capture (P1)
Q1
R1
S1
V1
U1
T1
W1
Y1
Z1
SFF
Pattern 1, Step 2: Change to Functional Mode, Capture from Comb Logic

## Slide 22: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
11
A2
0
P
Q1
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
R1
S1
V1
U1
T1
W1
Y1
Z1
A2

## Slide 23: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
S1
V1
U1
T1
W1
Y1
Z1
B2
11 12
A2 B2
0 0
P P
Q1 R1
A2

## Slide 24: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
V1
U1
T1
W1
Y1
Z1
B2
A2
11 12 13
A2 B2 C2
0 0 0
P P P
Q1 R1 S1
C2

## Slide 25: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
V1
U1
W1
Y1
Z1
B2
A2
C2
11 12 13 14
A2 B2 C2 D2
0 0 0 0
P P P P
Q1 R1 S1 T1
D2

## Slide 26: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
V1
W1
Y1
Z1
B2
A2
C2
D2
11 12 13 14 15
A2 B2 C2 D2 E2
0 0 0 0 0
P P P P P
Q1 R1 S1 T1 U1
E2

## Slide 27: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
W1
Y1
Z1
B2
A2
C2
D2
E2
11 12 13 14 15 16
A2 B2 C2 D2 E2 F2
0 0 0 0 0 0
P P P P P P
Q1 R1 S1 T1 U1 V1
F2

## Slide 28: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
Y1
Z1
B2
A2
C2
D2
E2
F2
G2
11 12 13 14 15 16 17
A2 B2 C2 D2 E2 F2 G2
0 0 0 0 0 0 0
P P P P P P P
Q1 R1 S1 T1 U1 V1 W1

## Slide 29: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus
Z1
B2
A2
C2
D2
E2
F2
G2
11 12 13 14 15 16 17 18
A2 B2 C2 D2 E2 F2 G2 H2
0 0 0 0 0 0 0 0
P P P P P P P P
Q1 R1 S1 T1 U1 V1 W1 Y1
H2

## Slide 30: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
Shift (Load Pattern 1)
A2
B2
C2
F2
E2
D2
G2
H2
I2
P
-
X
1
10
Capture (P1)
Pattern 1, Step 3: Enable Test Mode, Scan Chains Unload Captured Data
SFF
11 12 13 14 15 16 17 18 19
A2 B2 C2 D2 E2 F2 G2 H2 I2
0 0 0 0 0 0 0 0 0
P P P P P P P P P
Q1 R1 S1 T1 U1 V1 W1 Y1 Z1
Shift (Unload Pattern 1, Load Pattern 2)
Pattern 2, Step 1: Scan Chains Load Test Stimulus

## Slide 31: Applying Tests through Scan Chains
Primary Inputs
Primary Outputs
SCANIN
TC
SCANOUT
COMB LOGIC
COMB LOGIC
COMB LOGIC
COMB LOGIC
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Cycle
SCANIN
SCANOUT
TC
CLOCK
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
P
-
X
1
10
Shift (Load Pattern 1)
Capture (P1)
Q2
R2
S2
V2
U2
T2
W2
Y2
Z2
SFF
Pattern 2, Step 2: Change to Functional Mode, Capture from Comb Logic
11 12 13 14 15 16 17 18 19
A2 B2 C2 D2 E2 F2 G2 H2 I2
0 0 0 0 0 0 0 0 0
P P P P P P P P P
Q1 R1 S1 T1 U1 V1 W1 Y1 Z1
Shift (Unload Pattern 1, Load Pattern 2)
P
-
X
1
20
Capture (P2)
...

## Slide 32: Test Cost for Scan Patterns
- Number of Scan Flip Flops, length of one shift sequence
- Length of one capture sequence
- Number of scan test patterns
, where is Test Cycles
, where is Test Time, is Period of Tester Clock
Cycle
SCANIN
SCANOUT
TC
CLOCK
A1 B1 C1 D1 E1 F1 G1 H1 I1
1 2 3 4 5 6 7 8 9
0 0 0 0 0 0 0 0 0
X X X X X X X X X
P P P P P P P P P
11 12 13 14 15 16 17 18 19
P
-
X
1
A2 B2 C2 D2 E2 F2 G2 H2 I2
0 0 0 0 0 0 0 0 0
P P P P P P P P P
Q1 R1 S1 T1 U1 V1 W1 Y1 Z1
10
Shift (Load Pattern 1)
Shift (Unload Pattern 1, Load Pattern 2)
Capture (P1)
P
-
X
1
20
Capture (P2)

## Slide 33: Scan Chain Stitching
SCANIN
SCANOUT
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
Scan Chains configured based on SFF physical location
VS
1
2
3
4
5
6
7
8
9
Two Reasons:
Routing congestion contributes to area overhead of test-only logic
-- the faster our scan chains work, the lower our test time
SCANIN
SCANOUT
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
SFF
1
2
3
4
5
6
7
8
9

## Slide 34: Cost of Design-for-Test
Design-for-Test can significantly reduce test time, but has other impacts on circuit
  Circuit area overhead of Scan MUX, Scan Chain routing, TC signal routing
  Performance impact of Scan MUXs on Functional Paths
  Potential yield impact of test-only failures
  Implementation effort
Design-for-Test logic consumes 5-10% of overall chip area for current industrial designs
Still, Quality/Cost benefits of improved Testability outweigh other (not insignificant) negative impacts of Design-for-Test

## Slide 35: Alternate Technique – Partial Scan
Full Scan
Every functional flop becomes scan flop
Partial Scan
Strategically convert functional flops to scan flops
Partial scan gives opportunity to get benefits of scan while saving on circuit area
Clock not shown
(Only CK1 needed)

## Slide 36: Cycle-Free Example
F1
F2
F3
Level = 1
2
F1
F2
F3
Level = 1
2
3
3
dseq = 3
s - graph
Circuit
All faults are testable. See Example 8.6.

## Slide 37: Relevant Results
Theorem 8.1: A cycle-free circuit is always initializable. It is also initializable in the presence of any non-flip-flop fault.
Theorem 8.2: Any non-flip-flop fault in a cycle-free circuit can be detected by at most dseq + 1 vectors.
ATPG complexity: To determine that a fault is untestable in a cyclic circuit, an ATPG program using nine-valued logic may have to analyze 9Nff time-frames, where Nff is the number of flip-flops in the circuit.

## Slide 38: A Partial-Scan Method
Select a minimal set of flip-flops for scan to eliminate all cycles.
Alternatively, to keep the overhead low only long cycles may be eliminated.
In some circuits with a large number of self-loops, all cycles other than self-loops may be eliminated.

## Slide 39: The MFVS Problem
For a directed graph find a set of vertices with smallest cardinality such that the deletion of this vertex-set makes the graph acyclic.
The minimum feedback vertex set (MFVS) problem is NP-complete; practical solutions use heuristics.
A secondary objective of minimizing the depth of acyclic graph is useful.
1
2
3
4
5
6
L=3
1
2
3
4
5
6
L=2
L=1
s-graph
A 6-flip-flop circuit

## Slide 40: Partial vs. Full Scan: S5378
Original
2,781
179
0
0.0%
4,603
35/49
70.0%
70.9%
5,533 s
414
414
Full-scan
2,781
0
179
15.66%
4,603
214/228
99.1%
100.0%
5 s
585
105,662
Number of combinational gates
Number of non-scan flip-flops
(10 gates each)
Number of scan flip-flops
(14 gates each)
Gate overhead
Number of faults
PI/PO for ATPG
Fault coverage
Fault efficiency
CPU time on SUN Ultra II
200MHz processor
Number of ATPG vectors
Scan sequence length
Partial-scan
2,781
149
30
2.63%
4,603
65/79
93.7%
99.5%
727 s
1,117
34,691

## Slide 41: Test Compression
CSE 244A
18 November 2019
Content primarily constructed from: L.-T. Wang, C.-W. Wu, and X. Wen, VLSI Test Principles and Architectures: Design for Testability, Morgan Kaufmann, 2006.

## Slide 42: Outline
Motivation for Test Compression
Decompression
  Broadcast-Scan-Based Techniques
  Code-Based Techniques
  Linear Techniques
Compaction
  Combinational (Space)
  Sequential (Time)
Challenges of Compression

## Slide 43: Test Compression Motivation
Big Problem: Designs are growing larger – 200K+ scan flops may exist in modern designs
  If we use the same formula from before…
  … each test pattern could take 200K+ cycles
  What if we divide the scan flops across multiple scan chains?

## Slide 44: Single Scan Chain…
Primary Inputs
Primary Outputs
SCANIN
TC
D
Q
SCANOUT
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK

## Slide 45: …Becomes Three Scan Chains
Primary Inputs
Primary Outputs
SCANIN1
TC
D
Q
SCANOUT3
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK
SCANIN2
SCANIN3
SCANOUT2
SCANOUT1
Parallelizes data input, reducing effective pattern length by 3X

## Slide 46: Test Compression Motivation
  But, this brings another problem…
  Number of available primary input/output pins (also called tester channels) impact overall cost of test*
Reduces pattern length by 3X, but increases number of scanins/scanouts by 3X
  For input pins: what if we give up on controllability to save tester channels?
  For output pins: what if we give up on observability to save tester channels?
    *High number of tester channels can reduce potential multi-site testing (impacting overall throughput), increase probe-card complexity/cost…
Key idea: How can we give up the least to get the most benefit?

## Slide 47: Broadcast Scan-in Data to all Scan Chains
Primary Inputs
Primary Outputs
SCANIN1
TC
D
Q
SCANOUT3
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK
SCANOUT2
SCANOUT1
Retains pattern length, reduces scan-in pins, but gives up on full controllability…

## Slide 48: Why does Test Compression work?
Within a test cube, there may be unspecified input bits
These unspecified bits provide opportunity for leveraging to improve test cost
Test Compaction
Merging test cubes to cover more faults in fewer patterns
Test Compression
Design techniques to increase test stimulus effect
SCANIN
SCANOUT
1
U
1
U
0
U
U
U
U
Typically both are used in practice – ATPG must understand and work upon Test Compression Architecture

## Slide 49: Broadcast-Scan-Based Techniques
Broadcasting of data from one input to multiple internal bits
Broadcast Scan [Lee 1998], [Lee 1999]
  Simple fanout of input data to multiple scan chains (or circuits)
0
0
1
0
0
1
0
0
1
1
0
1
0
1
0
0
0
0
0
01
010

## Slide 50: Broadcast-Scan-Based Techniques
Illinois Scan [Hamzaoglu 1999], [Hsu 2001]
  Broadcast Mode: Simple fanout (similar to [Lee 1998])
  Serial Mode: Scan chains reconfigured to form one long scan chain, providing full controllability
Broadcast Mode
Serial Mode
Complementary modes can extract benefits of one technique, while using other modes to counter its weaknesses
Other advanced Broadcast-Scan techniques leverage reconfigurability and multiple scan inputs

## Slide 51: Code-Based Techniques
Use common data compression methods to encode test cubes
Dictionary Code Compression [Reddy 2002]
  Fixed-length code words fed into scan inputs used to represent test stimulus on internal scan chains
Test Stimulus
Symbols
Code Words
Symbols Encoded
Divided into Symbols
010
100
However, dictionaries can only store so many bits… they are typically not scalable to large and complex designs with many different needed input patterns
Dictionary
Input | Output
00 | 00010
01 | 01100
10 | 10010
11 | 00101
01
10
0
0
0
1
0
Dictionary
Input | Output
00 | 00010
01 | 01100
10 | 10010
11 | 00101
0
1
1
0
0
0
0
0
1
1
0
0
Dictionary
Input | Output
00 | 00010
01 | 01100
10 | 10010
11 | 00101
0
0
1
0
0
0
1
0
0
0
1
1
1
0
0
Dictionary
Input | Output
00 | 00010
01 | 01100
10 | 10010
11 | 00101
IN1
IN2
Cycle 1
IN1
IN2
IN1
IN2
IN1
IN2
Cycle 2
Cycle 3
Cycle 4

## Slide 52: Code-Based Techniques
Run-Length Encoding [Jas 1998]
  Fixed-length b-bit codewords determine variable-length symbols defined by run-length of 0s
Other advanced Code-Based compression techniques deploy Huffman and Golomb encoding
00100010100000011000001
Internal Scan Chain
2 “0”s
3
1
6
0
5
Symbol | Codeword
1 | 000
01 | 001
001 | 010
0001 | 011
00001 | 100
000001 | 101
0000001 | 110
0000000 | 111
Top-Level Scan In
010 011 001 110 000 101
This can also be paired with other decompression architecture techniques to increase amount of “0”s in stimulus

## Slide 53: Linear Techniques
Utilizes XOR and Flip Flop logic to perform decompression of test cubes solvable through linear system of equations
Combinational Decompressors [Bayraktaroglu 2001]
  XOR network constructed with fanouts from scan in pins
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
System of Equations defined by XOR network and decompressor input-to-output relationship solved to determine input stimulus

## Slide 54: Linear Techniques
Sequential Decompressors
  Through incorporation of FFs, variables in the temporal dimension can also be brought into system of equations
Example: Linear Feedback Shift Register (LFSR) with Input Taps
Complex System-of-Equations for test cube compression obtainable with just two input pins

## Slide 55: Test Compression – Compaction
On the input side, we’re leveraging one bit (or a few bits) at the scan in pins to represent many bits within the scan chains
On the output side, we need many bits within scan chains to be represented by a single bit (or a few bits) at the output pins
If what we care about is observing fault effect, what logic can help us retain fault effect in observation?

## Slide 56: Test Compression – Transparent Gate
Transparent gate: change in input will always be transferred to a change in the output
 | 0 | 1 | X | D | 
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | X | D | 
X | 0 | X | X | X | X
D | 0 | D | X | D | 0
 | 0 |  | X | 0 | 
 | 0 | 1 | X | D | 
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | X | D | 
X | 0 | X | X | X | X
D | 0 | D | X | D | 0
 | 0 |  | X | 0 | 
 | 0 | 1 | X | D | 
0 | 0 | 1 | X | D | 
1 | 1 | 0 | X |  | D
X | X | X | X | X | X
D | D |  | X | 0 | 1
 |  | D | X | 1 | 0
 | 0 | 1 | X | D | 
0 | 0 | 1 | X | D | 
1 | 1 | 0 | X |  | D
X | X | X | X | X | X
D | D |  | X | 0 | 1
 |  | D | X | 1 | 0
Forward Implication Tables
AND Gate
XOR Gate
Fault effect propagated when non-controlling value on other input…
… but blocked when controlling value on other input
For XOR gate, either value is non-controlling.
Single fault effect always propagated to output, no matter value on other input

## Slide 57: XOR Compression as compactor
Primary Inputs
Primary Outputs
SCANIN1
TC
D
Q
D
Q
COMB LOGIC
COMB LOGIC
D
Q
COMB LOGIC
COMB LOGIC
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
CLOCK
SCANIN2
SCANIN3
SCANOUT1
XOR
XOR
Retains pattern length, reduces scan-in pins, but gives up on full observability…

## Slide 58: Test Compactor Techniques
Combinational (Space) Compaction
  Simple XOR Network can be deployed to combine output of many scan chains
Single fault effect on input to XOR Network compactor will be propagated to output.
Many internal chains compacted into one top-level signal.

## Slide 59: Test Compactor Techniques
Sequential (Time) Compaction
  XOR gates and Flip Flops used to compact multiple inputs over multiple clock cycles
Example: Multiple-Input Signature Register (MISR)
Single fault effect on input to MISR Network compactor will be captured and retained until signature read-out

## Slide 60: Challenges of Compression
Impact of “X”s in compactors
Let’s look again at the forward implication table of an XOR gate
 | 0 | 1 | X | D | 
0 | 0 | 1 | X | D | 
1 | 1 | 0 | X |  | D
X | X | X | X | X | X
D | D |  | X | 0 | 1
 |  | D | X | 1 | 0
 | 0 | 1 | X | D | 
0 | 0 | 1 | X | D | 
1 | 1 | 0 | X |  | D
X | X | X | X | X | X
D | D |  | X | 0 | 1
 |  | D | X | 1 | 0
XOR Gate
Xs on either input produce X at output
Xs corrupt fault detection!!!
XOR
XOR
XOR
XOR
XOR
XOR
XOR
X
0
1
1
1
0
1
X
X
X
1
1
0
Any X on input to compactor overrides any fault detection on other inputs
Also significant effort in design/DFT on “cleaning” design to remove sources of Xs
State-of-the-art industrial and research techniques are often focused around “X-tolerant” compactors
D

## Slide 61: Challenges of Compression
Aliasing of Fault Effect
Again, the forward implication table of an XOR gate
 | 0 | 1 | X | D | 
0 | 0 | 1 | X | D | 
1 | 1 | 0 | X |  | D
X | X | X | X | X | X
D | D |  | X | 0 | 1
 |  | D | X | 1 | 0
 | 0 | 1 | X | D | 
0 | 0 | 1 | X | D | 
1 | 1 | 0 | X |  | D
X | X | X | X | X | X
D | D |  | X | 0 | 1
 |  | D | X | 1 | 0
XOR Gate
If two faults come together in an XOR compressor, they can cancel each other out and prevent detection
XOR
XOR
XOR
XOR
XOR
XOR
XOR
D
0
1
0
1
1
0
1
1
D or is not retained if two fault effects meet each other within an XOR
D
D
D
1
Consideration required in scan chain stitching, compactor construction, test pattern generation to avoid such cases

## Slide 62: Challenges of Compression
Debug and Diagnosis of Failures
XOR
XOR
XOR
XOR
XOR
XOR
XOR
D
0
1
0
1
1
0
1
1
Which of compactor inputs (scan chains) is failing?
D
Observation of the fault effect is great for achieving coverage, but gives little information to locate failures for debug purposes. Diagnosis techniques for failing flop identification may report in terms of confidence
1
1
0
D
All we see is the D at the failing output…
Output – Compactor
Input – Decompressor
Industrial solutions often also include other modes for improved controllability/observability in debug
(Much like serial mode in Illinois Scan Architecture)
If custom internal stimulus is desired, SAT solver analysis from ATPG tools is likely needed. Further, some of these custom test cubes might not be deployable in certain decompression architectures
SoE needs solving for all desired test stimulus