## Slide 1: CSE 140 Discussion

## Slide 2
S
R
y
Q
Q = (R+y)’
y = (S+Q)’
 |  |  | t0 |  | t1 |  | t2 |  | t3 | 
id | S | R | Qt | yt | Qt | yt | Qt | yt | Qt | yt
0 | 0 | 0 | 0 | 0 |  |  |  |  |  | 
1 | 0 | 0 | 0 | 1 |  |  |  |  |  | 
2 | 0 | 0 | 1 | 0 |  |  |  |  |  | 
3 | 0 | 0 | 1 | 1 |  |  |  |  |  | 
4 | 0 | 1 | 0 | 0 |  |  |  |  |  | 
5 | 0 | 1 | 0 | 1 |  |  |  |  |  | 
6 | 0 | 1 | 1 | 0 |  |  |  |  |  | 
7 | 0 | 1 | 1 | 1 |  |  |  |  |  | 
8 | 1 | 0 | 0 | 0 |  |  |  |  |  | 
9 | 1 | 0 | 0 | 1 |  |  |  |  |  | 
10 | 1 | 0 | 1 | 0 |  |  |  |  |  | 
11 | 1 | 0 | 1 | 1 |  |  |  |  |  | 
12 | 1 | 1 | 0 | 0 |  |  |  |  |  | 
13 | 1 | 1 | 0 | 1 |  |  |  |  |  | 
14 | 1 | 1 | 1 | 0 |  |  |  |  |  | 
15 | 1 | 1 | 1 | 1 |  |  |  |  |  | 
Truth table of SR latch with incremental steps in time
Lecture 7, Slide 17

## Slide 3
 |  |  | t0 |  | t1 |  | t2 |  | t3 | 
id | S | R | Qt | yt | Qt | yt | Qt | yt | Qt | yt
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
2 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
5 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
9 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
14 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Lecture 7, Slide 18
Qy\SR | 00 | 01 | 10 | 11
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
“State Table” of SR latch

## Slide 4
01
11
00
10
00
10
10
01
00
00
11
10
01
00
01
11
10
11
01
11
Q y
State
SR
Q y
State
Transition
Present
State
Next
State
State diagram
\SR Qy | 00 | 01 | 10 | 11
00 | 11 | 01 | 10 | 00
01 | 01 | 01 | 10 | 00
10 | 10 | 01 | 10 | 00
11 | 00 | 01 | 10 | 00
State Table and State Diagram
State Table
Lecture 7, Slide 20

## Slide 5
SR=01 (RESET) : (Q,y) = (0,1)
SR=10 (SET) : (Q,y) = (1,0)
SR=00 (NO CHANGE)
So (Q,y) should not become (0,0) or (1,1)
Solutions: Avoid the case that SR = (1,1).
SR=11 (ILLEGAL) : (Q,y) = (0,0)
Characteristic Expression
Q(t+1) = S(t)+R’(t)Q(t)
Q(t+1)
NS (next state)
0 0 0 - 1
1 1 0 - 1
PS
inputs
00 01 11 10
State table
SR
Q(t)
SR Latch
Lecture 7, Slide 26
\SR Qy | 00 | 01 | 10 | 11
00 | 11 | 01 | 10 | 00
01 | 01 | 01 | 10 | 00
10 | 10 | 01 | 10 | 00
11 | 00 | 01 | 10 | 00

## Slide 6: D-Latch vs. D-FF
D-Latch
  Analogy: Door
  CLK = 1 : Q = D
  CLK = 0 : Q = Qprev
D-FF
  Analogy: Camera
  CLK = 0 to 1 : Q = D
  Otherwise : Q = Qprev

## Slide 7: Pattern Recognizer FSM
Example:
  y = 1 if x(t − 2, t) = 101 or 010
  y = 0 otherwise
PS \ Input |  | X = 0 | X = 1
-- | S0 | S1, 0 | S2, 0
0 | S1 | S1, 0 | S3, 0
1 | S2 | S4, 0 | S2, 0
01 | S3 | S4, 1 | S2, 0
10 | S4 | S1, 0 | S3, 1
State Diagram
State Table

## Slide 8: HW3 Questions?

## Slide 9: Describing Sequential Ckts
State diagrams and next-state tables nor are suitable for describing very large digital designs
  large circuits must be described in a modular fashion -- as a collection of cooperating FSMs
BSV is a modern programming language to describe cooperating FSMs

## Slide 10: Modulo-4 counter circuit
Modulo-4
counter
inc
Read the
counter
q0t+1 = ~inc∙q0t + inc∙~q0t
q1t+1 = ~inc∙q1t + inc∙~q1t∙q0t + inc∙q1t∙~q0t
“Optimized” logic
q0t+1 = inc  q0t
q1t+1 = (inc == 1) ? q0t  q1t : q1t
q0
inc
1
0
q1

## Slide 11: Modulo-4 counter circuit
q0t+1 = ~inc∙q0t + inc∙~q0t
q1t+1 = ~inc∙q1t + inc∙~q1t∙q0t + inc∙q1t∙~q0t
“Optimized” logic
q0t+1 =inc  q0t
q1t+1 =(inc == 1) ? q0tq1t:q1t
q0
inc
1
0
q1
PS\input | inc=0 | inc=1
00 | 00 | 01
01 | 01 | 10
10 | 10 | 11
11 | 11 | 00
PS: q1t q0t, NS: q1t+1 q0t+1

## Slide 12: modulo4 counter in BSV
module moduloCounter(Counter);
Reg#(Bit#(2)) cnt <- mkReg(0);
method Action inc;
cnt <={!cnt[1]&cnt[0] | cnt[1]&!cnt[0], !cnt[0]};
endmethod
method Bit#(2) read;
return cnt;
endmethod
endmodule
~cnt[1]&…
inc.en
read
cnt
Notes: (Andy) ‘r’ and ‘w’ are ‘_read’ and ‘_write’ in BSV, but ‘r’ and ‘w’ are much easier to write on slides.
(Andy) I changed ‘||’ to ‘|’ in the logic because || is the boolean or and | is the bitwise or.

## Slide 13: Interface
Modulo counter has the following interface, i.e., type
An interface can have many different implementations
  For example, the numbers may be represented as Gray code
interface Counter;
method Action inc;
method Bit#(2) read;
endinterface

## Slide 14: Modules
A module in BSV is like a class definition in Java or C++
  It has internal state
  The internal state can only be read and manipulated by the (interface) methods
  An action specifies which state elements are to be modified
  Actions are atomic -- either all the specified state elements are modified or none of them are modified (no partially modified state is visible)

## Slide 15: FIFO Interface
interface Fifo#(numeric type size, type t);
method Bool notFull;
method Bool notEmpty;
method Action enq(t x);
method Action deq;
method t first;
endinterface
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first
- enq should be called only if notFull returns True;
- deq and first should be called only if notEmpty returns True

## Slide 16: One-Element FIFO Implementation
module mkCFFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Bool notFull;
return !v;
endmethod
method Bool notEmpty;
return v;
endmethod
method Action enq(t x);
v <= True; d <= x;
endmethod
method Action deq;
v <= False;
endmethod
method t first;
return d;
endmethod
endmodule
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first

## Slide 17: FIFO Module: methods with guarded interfaces
Every method has a guard (rdy wire); the value returned by a value method is meaningful only if its guard is true
Every action method has an enable signal (en wire); an action method is invoked (en is set to true) only if the guard is true
Guards make it possible to transfer the responsibility of the correct use of a method from the user to the compiler
Guards are extraordinarily convenient for programming and also enhance modularity of the code
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
interface Fifo#(numeric type size,
type t);
method Action enq(t x);
method Action deq;
method t first;
endinterface

## Slide 18: One-Element FIFO Implementation with guards
module mkCFFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x)
v <= True; d <= x;
endmethod
method Action deq
v <= False;
endmethod
method t first
return d;
endmethod
endmodule
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
if (!v);
if (v);
if (v);