## Slide 1: CSE 140 Discussion
Homework 4

## Slide 2
Decoder Definition
0
y0
y1
y7
I0
I1
I2
1
2
0
1
2
3
4
5
6
7
E (enable)
n inputs
n= 3
2n outputs
23= 8
yi = 1 if E = 1 & (In, In-1,…, I0 ) = i
yi = 0, otherwise
.
.
A digital module that converts a binary address to the assertion of the addressed device.

## Slide 3: Decoder Application
{Decoder, OR} is a universal set
  Any Boolean function can be implemented with a set of decoders and OR gates.
If the function is described in the sum-of-products (minterms) form:
  Decoder produces the minterms.
  OR gate produces the sum from the minterms.
  Ignore the don’t-cares.

## Slide 4
Problem 1: Example
Implement 3-variable functions with a 3:8 decoder and OR gates.
f1(a,b,c) = Σm(1,2,4) + Σd(0,5),
f2(a,b,c) = Σm(2,3) + Σd(1,4),
f3(a,b,c) = Σm(0,5,6)
I0
y0
.
.
y7
c
b
a
I1
I2
0
1
2
3
4
5
6
7
E=1
y1
y2
y4
f1
y2
y3
f2
y0
y6
f3
y5

## Slide 5
4 variables: Implement a 4:16 decoder using 3:8 decoders.
I0
y0
.
y7
I1
I2
0
1
2
3
4
5
6
7
I0
y8
.
y15
I1
I2
0
1
2
3
4
5
6
7
a
d
c
b
What if the function has more than three variables?

## Slide 6
E
D0
I2, I1, I0
D1
y0
y7
y8
y15
D7
y56
y63
E
I2, I1, I0
I2, I1, I0
I5, I4, I3
…
…
6 variables: Implement a 6:64 decoder using 3:8 decoders.
What if the function has more than three variables?

## Slide 7
Encoder Definition
A digital module that converts the assertion of a device to the binary address of the device.
8 inputs
3 outputs
y0
y1
y2
0
1
2
3
4
5
6
7
E
A
I0
I7
0
1
2
(yn-1,.., y0 ) = I if E = 1 & one i s.t. Ii = 1
(yn-1,.., y0 ) = 0, otherwise.
A = 1 if E = 1 & one i s.t. Ii = 1
A = 0, otherwise.
Only one input can be asserted

## Slide 8
Priority Encoder
(yn-1,.., y0 ) = I if E = 1 & Ii = 1 & Ik = 0 for all k > i
(yn-1,.., y0 ) = 0, otherwise.
Eo = 1 if E = 1 & Ii = 0 for all i
Gs = 1 if E = 1 & i s.t. Ii = 1
More than one input can be asserted
0
1
2
3
4
5
6
7
E
Eo
Gs
I0
I7
y0
y1
y2
0
1
2
E

## Slide 9
y32, y31, y30
I31-24
Eo
Gs
y22, y21, y20
I25-16
Eo
Gs
y12, y11, y10
I15-8
Eo
Gs
y02, y01, y00
I7-0
Eo
Gs
E
Problem 2: Example

## Slide 10
y = Di where i = (Sn-1, .. , S0) if E = 1
y = 0, otherwise
E
y
D2n-1-D0
(Data input)
Sn-1,0
(Selector or Address)
Multiplexer Definition
A digital module that selects one of data inputs according to the binary address of the selector.

## Slide 11: Multiplexer Application
{Mux} is a universal set.
  Any Boolean function can be implemented with a set of multiplexers.
  Use Shannon’s expansion to decompose the function into smaller ones
  simplify the decomposed functions using K-maps
  Feed the smaller functions to data inputs of the mux and use the the expansion variable as the selector.

## Slide 12
Implement f (a,b,c) = Σm (0,2,6) + Σd(1) using an 8-input Mux.
En
y
a
b
c
S2
S1
S0
0
1
2
3
4
5
6
7
id | abc | f
0 | 000 | 1
1 | 001 | -
2 | 010 | 1
3 | 011 | 0
4 | 100 | 0
5 | 101 | 0
6 | 110 | 1
7 | 111 | 0
Problem 3: Example

## Slide 13
E
y
a
b
S1
S0
0
1
2
3
ab | c = 0 | c = 1 | D(c)
00 | 1 | - | D0 = 1
01 | 1 | 0 | D1 = c’
10 | 0 | 0 | D2 = 0
11 | 1 | 0 | D3 = c’
Implement f (a,b,c) = Σm (0,2,6) + Σd(1) using an 4-input Mux.
What if the we have to use smaller muxes?

## Slide 14
E
0
1
a
y
a\bc | 00 | 01 | 10 | 11 | D(b,c)
0 | 1 | - | 1 | 0 | D0
1 | 0 | 0 | 1 | 0 | D1
Implement f (a,b,c) = Σm (0,2,6) + Σd(1) using an 2-input Mux.
What if the we have to use smaller muxes?

## Slide 15
Implement f (a,b,c) = Σm (0,2,6) + Σd(1) using an 2-input Mux.
What if the we have to use smaller muxes?
E
0
1
a
y
D0 (b,c) = c’
D1 (b,c) = bc’
D1
c = 0 | 1 | 1
c = 1 | - | 0
 | b = 0 | b = 1
c = 0 | 0 | 1
c = 1 | 0 | 0
 | b = 0 | b = 1
a\bc | 00 | 01 | 10 | 11 | D(b,c)
0 | 1 | - | 1 | 0 | D0 = c’
1 | 0 | 0 | 1 | 0 | D1 = bc’
D0

## Slide 16
D1 (b,c) = bc’
E
E
c’
0
1
a
b
y
0
1
D0
D1
b\c | 0 | 1 | D(c)
0 | 0 | 0 | D0= 0
1 | 1 | 0 | D1 = c’
Implement f (a,b,c) = Σm (0,2,6) + Σd(1) using an 2-input Mux.
What if the we have to use smaller muxes?