## Slide 1: CSE140 HW5 Preparation
Xinyuan Wang
06/01/2018

## Slide 2: Q1: Subtractor
How we implement the subtraction between binary bits?
  Given 2 binary inputs and borrow in bit , calculate
  A full subtractor with input output
  Write the truth table and derive Boolean expressions
borrow out

## Slide 3: Q1: Subtractor
A four bit borrow look ahead subtractor
  Refer to the carry look ahead adder
A N-bit carry look ahead adder is usually much faster than ripple than a ripple carry adder if N>16
  Delays for carry look ahead and ripple carry adder are defined in slide 18, 23 of lecture 14

## Slide 4: Q1: Subtractor
A four bit borrow look ahead subtractor
  Use full subtractors and minimal logic gates
  Generate and propagate signals for each column
    When a column will generate a borrow out?
    When a column will propagate a borrow in to borrow out?

## Slide 5: Q2: Prefix Adder
Compute the carry in for each column as fast as possible
Has stages
Column holds , so ,
Compute the prefixes:
  the generate and propagate for a block spanning bits
  Note: are the generate and propagate for column
The sum of each column

## Slide 6: Q2: Prefix Adder
A 16-bit Prefix Adder from slide 27 of Lecture 14
  Has 4 stages
  Compute for each column
  Compute for each box
  Compute sum with for each column

## Slide 7: Q2: Prefix Adder
Calculate sum of 13, 6 with a 4-bit Prefix Adder,
  Compute for each column
  Compute for each box
  Compute sum with for each column

## Slide 8: Q2: Prefix Adder
Calculate sum of 13, 6 with a 4-bit Prefix Adder,
  1101 + 0110
  Compute for each column

## Slide 9: Q2: Prefix Adder
Calculate sum of 13, 6 with a 4-bit Prefix Adder,
  1101 + 0110
  Compute for each column
  Compute for each box
  Stage 1:
  Stage 2:

## Slide 10: Q2: Prefix Adder
Calculate sum of 13, 6 with a 4-bit Prefix Adder,
  1101 + 0110
  Compute for each column
  Compute for each box
  Compute sum with for each column

## Slide 11: Q3: Carry Save Adder
A Redundant Number System
Save the Partial Solution for Multiple Additions
One Bit Propagation for Each Addition

## Slide 12: Q3: Carry Save Adder
Example: calculate the sum of 23, 11, 17
Weight | 32 | 16 | 8 | 4 | 2 | 1
n1=23 | 0 | 1 | 0 | 1 | 1 | 1
n2=11 | 0 | 0 | 1 | 0 | 1 | 1
n3=17 | 0 | 1 | 0 | 0 | 0 | 1

## Slide 13: Q3: Carry Save Adder
Example: calculate the sum of 23, 11, 17
Weight | 64 | 32 | 16 | 8 | 4 | 2 | 1
n1=23 | 0 | 0 | 1 | 0 | 1 | 1 | 1
n2=11 | 0 | 0 | 0 | 1 | 0 | 1 | 1
n3=17 | 0 | 0 | 1 | 0 | 0 | 0 | 1
n1 | 00 | 00 | 10 | 00 | 10 | 10 | 10
n2 | 0 | 0 | 0 | 1 | 0 | 1 | 1
A=n1+n2 |  |  |  |  |  |  | 
n3 |  |  |  |  |  |  | 
B=A+n3 |  |  |  |  |  |  | 
Sum |  |  |  |  |  |  | 

## Slide 14: Q3: Carry Save Adder
Example: calculate the sum of 23, 11, 17
Weight | 64 | 32 | 16 | 8 | 4 | 2 | 1
n1=23 | 0 | 0 | 1 | 0 | 1 | 1 | 1
n2=11 | 0 | 0 | 0 | 1 | 0 | 1 | 1
n3=17 | 0 | 0 | 1 | 0 | 0 | 0 | 1
n1 | 00 | 00 | 10 | 00 | 10 | 10 | 10
n2 | 0 | 0 | 0 | 1 | 0 | 1 | 1
A=n1+n2 | 00 | 00 | 10 | 10 | 11 | 01 | 00
n3 |  |  |  |  |  |  | 
B=A+n3 |  |  |  |  |  |  | 
Sum |  |  |  |  |  |  | 

## Slide 15: Q3: Carry Save Adder
Example: calculate the sum of 23, 11, 17
Weight | 64 | 32 | 16 | 8 | 4 | 2 | 1
n1=23 | 0 | 0 | 1 | 0 | 1 | 1 | 1
n2=11 | 0 | 0 | 0 | 1 | 0 | 1 | 1
n3=17 | 0 | 0 | 1 | 0 | 0 | 0 | 1
n1 | 00 | 00 | 10 | 00 | 10 | 10 | 10
n2 | 0 | 0 | 0 | 1 | 0 | 1 | 1
A=n1+n2 | 00 | 00 | 10 | 10 | 11 | 01 | 00
n3 | 0 | 0 | 1 | 0 | 0 | 0 | 1
B=A+n3 |  |  |  |  |  |  | 
Sum |  |  |  |  |  |  | 

## Slide 16: Q3: Carry Save Adder
Example: calculate the sum of 23, 11, 17
Weight | 64 | 32 | 16 | 8 | 4 | 2 | 1
n1=23 | 0 | 0 | 1 | 0 | 1 | 1 | 1
n2=11 | 0 | 0 | 0 | 1 | 0 | 1 | 1
n3=17 | 0 | 0 | 1 | 0 | 0 | 0 | 1
n1 | 00 | 00 | 10 | 00 | 10 | 10 | 10
n2 | 0 | 0 | 0 | 1 | 0 | 1 | 1
A=n1+n2 | 00 | 00 | 10 | 10 | 11 | 01 | 00
n3 | 0 | 0 | 1 | 0 | 0 | 0 | 1
B=A+n3 | 00 | 01 | 00 | 11 | 00 | 10 | 10
Sum |  |  |  |  |  |  | 
An extra non-redundant addition is needed!

## Slide 17: Q3: Carry Save Adder
Example: calculate the sum of 23, 11, 17
Weight | 64 | 32 | 16 | 8 | 4 | 2 | 1
n1=23 | 0 | 0 | 1 | 0 | 1 | 1 | 1
n2=11 | 0 | 0 | 0 | 1 | 0 | 1 | 1
n3=17 | 0 | 0 | 1 | 0 | 0 | 0 | 1
n1 | 00 | 00 | 10 | 00 | 10 | 10 | 10
n2 | 0 | 0 | 0 | 1 | 0 | 1 | 1
A=n1+n2 | 00 | 00 | 10 | 10 | 11 | 01 | 00
n3 | 0 | 0 | 1 | 0 | 0 | 0 | 1
B=A+n3 | 00 | 01 | 00 | 11 | 00 | 10 | 10
Two bits of B | 0 | 1 | 0 | 1 | 0 | 0 | 0
 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Sum |  |  |  |  |  |  | 

## Slide 18: Q3: Carry Save Adder
Example: calculate the sum of 23, 11, 17
Weight | 64 | 32 | 16 | 8 | 4 | 2 | 1
n1=23 | 0 | 0 | 1 | 0 | 1 | 1 | 1
n2=11 | 0 | 0 | 0 | 1 | 0 | 1 | 1
n3=17 | 0 | 0 | 1 | 0 | 0 | 0 | 1
n1 | 00 | 00 | 10 | 00 | 10 | 10 | 10
n2 | 0 | 0 | 0 | 1 | 0 | 1 | 1
A=n1+n2 | 00 | 00 | 10 | 10 | 11 | 01 | 00
n3 | 0 | 0 | 1 | 0 | 0 | 0 | 1
B=A+n3 | 00 | 01 | 00 | 11 | 00 | 10 | 10
Two bits of B | 0 | 1 | 0 | 1 | 0 | 0 | 0
 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Sum | 0 | 1 | 1 | 0 | 0 | 1 | 1

## Slide 19: Q4: Counter
A modulo-m counter
  Count from 0 to m-1 when CNT = 1 and LD = 0
  Don’t forget the labels
LD
D
Q
TC
CNT
CLR
Clk
Q (t+1) = (0, 0, .. , 0) if CLR = 1
= D if LD = 1 and CLR = 0
= (Q(t)+1)mod n if LD = 0, CNT = 1 and CLR = 0
= Q (t) if LD = 0, CNT = 0 and CLR = 0
TC = 1 if Q (t) = n-1 and CNT = 1
= 0 otherwise

## Slide 20: Q4: Counter
Design a a-to-b counter with modulo-16 counter
  Count from a to b , a 5-to-11 counter from slide 14 of Lecture 15
  Set (D3D2D1D0) = a
  When CNT = 1 and (Q3Q2Q1Q0) = b, set LD = 1 then
  Comb logic for LD only takes 1s
  (Q3Q2Q1Q0) = 1011
A 5-to-11 Counter
Q3 Q2 Q1 Q0
Clk
CLR
CNT
D3 D2 D1 D0
0 1 0 1 (a)
LD
Q3
Q0
X
Q1
(b)
(Q3Q2Q1Q0) = 1111 cannot be reached in this 5-to-11 counter!

## Slide 21: Q4: Counter
Design a counter of an arbitrary sequence with a modulo-16 counter
  an arbitrary sequence 3,4,5, 0,1,2, 8,9
  when , load
  when , load
  when , load
Q3 Q2 Q1 Q0
Clk
CLR
CNT
D3 D2 D1 D0
LD
X

## Slide 22: Q4: Counter
Design a counter of an arbitrary sequence with a modulo-16 counter
  an arbitrary sequence 3,4,5, 0,1,2, 8,9
  when , load
  when , load
  when , load
  Set LD = 1 for load new number,
  otherwise LD = 0. If number not in the
  sequence, set LD as don’t care.
  Set D = new number when LD = 1,
  otherwise set D as don’t cares.
Id | Q3Q2Q1Q0 | LD | D3 | D2 | D1 | D0
0 | 0000 | 0 | - | - | - | -
1 | 0001 | 0 | - | - | - | -
2 | 0010 | 1 | 1 | 0 | 0 | 0
3 | 0011 | 0 | - | - | - | -
4 | 0100 | 0 | - | - | - | -
5 | 0101 | 1 | 0 | 0 | 0 | 0
8 | 1000 | 0 | - | - | - | -
9 | 1001 | 1 | 0 | 0 | 1 | 1
6,7,10~15 | 0110, 0111, 1010~1111 | - | - | - | - | -

## Slide 23: Q4: Counter
Design a counter of an arbitrary sequence with a modulo-16 counter
  an arbitrary sequence 3,4,5, 0,1,2, 8,9
  Use K-maps
Id | Q3Q2Q1Q0 | LD | D3 | D2 | D1 | D0
0 | 0000 | 0 | - | - | - | -
1 | 0001 | 0 | - | - | - | -
2 | 0010 | 1 | 1 | 0 | 0 | 0
3 | 0011 | 0 | - | - | - | -
4 | 0100 | 0 | - | - | - | -
5 | 0101 | 1 | 0 | 0 | 0 | 0
8 | 1000 | 0 | - | - | - | -
9 | 1001 | 1 | 0 | 0 | 1 | 1
6,7,10~15 | 0110, 0111, 1010~1111 | - | - | - | - | -
 | 00 | 01 | 11 | 10
00 | 0 | 0 | X | 0
01 | 0 | 1 | X | 1
11 | 0 | X | X | X
10 | 1 | X | X | X
 | 00 | 01 | 11 | 10
00 | 0 | 0 | X | 0
01 | 0 | 1 | X | 1
11 | 0 | X | X | X
10 | 1 | X | X | X
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
LD =