## Slide 1: CSE 140 Lecture 11 Standard Combinational Modules
CK Cheng
CSE Dept.
UC San Diego

## Slide 2: Part III - Standard Combinational Modules
Introduction
Decoder
  Behavior, Logic, Usage
Encoder
Multiplexer (Mux)
  Behavior, Logic, Usage
Demultiplexier (DeMux)

## Slide 3: Part III - Standard Combinational Modules
Signal Transport
Decoder: Decode address
Encoder: Encode address
Multiplexer (Mux): Select data by address
Demultiplexier (DeMux): Direct data by address
Shifter: Shift bit location
Data Operator
Adder: Add two binary numbers
Multiplier: Multiply two binary numbers

## Slide 4: Interconnect: Decoder, Encoder, Mux, DeMux
Processors
Decoder: Decode the address to assert the addressed device
Mux: Select the inputs according to the index addressed by the control signals
P1
Memory Bank
Mux
P2
Pk
Demux
Decoder
Mux
Data
Address
Address k
Address 2
Address 1
Data 1
Data k
Arbiter
n
n-m
m
2m

## Slide 5: 1. Decoder
Definition
Logic Diagram
Application (Universal Set)
Tree of Decoders

## Slide 6: iClicker: Decoder Definition
A device that decodes
An electronic device that converts signals from one form to another
A machine that converts a coded text into ordinary language
A device or program that translates encoded data into its original format
All of the above

## Slide 7
Decoder Definition: A digital module that converts a binary address to the assertion of the addressed device
0
y0
y1
y7
I0
I1
I2
1
2
0
1
2
3
4
5
6
7
E (enable)
n inputs
n= 3
2n outputs
23= 8
yi = 1 if E= 1 & (I2, I1, I0 ) = i
yi= 0 otherwise
n to 2n decoder function:
.
.

## Slide 8: 1. Decoder: Definition
N inputs, 2N outputs
One-hot outputs: only one output HIGH at most
E
E= 1

## Slide 9: 1. Decoder: Definition
E
iClicker: A 3-input decoder has how many outputs?
2 outputs
4 outputs
8 outputs
10 outputs

## Slide 10
Decoder Definition
iClicker: For a 3-input decoder, suppose
(E,I2,I1,I0)=(1,0,0,0), then (y7,y6, …, y0) is equal to:
(00000000)
(00000001)
(00000010)
(01000000)
(10000000)
0
y0
y1
y7
I0
I1
I2
1
2
0
1
2
3
4
5
6
7
E (enable)
3 inputs
8 outputs
.
.

## Slide 11
Decoder: Logic Diagram (Inside a decoder)
y0
A1’
A0’
y1
En
y3
.
.
yi = mi En
y0 = 1 if (A1, A0 ) = (0,0) & En = 1
y3 = A1A0En

## Slide 12: 1. Decoder: Definition
PI Q: What is the output Y3:0 of the 2:4 decoder for (A1, A0) = (1,0)?
(1, 1, 0, 0 )
(1, 0, 1, 1)
(0, 0, 1, 0)
(0, 1, 0, 0)

## Slide 13
Decoder Application: universal set {Decoder, OR}
Example:
Implement the following functions with a 3-input decoder and OR gates.
i) f1(a,b,c) = Σm(1,2,4)
ii) f2(a,b,c) = Σm(2,3),
iii) f3(a,b,c) = Σm(0,5,6)

## Slide 14
Decoder Application: universal set {Decoder, OR}
Decoder produces minterms when E=1.
We can use an OR gate to collect the minterms to cover the On-set.
For the Don’t Care-Set, we can just ignore the terms.

## Slide 15
Decoder Application: universal set {Decoder, OR}
Example:
Implement functions
f1(a,b,c) = Σm(1,2,4) + Σd(0,5),
f2(a,b,c) = Σm(2,3) + Σd(1,4),
f3(a,b,c) = Σm(0,5,6)
with a 3-input decoder and OR gates.
I0
y0
.
.
y7
c
b
a
I1
I2
0
1
2
3
4
5
6
7
E=1
y1
y2
y4
f1
y2
y3
f2
y0
y6
f3
y5

## Slide 16: Decoders
OR minterms
E=1

## Slide 17
Tree of Decoders: Scale up the size of the decoders using a tree structure
Implement a 4-24 decoder with 3-23 decoders.
I0
y0
.
y7
I1
I2
0
1
2
3
4
5
6
7
I0
y8
.
y15
I1
I2
0
1
2
3
4
5
6
7
a
d
c
b

## Slide 18
Implement a 6-26 decoder with 3-23 decoders.
E
D0
I2, I1, I0
D1
y0
y7
y8
y15
D7
y56
y63
E
I2, I1, I0
I2, I1, I0
I5, I4, I3
Tree of Decoders
…
…

## Slide 19: PI Q: A four variable switching function f(a,b,c,d) can be implemented using which of the following?
1:2 decoders and OR gates
2:4 decoders and OR gates
3:8 decoders and OR gates
All of the above
None of the above

## Slide 20: 2. Encoder
Definition
Logic Diagram
Priority Encoder

## Slide 21: iClicker: Definition of Encoder
Any program, circuit or algorithm which encodes
In digital audio technology, an encoder is a program that converts an audio WAV file into an MP3 file
A device that convert a message from plain text into code
A circuit that is used to convert between digital video and analog video
All of the above

## Slide 22
Encoder Definition: A digital module that converts the assertion of a device to the binary address of the device.
yn-1 …y0
E
A
I2n-1…I0
8 inputs
3 outputs
y0
y1
y2
0
1
2
3
4
5
6
7
E
At most one Ii = 1.
(yn-1,.., y0 ) = i if Ii = 1 & E = 1
(yn-1,.., y0 ) = 0 otherwise.
A = 1 if E = 1 and one i s.t. Ii = 1
A = 0 otherwise.
Encoder Description:
A
I0
I7
0
1
2

## Slide 23
Encoder: Logic Diagram
En
I1
I3
I5
I7
y0
En
I2
I3
I6
I7
y1
En
I4
I5
I6
I7
y2
En
I0
I1
I6
I7
A
.
.

## Slide 24
Priority Encoder:
0
1
2
3
E
Eo
Gs
I0
I3
y0
y1
0
1

## Slide 25
Priority Encoder: Definition
Description: Input (I2n-1,…, I0), Output (yn-1 ,…,,y0)
(yn-1 ,…,,y0) = i if Ii = 1 & E = 1 & Ik = 0
for all k > i (high bit priority) or
for all k< i (low bit priority).
Eo = 1 if E = 1 & Ii = 0 for all i,
Gs = 1 if E = 1 & i s.t. Ii = 1.
E
(Gs is like A, and Eo passes on enable).
0
1
2
3
4
5
6
7
E
Eo
Gs
I0
I7
y0
y1
y2
0
1
2

## Slide 26
Priority Encoder: Implement a 32-input priority encoder w/ 8 input priority encoders (high bit priority).
y32, y31, y30
I31-24
Eo
Gs
y22, y21, y20
I23-16
Eo
Gs
y12, y11, y10
I15-8
Eo
Gs
y02, y01, y00
I7-0
Eo
Gs
E