## Slide 1: CS 140 Lecture 14 Standard Combinational Modules
Professor CK Cheng
CSE Dept.
UC San Diego
Some slides from Harris and Harris

## Slide 2: Part III. Standard Modules
Interconnect
Operators. Adders Multiplier
Adders 1. Representation of numbers
  2. Full Adder
  3. Half Adder
  4. Ripple-Carry Adder
  5. Carry Look Ahead Adder
  6. Prefix Adder
  7. Carry Save Adder
  ALU
  Multiplier
  Division

## Slide 3: Operators
Specification: Data Representations
Arithmetic: Algorithms
Logic: Synthesis
Layout: Placement and Routing

## Slide 4: 1. Representation
2’s Complement
-x: 2n-x
1’s Complement
-x: 2n-x-1

## Slide 5
1. Representation
Id | 2’s comp. | 1’s comp.
0 | 0 | 15
-1 | 15 | 14
-2 | 14 | 13
-3 | 13 | 12
-4 | 12 | 11
-5 | 11 | 10
-6 | 10 | 9
-7 | 9 | 8
-8 | 8 | 
2’s Complement
-x: 2n-x
e.g. 16-x
1’s Complement
-x: 2n-x-1
e.g. 16-x-1

## Slide 6
1. Representation
Id | -Binary | sign mag | 2’s comp | 1’s comp
0 | 0000 | 1000 | 0000 | 1111
-1 | 0001 | 1001 | 1111 | 1110
-2 | 0010 | 1010 | 1110 | 1101
-3 | 0011 | 1011 | 1101 | 1100
-4 | 0100 | 1100 | 1100 | 1011
-5 | 0101 | 1101 | 1011 | 1010
-6 | 0110 | 1110 | 1010 | 1001
-7 | 0111 | 1111 | 1001 | 1000
-8 |  |  | 1000 | 

## Slide 7: Representation
1’s Complement
For a negative number, we take the positive number and complement every bit.
2’s Complement
For a negative number, we do 1s complement and plus one.
(bn-1, bn-2, …, b0): -bn-12n-1+ sumi<n-1 bi2i

## Slide 8: Representation
2’s Complement
x+y
x-y: x+2n-y= 2n+x-y
-x+y: 2n-x+y
-x-y: 2n-x+2n-y
= 2n+2n-x-y
-(-x)=2n-(2n-x)=x
1’s Complement
x+y
x-y: x+2n-y-1= 2n-1+x-y
-x+y: 2n-x-1+y=2n-1-x+y
-x-y: 2n-x-1+2n-y-1
= 2n-1+2n-x-y-1
-(-x)=2n-(2n-x-1) -1=x

## Slide 9: Examples
2 + 3 = 5
0 0 1 0
0 0 1 0
+ 0 0 1 1
0 1 0 1
2 - 3 = -1 (2’s)
0 0 0 0
0 0 1 0
+ 1 1 0 1
1 1 1 1
2 - 3 = -1 (1’s)
0 0 1 0
+ 1 1 0 0
1 1 1 0
-2 - 3 = -5 (2’s)
1 1 0 0
1 1 1 0
+ 1 1 0 1
1 0 1 1
-2 - 3 = -5 (1’s)
1 1 0 0
1 1 0 1
+ 1 1 0 0
1 0 0 1
1
1 0 1 0
3 + 5 = 8
0 1 1 1
0 0 1 1
+ 0 1 0 1
1 0 0 0
C4C3
Check for overflow (2’s)
-3 + -5 = -8
1 1 1 1
1 1 0 1
+ 1 0 1 1
1 0 0 0
C4C3

## Slide 10
Addition: 2’s Complement Overflow
In 2’s complement:
overflow = cn xor cn-1
Exercise:
Demonstrate the overflow with more examples.
Prove the condition.

## Slide 11
Adder
MUX
Sum
minus
b
b’
a
Cout
overflow
C4
C3
Cin
Addition and Subtraction using 2’s Complement

## Slide 12: 1-Bit Adders

## Slide 13: Half Adder
a b Cout Sum
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0
Sum = ab’ + a’b = a + b
Cout = ab
Cout
Sum
a
b
HA
a b
Sum
Cout

## Slide 14
Full Adder Composed of Half Adders
HA
HA
a
b
cin
x
sum
cout
OR
sum
cout
cout
sum
y
z

## Slide 15
Full Adder Composed of Half Adders
HA
HA
a
b
cin
x
sum
cout
sum
cout
cout
sum
y
z
Id | a | b | cin | x | y | z | cout | sum
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
3 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
5 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0
6 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
7 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1
Id | x | z | cout
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | -

## Slide 16: Adder
Several types of carry propagate adders (CPAs) are:
  Ripple-carry adders (slow)
  Carry-lookahead adders (fast)
  Prefix adders (faster)
Carry-lookahead and prefix adders are faster for large adders but require more hardware.
  Symbol

## Slide 17: Ripple-Carry Adder
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow

## Slide 18: Ripple-Carry Adder Delay
The delay of an N-bit ripple-carry adder is:
tripple = NtFA
where tFA is the delay of a full adder

## Slide 19: Carry-Lookahead Adder
Compress the logic levels of Cout
Some definitions:
  Generate (Gi) and propagate (Pi) signals for each column:
    A column will generate a carry out if Ai AND Bi are both 1.
  Gi = Ai Bi
    A column will propagate a carry in to the carry out if Ai OR Bi is 1.
  Pi = Ai + Bi
    The carry out of a column (Ci) is:
  Ci+1 = Ai Bi + (Ai + Bi )Ci = Gi + Pi Ci

## Slide 20: Carry Look Ahead Adder
C1 = a0b0 + (a0+b0)c0 = g0 + p0c0
C2 = a1b1 + (a1+b1)c1 = g1 + p1c1 = g1 + p1g0 + p1p0c0
C3 = a2b2 + (a2+b2)c2 = g2 + p2c2 = g2 + p2g1 + p2p1g0 + p2p1p0c0
C4 = a3b3 + (a3+b3)c3 = g3 + p3c3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0c0
qi = aibi pi = ai + bi
a3 b3
g3
p3
a2 b2
g2
p2
a1 b1
g1
p1
a0 b0
g0
p0
c1
c2
c3
c4
c0

## Slide 21: Carry-Lookahead Addition
Step 1: compute generate (G) and propagate (P) signals for columns (single bits)
Step 2: compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate block

## Slide 22: 32-bit CLA with 4-bit blocks

## Slide 23: Carry-Lookahead Adder Delay
Delay of an N-bit carry-lookahead adder with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
where
  tpg : delay of the column generate and propagate gates
  tpg_block : delay of the block generate and propagate gates
  tAND_OR : delay from Cin to Cout of the final AND/OR gate in the k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16

## Slide 24: Prefix Adder
Computes the carry in (Ci-1) for each of the columns as fast as possible and then computes the sum:
Si = (Ai Å Bi) Å Ci
Computes G and P for 1-bit, then 2-bit blocks, then 4-bit blocks, then 8-bit blocks, etc. until the carry in (generate signal) is known for each column
Has log2N stages

## Slide 25: Prefix Adder
A carry in is produced by being either generated in a column or propagated from a previous column.
Define column -1 to hold Cin, so G-1 = Cin, P-1 = 0
Then, the carry in to col. i = the carry out of col. i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1 is the generate signal spanning columns i-1 to -1.
There will be a carry out of column i-1 (Ci-1) if the block spanning columns i-1 through -1 generates a carry.
Thus, we rewrite the sum equation:Si = (Ai Å Bi) Å Gi-1:-1
Goal: Compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (These are called the prefixes)

## Slide 26: Prefix Adder
The generate and propagate signals for a block spanning bits i:j are:
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words, these prefixes describe that:
  A block will generate a carry if the upper part (i:k) generates a carry or if the upper part propagates a carry generated in the lower part (k-1:j)
  A block will propagate a carry if both the upper and lower parts propagate the carry.

## Slide 27: Prefix Adder Schematic

## Slide 28: Carry Save Adder
Fast and low power addition for multiple additions
A Redundant Number System
Save the Partial Solution for Multiple Additions
One Bit Propagation for Each Addition

## Slide 29: Carry Save Adder: A Redundant Number System
For each digit, we have two bits
  (0,0) (0,1) (1,0) (1,1)
Weight 0 (0,0)
Weight 1 (0,1) (1,0)
Weight 2 (1,1)

## Slide 30: Carry Save Adder: A Simple Example
Weight | 32 | 16 | 8 | 4 | 2 | 1
n1 | 0 | 0 | 1 | 0 | 0 | 1
n2 | 0 | 1 | 1 | 1 | 1 | 0
n3 | 0 | 1 | 1 | 1 | 0 | 1
n4 | 0 | 0 | 1 | 0 | 1 | 1

## Slide 31: Carry Save Adder: A Simple Example
Weight | 64 | 32 | 16 | 8 | 4 | 2 | 1
n1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
n2 | 0 | 0 | 1 | 1 | 1 | 1 | 0
n3 | 0 | 0 | 1 | 1 | 1 | 0 | 1
n4 | 0 | 0 | 0 | 1 | 1 | 1 | 1
n1 | 00 | 00 | 00 | 10 | 10 | 00 | 10
n2 | 0 | 0 | 1 | 1 | 1 | 1 | 0
A=n1+n2 | 00 | 00 | 11 | 01 | 00 | 10 | 10
n3 | 0 | 0 | 1 | 1 | 1 | 0 | 1
B=A+n3 | 00 | 01 | 11 | 00 | 10 | 11 | 00
n4 | 0 | 0 | 0 | 1 | 1 | 1 | 1
C=B+n4 | 00 | 10 | 11 | 11 | 01 | 10 | 10
Sum | 1 | 0 | 1 | 0 | 1 | 1 | 1

## Slide 32: Carry Save Adder: One Digit Logic Diagram
For digit i, the addition of addend in two bits and addend in one bit produces the carry out and sum.
The sum and the carry out from digit i-1 become the two bit output at digit i.
Full Adder
Full Adder
Sum
Cout
A
B
Cin
Addend in two bit
Addend in one bit
Carry out form digit i-1
Sum in two bits
Carry out to digit i+1

## Slide 33: Carry Save Adder: Three Digit Logic Diagram
For digit i, the addition of addend in two bits and addend in one bit produces the carry out and sum.
The sum and the carry out from digit i-1 become the two bit output at digit i.
Full Adder
Full Adder
Sum
Cout
A
B
Cin
Addend in two bit
Addend in one bit
Cout form digit i-1
Sum in two bits
Cout to digit i+1
Full Adder
Full Adder
Sum
Cout
A
B
Cin
Addend in two bit
Addend in one bit
Cout form digit i-2
Sum in two bits
Full Adder
Full Adder
Sum
Cout
A
B
Cin
Addend in two bit
Addend in one bit
Sum in two bits
Cout to digit i+2

## Slide 34: Carry Save Adder
Procedure of carry save addition system
Convert the first addend to the redundant number system
For intermediate solution, perform carry save addition.
Split the redundant number into two numbers.
Perform the addition on the two numbers to general the solution.

## Slide 35: Prefix Adder Delay
The delay of an N-bit prefix adder is:
tPA = tpg + log2N(tpg_prefix ) + tXOR
where
  tpg is the delay of the column generate and propagate gates (AND or OR gate)
  tpg_prefix is the delay of the black prefix cell (AND-OR gate)

## Slide 36: Adder Delay Comparisons
Compare the delay of 32-bit ripple-carry, carry-lookahead, and prefix adders. The carry-lookahead adder has 4-bit blocks. Assume that each two-input gate delay is 100 ps and the full adder delay is 300 ps.

## Slide 37: Adder Delay Comparisons
Compare the delay of 32-bit ripple-carry, carry-lookahead, and prefix adders. The carry-lookahead adder has 4-bit blocks. Assume that each two-input gate delay is 100 ps and the full adder delay is 300 ps.
  tripple = NtFA = 32(300 ps) = 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns

## Slide 38: Comparator: Equality

## Slide 39: Comparator: Less Than
For unsigned numbers

## Slide 40: Arithmetic Logic Unit (ALU)
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 41: ALU Design
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 42: Set Less Than (SLT) Example
Configure a 32-bit ALU for the set if less than (SLT) operation. Suppose A = 25 and B = 32.

## Slide 43: Set Less Than (SLT) Example
Configure a 32-bit ALU for the set if less than (SLT) operation. Suppose A = 25 and B = 32.
  A is less than B, so we expect Y to be the 32-bit representation of 1 (0x00000001).
  For SLT, F2:0 = 111.
  F2 = 1 configures the adder unit as a subtracter. So 25 - 32 = -7.
  The two’s complement representation of -7 has a 1 in the most significant bit, so S31 = 1.
  With F1:0 = 11, the final multiplexer selects Y = S31 (zero extended) = 0x00000001.

## Slide 44: Shifters
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb).
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111

## Slide 45: Shifter Design

## Slide 46: Shifter
Can be implemented with a mux
s
d
yi
En
1
0
3 2 1 0
xi+1
xi-1
xi
s
d
xn
x0
x-1
xn-1
yn-1
y0
En
s / n
l / r
yi = xi-1 if En = 1, s = 1, and d = L
= xi+1 if En = 1, s = 1, and d = R
= xi if En = 1, s = 0
= 0 if En = 0

## Slide 47: Barrel Shifter
O or 1 shift
O or 2 shift
O or 4 shift
x
s0
s1
s2
y
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
shift

## Slide 48: Shifters as Multipliers and Dividers
A left shift by N bits multiplies a number by 2N
  Ex: 00001 << 2 = 00100 (1 × 22 = 4)
  Ex: 11101 << 2 = 10100 (-3 × 22 = -12)
The arithmetic right shift by N divides a number by 2N
  Ex: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Ex: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)

## Slide 49: Multipliers
Steps of multiplication for both decimal and binary numbers:
  Partial products are formed by multiplying a single digit of the multiplier with the entire multiplicand
  Shifted partial products are summed to form the result

## Slide 50: 4 x 4 Multiplier

## Slide 51: Division Algorithm
Q = A/B
R: remainder
D: difference
R = A
for i = N-1 to 0
D = R - B
if D < 0 then Qi = 0, R’ = R // R < B
else Qi = 1, R’ = D // R  B
R = 2R’

## Slide 52: 4 x 4 Divider