## Slide 1: CSE 140 Lecture 16 System Designs
CK Cheng
CSE Dept.
UC San Diego

## Slide 2: System Designs
Introduction
  Methodology and Framework
Components
Specification
Implementation

## Slide 3: Introduction
Methodology
  Approach with success stories.
  Hierarchical designs with interface between the modules (BSV).
Data Subsystem and Control Subsystem
  For n-bit data, each operation takes n times or more in hardware complexity.
  Data subsystem carries out the data operations and transports.
  Control system sequences the data subsystem and itself.

## Slide 4
I. Introduction: Framework
Data
Subsystem
Control
Subsystem
Conditions
Control
Signals
n=128
n=64
Data
Inputs
Control
Inputs
Data
Outputs
Control
Outputs
Start/Request
Done/Acknowledgement

## Slide 5: I. Introduction: Handshaking
start
module S
X
Y
Z
done
Master that
calls module S
X
Y
Z
start
done
Data
Subsystem
Control
Subsystem
Conditions
Control
Signals
n=128
n=64
Data
Inputs
Control
Inputs
Data
Outputs
Control
Outputs
Start/Request
Done/Acknowledgement

## Slide 6: Handshaking
start
done
t
t

## Slide 7: Handshaking: iClicker
The master module that calls module S controls the following signals
Signal start
Signal done
Signals start and done
None of the above

## Slide 8
Data
Subsystem
Control
Subsystem
Components
Storage Modules
Operators
Interconnections
Sequential machines
Functions
Data storage
Data operations
Data transport
Control of data operations
Control of data transports
Control of the sequential system
II. Components

## Slide 9: II. Data Subsystem Components
Storage: Register, RAM, FIFO, LIFO, Counter, Shifter
Operator: ALU, Floating Point Operators
Interconnect: Wire, Buses, Crossbars

## Slide 10
II. Components: Storage Modules, Register
LD
CLR
LD
CLR
D
Q
CLK
Q(t+1) = (0, 0, .. , 0) if CLR = 1
= D if LD = 1 and CLR = 0
= Q(t) if LD = 0 and CLR = 0
LD: Load
CLR: Clear
D
Q

## Slide 11
Modulo-n Counter
Q (t+1) = (0, 0, .. , 0) if CLR = 1
= D if LD = 1 and CLR = 0
= (Q(t)+1)mod n if LD = 0, CNT = 1 and CLR = 0
= Q (t) if LD = 0, CNT = 0 and CLR = 0
TC = 1 if Q (t) = n-1 and CNT = 1
= 0 otherwise
CNT
LD
CLR
LD
D
Q
TC
CNT
CLR
Clk
D
Q
TC

## Slide 12
Storage Component: Registers, Array of Registers
LD
C
R
D
Register Array: If C then Raddress  D
Sharing connections and controls
LD
R
D
Decoder
address
Registers: If C then R  D
C

## Slide 13
Decoder
RAM
Address
Size of RAM larger
than registers
Performance is slower
FIFO (First in first out)
LIFO (Last in first out:
Stack)
Storage Components: RAM, FIFO, LIFO
RAM

## Slide 14: Functional Modules
Op-Sel
A
B
Z
Operation
selection
CASE Op-Sel Is
When F1, Z <= A op1 B
When F2, Z <= A op2 B
.
.
End CASE
Example:
CASE Op-Set Is
Z <= (A + B)mod 2n if Op-Sel=addition,
Z <= (A - B)mod 2n if Op-Sel=subtraction
End CASE
OpA
OpB
Z

## Slide 15: Interconnect Modules (Wires and Switches)
1. Single line (shifting, time sharing)
Single Lines
Band of Wires
Shared Buses
Crossbar
Shift Register
Shift Register

## Slide 16
2. Band of Wires (BUS)
3. Shared Bus
R0
R1
R2
Rn-1
…..
c
y
x
x
y
c
d
0 1 2 .. n-1
0 1 2 .. n-1
MUX
DEMUX
Switches
switch
switch
switch
switch
S
S
x
x
R0
Rn-1
R0
Rn-1

## Slide 17
4. Crossbar (Multiple buses running horizontally)
m simultaneous transfers are possible, but more expensive.
MUX0
MUX1
MUXn-1
…
Bus 0
64
Bus n-1
R0
Rn-1

## Slide 18
III. Specification: Program
Objects (Registers, Outputs of combinational logic)
Operation (Logic, Add, Multiplication, DSP, and etc.)
Assignment
Sequencing
Example:
Signal S1, S2, R[15:0]: FFs, Registers, wires
Z  A + B: Registers, Adder, Interconnect
R1  R2: Registers and Interconnect
Begin, End: Control
if ( ) then ( ), ENDIF: Control

## Slide 19
Ex. If C then R1 S1
Else R2  S2
Endif;
R1
LD
R2
S2
S1
C
If C1 then X  A
Else X  B + C
Endif
If C2 then Rg  X
Endif
MUX
1 0
Adder
B
C
A
Rg
C1
C2
CLK
LD

## Slide 20: VI. Implementation
Example
Handshaking
  Request and Acknowledgement
Datapath Subsystem
  Data Operators
  Data Transporters
Control Subsystem
  One Hot Machine Design

## Slide 21: VI. Implementation: Example
AddModule(X, Y, Z, start, done)
{ Input X[15:0], Y[15:0] type bit-vector,
start type Boolean;
Local-Object A[15:0], B[15:0] type bit-vector;
Output Z[15:0] type bit-vector,
done type Boolean;
S0: If start’ goto S0 || done 1;
S1: A  X || B  Y || done 0;
S2: Z  Add(A, B) || goto S0;
}
Exercise: Go through the handshaking, data subsystem and control subsystem designs.

## Slide 22: AddModule(X,Y,start,done)
start
AddModule
X
Y
Z
done
Call AddModule
X
Y
Z
start
done

## Slide 23: Handshaking
start
done
t
t

## Slide 24: iClicker
Suppose that each step (Si) takes one clock cycle. How many clock cycles does the AddModule take to complete one handshaking iteration?
One cycle
Two cycles
More than two cycles