## Slide 1: CSE 140, Lecture 2 Combinational Logic
CK Cheng
CSE Dept.
UC San Diego

## Slide 2: Combinational Logic Outlines
Introduction
  Scope
  Boolean Algebra (Review)
    Definition
    Duality
    AND/OR Gates
    Expressions vs Circuits
  Handy Tools
    DeMorgan’s Theorem
    Consensus Theorem
    Shannon’s Expansion
Specification
Synthesis

## Slide 3: 1.1 Combinational Logic: Scope
Description
  Language: e.g. C Programming, BSV, Verilog, VHDL
  Boolean algebra
  Truth table: Powerful engineering tool
Design
  Schematic Diagram
  Inputs, Gates, Nets, Outputs
Goal
  Validity: correctness, turnaround time
  Performance: power, timing, cost
  Testability: yield, diagnosis, robustness

## Slide 4: Scope: Boolean algebra, switching algebra, logic
Boolean Algebra: multiple-valued logic, i.e. each variable have multiple values.
Switching Algebra: binary logic, i.e. each variable can be either 1 or 0.
Boolean Algebra ≠ Switching Algebra
BB
Boolean Algebra
Switching Algebra
Two Level Logic

## Slide 5: Scope: Switching Algebra (Binary Values)
1-<5>
Typically consider only two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0 can be represented by specific voltage levels, rotating gears, fluid levels, etc.
Digital circuits usually depend on specific voltage levels to represent 1 and 0
Bit: Binary digit

## Slide 6: Scope: Levels of Logic
Multiple Level Logic: Many layers of two level logic with some inverters, e.g. (((a+bc)’+ab’)+b’c+c’d)’bc+c’e
(A network of two level logic)
Two Level Logic: Sum of products, or product of sums, e.g. ab + a’c + a’b’, (a’+c )(a+b’)(a+b+c’)
Features of Digital Logic Design
Multiple Outputs
Don’t care sets
BB
Boolean Algebra
Switching Algebra
Two Level Logic

## Slide 7: 1.2 Boolean Algebra (Review)
1-<7>
George Boole, 1815-1864
Born to working class parents: Son of a shoemaker
Taught himself mathematics and joined the faculty of Queen’s College in Ireland.
Wrote An Investigation of the Laws of Thought (1854): systematize Aristotle’s logic
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT.

## Slide 8: Review of Boolean Algebra
Let B be a nonempty set with two 2-input operations, a 1-input operation ` (complement), and two distinct elements 0 and 1. Then B is called a Boolean algebra if the following axioms hold.
Associative laws: (a+b)+c=a+(b+c), (a·b) ·c=a·(b·c)
Commutative laws: a+b=b+a, a·b=b·a
Distributive laws: a+(b·c)=(a+b)·(a+c), a·(b+c)=a·b+a·c
Identity laws: a+0=a, a·1=a
Complement laws: a+a’=1, a·a’=0

## Slide 9: Review of Boolean Algebra: Duality
Associative laws | (a+b)+c=a+(b+c) | (a·b) ·c=a·(b·c)
Commutative laws | a+b=b+a | a·b=b·a
Distributive laws | a+(b·c)=(a+b)·(a+c) | a·(b+c)=a·b+a·c
Identity laws | a+0=a | a·1=a
Complement laws | a+a’=1 | a·a’=0
Duality: We swap all operators between (+,.) and interchange all elements between (0,1).
For a theorem if the statement can be proven with the laws of Boolean algebra, then the duality of the statement is also true.

## Slide 10: 1.3 Switching functions: Operators and Digital Logic Gates
AND
Y=AB
Input 0 dominates Y
0 blocks the output
1 passes signal A
Input 1 dominates Y
0 passes signal A
1 blocks the output
A
1
1
A
0
A
A
1
A
A
0
0
A | Y
0 | 1
1 | 0
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
NOT
Y=A’
OR
Y=A+B
id | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 0
2 | 1 | 0 | 0
3 | 1 | 1 | 1

## Slide 11: 1.3 Switching functions: Operators and Digital Logic Gates
AND
Y=ABC
0 blocks the output
1 passes signal A
For AND, only one row is true
(minterm)
0 passes signal A
1 blocks the output
For OR, only one row is false
(maxterm)
OR
Y=A+B+C
id | A | B | C | Y
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 0
7 | 1 | 1 | 1 | 1
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 12: 1.3 Switching functions: Example on AND and OR
AND
Y=A’B’C
Y=A’+B’+C
OR
id | A | B | C | Y
0 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 
2 | 0 | 1 | 0 | 
3 | 0 | 1 | 1 | 
4 | 1 | 0 | 0 | 
5 | 1 | 0 | 1 | 
6 | 1 | 1 | 0 | 
7 | 1 | 1 | 1 | 
A | B | C | Y
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 13: Switching Expressions vs Logic Diagrams
Switching Expression: #literals, #operators
Schematic Diagram: #gates, #nets, #pins
Switching expression is related to logic implementation

## Slide 14
Associativity Laws
(A+B) + C = A + (B+C)
(AB)C = A(BC)
C
A
B
A
B
C
C
A
B
A
B
C
Laws and Logic Diagrams

## Slide 15
Identity Laws A ∙ 1 = A A + 1 = 1
A ∙ 0 = 0 A + 0 = A
Complement Laws A + A’ = 1 A ∙ A’ = 0
Distributive Laws
A ∙(B+C) = A ∙ B + A ∙ C
A+B ∙ C = (A+B) ∙(A+C)
A
B
C
A
C
A
B
A
B
C
A
C
A
B
Laws and Logic Diagrams

## Slide 16: Switching Expression and Logic
Schematic Diagram:
5 primary inputs
1 primary output
4 gates (3 ANDs, 1 OR)
9 signal nets
12 pins
a·b + c·d
a
b
c
d
e
c·d
a·b
y=e·(a·b+c·d)
Boolean Algebra:
5 variables
1 expression
4 operators (3 ANDs, 1 OR)
5 literals
Cost: #gates, #nets, #pins

## Slide 17: Switching Expression and Logic
Schematic Diagram:
5 primary inputs
4 components (gates)
9 signal nets
12 pins
a·b + c·d
a
b
c
d
e
c·d
a·b
y=e·(a·b+c·d)
Boolean Algebra:
5 literals
4 operators
#variables
#operators
#variables + #operators
#literals + 2 #operators - 1
#inputs
#gates
#nets
#pins
None

## Slide 18: Example: f(a,b,c)= ab+a’c+a’b’

## Slide 19: Example: f(a,b,c)= (a’+c)(a+b’)(a+b+c)

## Slide 20: 1.4 Handy Tools
Boolean Algebra
DeMorgan’s Law: Complements
Consensus Theorem
Switching Logic
Shannon’s Expansion
Truth Table
Karnaugh Map (single output, two level logic)
BB
Boolean Algebra
Switching Algebra
Two Level Logic

## Slide 21: DeMorgan’s Theorem and Digital Logic
Y = (AB)’ = A’ + B’
Y = (A + B)’= A’B’
T12. DeMorgan’s Theorem (A+B)’ = A’B’ (AB)’ = A’ + B’

## Slide 22: DeMorgan’s Theorem: Bubble Pushing
Pushing bubbles backward (from the output) or forward (from the inputs) changes the body of the gate from AND to OR or vice versa.
Pushing a bubble from the output back to the inputs puts bubbles on all gate inputs.
Pushing bubbles on all gate inputs forward toward the output puts a bubble on the output and changes the gate body.

## Slide 23: Consensus Theorem
AB+AC+B’C
=AB+B’C
(A+B)(A+C)(B’+C)
=(A+B)(B’+C)
Exercise: to prove the reduction using
Venn Diagrams,
Boolean algebra,
Logic simulation and
Shannon’s expansion
The consensus of AB, B’C is: ?

## Slide 24: Consensus Theorem: Venn Diagrams
AB+AC+B’C : AB+B’C
B
A
C
B
A
C

## Slide 25: Consensus Theorem: Boolean Algebra
AB+AC+B’C
=AB+B’C
(A+B)(A+C)(B’+C)
=(A+B)(B’+C)
AB+AC+B’C
=AB+AC1+B’C
=AB+AC(B+B’)+B’C
=AB+ABC+AB’C+B’C
=AB(1+C)+(A+1)B’C
=AB+B’C

## Slide 26: Consensus Theorem: Logic Simulation
f(A,B,C)= AB+AC+B’C
g(A,B,C)=AB+B’C
Index | A | B | C | AB | AC | B’C | f | g
0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 | 0 | 0 | 1 |  | 
2 | 0 | 1 | 0 | 0 | 0 | 0 |  | 
3 | 0 | 1 | 1 | 0 | 0 | 0 |  | 
4 | 1 | 0 | 0 | 0 | 0 | 0 |  | 
5 | 1 | 0 | 1 | 0 | 1 | 1 |  | 
6 | 1 | 1 | 0 | 1 | 0 | 0 |  | 
7 | 1 | 1 | 1 | 1 | 1 | 0 |  | 

## Slide 28: Consensus Theorem (Examples)
A+A’B
A+A’BC
A(B+C)+A’D
ABC+A’D+BCDE
B
BC
(B+C)D
BCD
BCDE
iClicker: Which one is not a consensus of the expressions on the right.

## Slide 29: Shannon’s Expansion
Shannon’s expansion assumes a switching algebra system
Divide a switching function into smaller functions
Pick a variable x, partition the switching function into two cases: x=1 and x=0
  f(x,y,z,…)= xf(x=1,y,z,…) + x’f(x=0,y,z,…)
For example
  f(x)=xf(1)+x’f(0)
  f(x,y)=xf(1,y)+x’f(0,y)

## Slide 30: Shannon’s Expansion (Example)
Shannon’s expansion:

## Slide 31: Shannon’s Expansion: Example
A. ?=0
B. ?=1.

## Slide 32: Shannon’s Expansion
Decompose the switching function into minterms
  .
id | x | y | f(x,y)
0 | 0 | 0 | f(0,0)
1 | 0 | 1 | f(0,1)
2 | 1 | 0 | f(1,0)
3 | 1 | 1 | f(1,1)
Shannon’s expansion can decompose a switching function into a truth table.

## Slide 33: Shannon’s Expansion vs Truth Table
  Example: f(x,y)= x+ x’y
  .
id | x | y | f(x,y)
0 | 0 | 0 | f(0,0)
1 | 0 | 1 | f(0,1)
2 | 1 | 0 | f(1,0)
3 | 1 | 1 | f(1,1)
Shannon’s expansion can decompose a switching function into a truth table.

## Slide 34: Shannon’s Expansion
Decompose the switching function into minterms
  .
Decompose the switching function into maxterms

## Slide 35: Shannon’s Expansion: Example
Which variable in ab’+ac+bc can be used for expansion?
a
b
c
None of the above

## Slide 36: Shannon’s Expansion: Example
F(A,B,C)=AB’+AC+BC

## Slide 37
Remark: The choice of the variable for expansion is a nontrivial question.

## Slide 38: Review Summary: Switching Algebra and Karnaugh Map
Shannon’s expansion and consensus theorem are used for logic optimization
Shannon’s expansion divides the problem into smaller functions
Consensus theorem finds common terms when we merge small functions
Karnaugh map mimics the above two operations in two dimensional space as a visual aid.

## Slide 39: Part I. Combinational Logic
II) Specification
  1. Language
  2. Boolean Algebra
  Canonical Expression: Sum of minterms and
  Product of maxterms
  3. Truth Table: minterms and maxterms
  4. Incompletely Specified Function

## Slide 40: Decimal Addition
5
+ 7
1 2
Carry Sum
1 1 1
1 0 1
+ 1 1 1
1 1 0 0
Carryout Sums
Carry bits
5
7
12
II. Specification (use addition as an example)
Binary Addition

## Slide 41: Decimal Addition
II. Specification (use addition as an example)
Binary Addition

## Slide 42
II. Specification (use addition as an example)
a
A B
S
Cin
Cout
a
A B
S
Cin
Cout
a
A B
S
Cin
Cout
a
A B
S
Cin
Cout

## Slide 43: Binary Addition: Hardware
Half Adder: Two inputs (a,b) and two outputs (carry, sum).
Full Adder: Three inputs (a,b,cin) and two outputs (carry, sum).

## Slide 44: Half Adder
Truth Table
a
b
Sum
Carry
id | a | b | carry | sum
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
2 | 1 | 0 | 0 | 1
3 | 1 | 1 | 1 | 0

## Slide 45
Switching Function
Switching Expressions:
Sum (a,b) = a’·b + a·b’
Carry (a, b) = a·b
Ex:
Sum (0,0) = 0’·0 + 0·0’ = 0 + 0 = 0
Sum (0,1) = 0’·1 + 0·1’ = 1 + 0 = 1
Sum (1,1) = 1’·1 + 1·1’ = 0 + 0 = 0
a
b
sum
a
b
carry

## Slide 46: BSV notes
{c, s} represents bit concatenation
function Bit#(2) ha(Bit#(1) a, Bit#(1) b);
Bit#(1) s = (~a & b) | (a & ~b);
Bit#(1) c = a & b;
return {c,s};
endfunction

## Slide 47: Full Adder
a
b
sum
cout
cin
id | a | b | cin | cout | sum
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1
3 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0 | 1
5 | 1 | 0 | 1 | 1 | 0
6 | 1 | 1 | 0 | 1 | 0
7 | 1 | 1 | 1 | 1 | 1
Arithmetic:
2cout+sum=a+b+cin

## Slide 48: Minterms
A product of all variables in the function.
A minterm is equal to 1 on exactly one row of the truth table.
id | a | b | c | carry | sum
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | a’b’c
2 | 0 | 1 | 0 | 0 | a’bc’
3 | 0 | 1 | 1 | a’bc | 0
4 | 1 | 0 | 0 | 0 | ab’c’
5 | 1 | 0 | 1 | ab’c | 0
6 | 1 | 1 | 0 | abc’ | 0
7 | 1 | 1 | 1 | abc | abc

## Slide 49: Maxterms
A sum of all variables in the function.
A maxterm is equal to 0 on exactly one row of the truth table.
id | a | b | c | carry | sum
0 | 0 | 0 | 0 | a+b+c | a+b+c
1 | 0 | 0 | 1 | a+b+c’ | 1
2 | 0 | 1 | 0 | a+b’+c | 1
3 | 0 | 1 | 1 | 1 | a+b’+c’
4 | 1 | 0 | 0 | a’+b+c | 1
5 | 1 | 0 | 1 | 1 | a’+b+c’
6 | 1 | 1 | 0 | 1 | a’+b’+c
7 | 1 | 1 | 1 | 1 | 1

## Slide 50: Minterms and Maxterms
id | a | b | c | minterm | maxterm
0 | 0 | 0 | 0 | m0=a’b’c’ | M0=a+b+c
1 | 0 | 0 | 1 | m1=a’b’c | M1=a+b+c’
2 | 0 | 1 | 0 | m2=a’bc’ | M2=a+b’+c
3 | 0 | 1 | 1 | m3=a’bc | M3=a+b’+c’
4 | 1 | 0 | 0 | m4=ab’c’ | M4=a’+b+c
5 | 1 | 0 | 1 | m5=ab’c | M5=a’+b+c’
6 | 1 | 1 | 0 | m6=abc’ | M6=a’+b’+c
7 | 1 | 1 | 1 | m7=abc | M7=a’+b’+c’
Minterms cover all the outputs which are true (1).
Maxterms cover all the outputs which are false (0).

## Slide 51
f1(a,b,c) = a’bc + ab’c + abc’ + abc
a’bc = 1 iff (a,b,c,) = (0,1,1)
ab’c = 1 iff (a,b,c,) = (1,0,1)
abc’ = 1 iff (a,b,c,) = (1,1,0)
abc = 1 iff (a,b,c,) = (1,1,1)
f1(a,b,c) = 1 iff (a,b,c) = (0,1,1), (1,0,1), (1,1,0), or (1,1,1)
Minterms
Ex: f1(1,0,1) = 1’01 + 10’1 + 101’ + 101 = 1
f1(1,0,0) = 1’00 + 10’0 + 100’ + 100 = 0

## Slide 52
f2(a,b,c) = (a+b+c)(a+b+c’)(a+b’+c)(a’+b+c)
a + b + c = 0 iff (a,b,c,) = (0,0,0)
a + b + c’ = 0 iff (a,b,c,) = (0,0,1)
a + b’ + c = 0 iff (a,b,c,) = (0,1,0)
a’ + b + c = 0 iff (a,b,c,) = (1,0,0)
f2(a,b,c) = 0 iff (a,b,c) = (0,0,0), (0,0,1), (0,1,0), (1,0,0)
Maxterms
Ex: f2(1,0,1) = (1+0+1)(1+0+1’)(1+0’+1)(1’+0+1) = 1
f2(0,1,0) = (0+1+0)(0+1+0’)(0+1’+0)(0’+1+0) = 0

## Slide 53
f1(a,b,c) = a’bc + ab’c + abc’ + abc
f2(a,b,c) = (a+b+c)(a+b+c’)(a+b’+c)(a’+b+c)
f1(a, b, c) = m3 + m5 + m6 + m7 = Sm(3,5,6,7)
f2(a, b, c) = M0M1M2M4 = PM(0, 1, 2, 4)
iClicker: Does f1 = f2?
Yes
No.

## Slide 54
Id a b cin carry minterm 4 = ab’c’
0 0 0 0 0 0
1 0 0 1 0 0
2 0 1 0 0 0
3 0 1 1 1 0
4 1 0 0 0 1
5 1 0 1 1 0
6 1 1 0 1 0
7 1 1 1 1 0
The coverage of a single minterm. e.g. m4 = ab’c’
Only one row has a 1.

## Slide 55
Id a b cin carry maxterm 4 = a+b+c
0 0 0 0 0 1
1 0 0 1 0 1
2 0 1 0 0 1
3 0 1 1 1 1
4 1 0 0 0 0
5 1 0 1 1 1
6 1 1 0 1 1
7 1 1 1 1 1
The coverage of a single maxterm. E.g. M4 = a’+b+c
Only one row has a 0.

## Slide 56
f1(a,b,c) = a’bc + ab’c + abc’ + abc
f2(a,b,c) = (a+b+c)(a+b+c’)(a+b’+c)(a’+b+c)
Canonical presentation of logic functions
Conversion between truth tables and switching functions
Minterms and Maxterms: Summary

## Slide 57
Id a b f (a, b)
0 0 0 1
1 0 1 0
2 1 0 1
3 1 1 -
The input does not happen.
The input happens, but the output is ignored.
Examples:
Decimal number 0… 9 uses 4 bits. (1,1,1,1) does not happen.
Final carry out bit (output is ignored).
Don’t care set is important because it allows us to
minimize the function
Incompletely Specified Function

## Slide 58: Incompletely Specified Function
g1(a,b,c)=a’b’c+a’bc+ab’c’+abc
=m1+m3+m4+m7
=∑ m(1,3,4,7)
g2(a,b,c)=(a+b+c)(a’+b’+c)
=M0M6
=∏M(0,6)
id | a | b | c | g
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | -
3 | 0 | 1 | 1 | 1
4 | 1 | 0 | 0 | 1
5 | 1 | 0 | 1 | -
6 | 1 | 1 | 0 | 0
7 | 1 | 1 | 1 | 1

## Slide 59: Incompletely Specified Function
g1(a,b,c)=∑ m(1,3,4,7)
g2(a,b,c)=∏M(0,6)
iClicker: Does g1(a,b,c) = g2(a,b,c)?
A: Yes
B: No
id | a | b | c | g
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | -
3 | 0 | 1 | 1 | 1
4 | 1 | 0 | 0 | 1
5 | 1 | 0 | 1 | -
6 | 1 | 1 | 0 | 0
7 | 1 | 1 | 1 | 1