## Slide 1
CSE 140: Components and Design Techniques for Digital Systems
Lecture 6: Universal Gates
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Combinational Logic: Various Types of Gates
Universal Set of Gates
  Motivation
  Definition
  Examples
Other Types of Gates
  XOR
  NAND / NOR
  Block Diagram Transfers
Notes: Here we finish up our discussion on combination logic. We first will talk about complete set of gates, then move on to talk about other types of gates such as XOR gates and NAND / NOR gates. We will also talk about block diagram transfers, which is like converting a circuit into an equivalent circuit (i.e. it has the same exact function), but in the process changing and even reducing the number of gates.

## Slide 3: Universal Set of Gates: Motivation
AND, OR, NOT: Logic gates related to reasoning from Aristotle (384-322BCE).
NAND, NOR: Inverted AND, Inverted OR gates. For VLSI technologies, all gates are inverted (AND,OR operation with a bubble at output).
XOR: Exclusive OR gates. Parity check.
Multiplexer + input table: Table based logic for programmability. FPGA technology.
Neuron and Synapse: Neural network.
Reversible Gates: Quantum computing.
In the future, we may have new sets of gates due to new technologies.
Given a set of gates, can the gates in the set cover all possible switching functions?

## Slide 4: Universal Set
Universal set is a powerful concept to identify the coverage of a set of gates afforded by a given technology.
Criterion: If the set of gates can implement AND, OR, and NOT gates, the set is universal.

## Slide 5: Universal Set Definition
Universal Set: A set of gates such that every switching function can be implemented with the gates in this set.
Examples
{AND, OR, NOT}
{AND, NOT}
{OR, NOT}
Notes: A universal set simply means that some set of gates can implement any switching function. For example, {AND OR NOR} is a universal set because you can do any possible switching (0 or 1) function with it. {AND NOR} is also universal because you can implement OR with just AND, NOT. Since you can do that, you can implement any switching function.

## Slide 6: Universal Set: Examples
Universal Set: A set of gates such that every switching function can be implemented with the gates in this set.
Examples
{AND, OR, NOT}
{AND, NOT} OR can be implemented with AND & NOT gates:
{OR, NOT} AND can be implemented with OR & NOT gates:
{XOR} is not universal
{XOR, AND} is universal
Notes: A universal set simply means that some set of gates can implement any switching function. For example, {AND OR NOR} is a universal set because you can do any possible switching (0 or 1) function with it. {AND NOR} is also universal because you can implement OR with just AND, NOT. Since you can do that, you can implement any switching function.

## Slide 7: iClicker
Is the set {AND, OR} (but no NOT gate) universal?
Yes
No
Note that the set was used in a once popular design style as domino logic for high performance computing.

## Slide 8: iClicker
Is the set {} universal?
Yes
No

## Slide 9
{NAND, NOR}
{XOR}
{XOR, AND}
if constant “1” is available.
1
Universal Set: Examples
Notes: We see that a set consisting of just the NAND and NOR gates forms a universal set. We can implement a NOT gate by using a NAND gate and we can form an AND and OR gate by simply negating the NAND and NOR gates.

## Slide 10: Other Types of Gates: Properties and Usage
XOR
NAND, NOR
Block Diagram Transfers
Notes: A XOR gate is a gate that is 1 only when one and only one of the two inputs is also 1. If both are 0 or both are 1, then the XOR gate will output a 0 also.

## Slide 11: Other Types of Gates: XOR
It is a parity function (examples)
useful for testing because the flipping of a single input changes the output.
id | x | y | x ⊕ y
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | 0
 | x=0 | x=1
y=0 | 0 | 1
y=1 | 1 | 0
Notes: A XOR gate is a gate that is 1 only when one and only one of the two inputs is also 1. If both are 0 or both are 1, then the XOR gate will output a 0 also.

## Slide 12: Other Types of Gates: XOR
    Commutative
    Associative (
XOR
X
Y
XY’
X’Y
Notes: A XOR gate is a gate that is 1 only when one and only one of the two inputs is also 1. If both are 0 or both are 1, then the XOR gate will output a 0 also.

## Slide 13: Other Types of Gates: XOR
    Commutative
    Associative
XOR
X
Y
XY’
X’Y
Notes: A XOR gate is a gate that is 1 only when one and only one of the two inputs is also 1. If both are 0 or both are 1, then the XOR gate will output a 0 also.

## Slide 14
e) If ab = 0, then a ⊕ b = a + b
Proof: If ab = 0, then
a = a (b+b’) = ab+ab’ = ab’
b = b (a + a’) = ba + ba’ = a’b
Therefore, a+b = ab’ + a’b = a ⊕ b
Note that in full adder, we have
cout=ab+bc+ac=ab+c(a+b)
From property e), we can also write cout=ab+c(a ⊕ b)
Other Types of Gates: Properties and Usage

## Slide 15
f)
(Priority of operations: AND, ⊕, OR)
Hint: We apply Shannon’s Expansion.
Other Types of Gates: XOR

## Slide 16: Shannon’s Expansion (for switching functions)
Formula:
Proof by enumeration:
If
==
If
=
Notes: Shannon’s Expression is actually very useful equation. It simply says a function can be decomposed by restricting X. Thus we have two cases, one when X is 0 and one when X is 1.

## Slide 17: Other types of gates: XOR
Simplify the function (Priority of operations: AND, ⊕, OR)
f(X,Y) = X⊕XY’⊕X’Y⊕(X+Y)⊕X
Case X = 1: f (1, Y) = 1 ⊕ Y’⊕ 0 ⊕ 1 ⊕ 1 = Y
Case X = 0: f (0, Y) = 0 ⊕ 0 ⊕ Y ⊕ Y ⊕ 0 = 0
Thus, using Shannon’s expansion, we have
f (X, Y) = Xf(1,Y)+X’f(0,Y)= XY
Notes: Using Shannon’s Expression, we can easily solve for the answer to our problem. First we put parentheses around terms with higher precedence (like AND terms), and then from there we apply Shannon’s Expression to derive the two cares of when X is 1 and X is 0. Because we see that when X is 1, the function is Y, and when X is 0, the function is 0, we realize that the function is simply XY.

## Slide 18: XOR gates
iClicker: Is the equation
a+(b⊕c) = (a+b)⊕(a+c) true?
Yes
No

## Slide 19
2) NAND, NOR gates
NAND (NOR) gates are not associative
Let a | b = (ab)’
(a | b) | c ≠ a | (b | c)
Other Types of Gates: NAND, NOR

## Slide 20
3) Block Diagram Transformation
a) Reduce # of inputs.


Other Types of Gates: Block Diagram Transform

## Slide 21
b. DeMorgan’s Law

(a+b)’ = a’b’

(ab)’ = a’+b’
Other Types of Gates: Block Diagram Transform
Notes: DeMorgan’s Law implies that if you are given a NOR gate, you can convert that to an AND gate with two inverted inputs. Same with a NAND gate, you can replace a NAND gate with a OR gate with two inverted inputs.

## Slide 22
c. Sum of Products (Using only NAND gates)


Sum of Products (We create many bubbles with NOR gates)


Other Types of Gates: Block Diagram Transform
Notes: As we can see, there is a difference in how we transform our circuit. Comparing the two above, it is clear that using the NAND gates is much preferable to using the NOR gates as there are much less gates in the NAND version.

## Slide 23
d. Product of Sums (NOR gates only)


We will create many bubbles with NAND gates.
Other Types of Gates: Block Diagram Transform
Notes: Here we transform a product of sums circuit (two OR gates followed by an AND gate) into one with just NOR gates. We see that in this case, we don’t have a lot of gates like we did in the Sum of Products case.

## Slide 24: NAND, NOR gates
Remark:
Two level NAND gates: Sum of Products
Two level NOR gates: Product of Sums
Other Types of Gates: Block Diagram Transform

## Slide 25: Part II. Sequential Networks
Memory / Timesteps
Clock
Flip flops
Specification
Implementation
Notes: A combinational logic cannot have some sort of feedback loop where the output of a logic is also the input of it. A sequential network on the other hand can have this feature.