## Slide 1: CSE140 - Processors
Edited file from Bryan Chin
http://www.megaprocessor.com/
8-bit adder
Notes: 2800 chips, each made of 2 3-input NOR gates
16 bit computer – 15 bits + parity

## Slide 2: Navigation Check
Simple (RISC) Processor

## Slide 3: Simplified Digital Computer
Instruction Store
Memory
Execute
Register
File
Control
ALU
Multiply/Divide

## Slide 4: Simplified Digital Computer
Instruction Store
Memory
Execute
Register
File
Control
ALU
Add, logic, shift
Multiply/Divide
Instruction Types
Load
Store
Control Flow
Execute
PC

## Slide 5: SRAM (single port)
32 rows, 32 columns
Can read or write one row at a time (32 bits wide)
Decoder – takes in 5 bits, generates 1 of 32 (one-hot output)
Sense Amp
Write Driver
WL
B+
B-
Memory Cells
Memory Cells
Memory Cells
Memory Cells
32 columns
32 rows
Decoder
Addr[4:0]
WE*
Data[31:0]
Processor Register file
  MIPS I - 32 registers, 32 bits
  Need to read 2 operands and write 1
  3 ports
Notes: Draw example decoder structure – 5 input AND gate with inverters on some input bits

## Slide 6: Register File – smallish SRAM with more ports
Processor Register file
  MIPS I - 32 registers, 32 bits
  Need to read 2 operands and write 1
  3 ports
Modern processor register files may have lots of ports (e.g 14 R and 7 W)
Sense Amp
Write Driver
Make an array of these
WL
B+
B-
Memory Cells
Memory Cells
Memory Cells
Memory Cells
32 columns
32 rows
Decoder
WAddr[4:0]
WE*
writeData[31:0]
Sense Amp
rdA[31:0]
rdB[31:0]
Decoder
Decoder
AddrA[4]
AddrB[4]
Notes: Draw example decoder structure – 5 input AND gate with inverters on some input bits

## Slide 7: Row Decoder
5->32 decoder choses which row
One decoder per port
Addr[0]
Addr[1]
Addr[2]
Addr[3]
Addr[4]

## Slide 8: A register file is 128 bits wide and contains a total of 1 KB of storage. How many address bits will be required by the row decoder?
10 bits
9 bits
64 bits
6 bits
None of the above
* - B means byte, b means bit
Notes: (draw picture of box with 16 bytes on the bottom and 64 rows).
1KB / 16 = 64
Log(64) = 6

## Slide 9
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
MUX
0
1
ALU
ZERO
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
MUX
1
0
JUMP
<< 2
I[25-0]
JMP ADDRESS [25-0]
PC+4 [31-28]
JMP ADDRESS [31-0]
Src: TSR, Cummings, KFR

## Slide 10: Computer Program
MIPS (example RISC) architecture
Architecture
  Instruction Set
  Programming Resources (registers)
  View of memory (how to read and write it)
Label: addi r8, r8, -4
sw r0, 0(r8)
bne r3, r0, Label
00400000: 2108fffc ;
00400004: ac000000 ;
00400008: 1400fffd ;
Assembly
PC : Instruction

## Slide 11: Simple Single Cycle CPU
Assume each instruction executes in a single cycle
Instruction Format – MIPS RISC Instructions.
  Fixed instruction size (all instructions are 4 bytes (32 bits)).
  Load/Store, Compute and Control
R -Type |  |  |  |  | 
Opcode | Rs | Rt | Rd | Shift (shamt) | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
I-Type |  |  |  |  | 
Opcode | Rs | Rt | Immediate |  | 
6 bits | 5 bits | 5 bits | 12 bits |  | 
J Type |  |  |  |  | 
Opcode | Rs | Rt | Rd | Sa | Funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
e.g. add, sub, sll, …
add r6, r2, r3
e.g. ori, andi, bne, ld, st, …
ld r6, 0x100(r7)
bne r3, r0, target
e.g. jr, jalr
jr target

## Slide 12: CPU Components – Single Cycle Execution
  Assumptions:
  Every machine language instruction happens in 1 Clock Cycle
  MIPS architecture
    Microprocessor without interlocked pipeline stages
    reg-reg architecture: all operands must be in registers (total 32)
    3 Instruction Formats; each instruction 32 bits long
      R-type: all data in registers (most arithmetic and logical)
        e.g. add $s1, $s2, $s3
      2. I-type: branches, memory transfers, constants
      e.g. beq $s1, $s2, Label; lw $s1, 32($s2)
      3. J-type: jumps and calls
      e.g. j Label;
0
17
18
16
0
32
000000
10001
10010
10000
00000
100000
add $s0, $s1, $s2
Src: TSR, Cummings, KFR

## Slide 13: R-type Instruction: reg-reg ALU ops (e.g. add, and)
OPCODE
= 0
RT
RD
FUNCT
= 32 or 34
RS
R-type
Instruction
31-26
25-21
20-16
15-11
5-0
Source Register 1
(attached to “Read Register 1” input)
Source Register 2
(attached to “Read Register 2” input)
Destination Register
(attached to “Write Register” input)
Tells operation to be performed
Tells specific variant of operation (e.g. add/sub have same opcode)
Shift amount (for sll, srl etc.)
ADD r5, r7, r2
ADD RD, RS, RT
10-6
shamt
Src: TSR, Cummings, KFR
Notes: Write it on board!

## Slide 14
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
MUX
0
1
ALU
ZERO
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
Step 1 (R-type): Fetch instruction and advance PC
Notes: PC – program counter points to current instruction in memory.
Instruction is fetched form Instruction memory and sent to datapath for execution
At the same time, the adder at the top adds +4 to the PC to point to the next instruction – MIPS instructions are always 4 bytes.
Mux selects PC + 4 and its sent back to the PC to update it.
The PC+4 adder is a version of an incrementer. half adders may be used in most of it because only +4 is being added.
More specifically, the current value of the PC register is used to specify a location in the instruction memory, and the instruction stored at that location is read and passed on to other parts of the datapath.
Simultaneously, an adder adds 4 to the current value of the PC (since MIPS instructions are exactly 4 bytes long). Then, since the Branch control line is not set by default, the multiplexor will pass through the new value, old PC + 4, and this value will be stored into the PC register on the next clock edge.
Thus we have read the instruction at the current value of the PC and also updated the PC to refer to the next instruction.

## Slide 15
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
ALU
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
Step 2 (R-type): Read two registers and set control signals
ZERO
MUX
0
1

## Slide 16
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
MUX
0
1
ALU
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
Step 3 (R-type): Perform the ALU operation
ZERO

## Slide 17
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
MUX
0
1
ALU
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
Step 4 (R-type): Write result to register
ZERO

## Slide 18
OPCODE
= 35 or 43
RT
RS
Store Instruction
31-26
25-21
20-16
15-0
Base Address Register
(attached to “Read Register 1” input)
Source register whose value will be stored to memory
(attached to “Read Register 2” input)
Constant offset
(added to the base address in RS)
OFFSET
I-Type: Store Instruction
Tells operation to be performed
SW r0, 32(r5)
SW RT, #(RS)
Note: same as x86 MOV [ebx+32], eax

## Slide 19
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
MUX
0
1
ALU
ZERO
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
Step 1 (store): Fetch instruction and advance PC
MUX
0
1

## Slide 20
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
INSTRUCTION[15-0]
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
ALU
RESULT
ZERO
MUX
0
1
Step 2 (store): Read register values and set control signals
MUX
0
1
MUX
0
1

## Slide 21
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
INSTRUCTION[15-0]
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
ALU
RESULT
ZERO
MUX
0
1
Step 3 (store): Compute the address
MUX
0
1
MUX
0
1

## Slide 22
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
INSTRUCTION[15-0]
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
ALU
RESULT
ZERO
MUX
0
1
Step 4 (store): Write the value to memory
MUX
0
1
MUX
0
1

## Slide 23: I-Type: Conditional Branch
OPCODE
= 4 or 5
RT
RS
BEQ/BNE Instruction
31-26
25-21
20-16
15-0
Source Register 1
(attached to “Read Register 1” input)
Source register 2
(attached to “Read Register 2” input)
Word Offset, which we multiply by 4 (via <<2) to get Bit Offset, then add to PC+4 to get the address of the instruction to which we branch if RS == RT)
“PC-relative address”
BRANCH TARGET’S OFFSET
BEQ Source1, Source2, Offset
BEQ $r7, r20, 100
4 7 20 25

## Slide 24
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
MUX
0
1
ALU
ZERO
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
Step 1 (beq): Fetch instruction and advance PC
MUX
0
1

## Slide 25
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
INSTRUCTION[15-0]
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
ALU
RESULT
ZERO
MUX
0
1
Step 2 (beq): Read register values and set control signals
MUX
0
1
MUX
0
1

## Slide 26
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
INSTRUCTION[15-0]
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
ALU
RESULT
ZERO
MUX
0
1
Step 3 (beq): Compare registers, calculate branch target, and choose new PC
MUX
0
1
MUX
0
1

## Slide 27: J-Type: Unconditional Branch
OPCODE
= 2 or 3
JMP/JAL Instruction
31-26
25-0
Actual Address (in words) which we multiply by 4 (<<2) to get 28-Bit Address, then concatenate to upper 4 bits of PC+4 to get the 32-bit address of instruction to which we branch unconditionally
BRANCH TARGET ADDRESS
J Offset
J 10000
2 2500

## Slide 28
INSTRUCTION
MEMORY
READ
ADDRESS
INSTRUCTION
[31-0]
MUX
0
1
MUX
0
1
ALU
ZERO
RESULT
DATA
MEMORY
ADDRESS
WRITE
DATA
READ
DATA
MUX
0
1
ADDER
RESULT
ADDER
RESULT
PC
MUX
0
1
4
Sign
Extend
ALU
CONTROL
INSTRUCTION[15-0]
INSTRUCTION[5-0]
<< 2
CON TROL
INSTRUCTION[31-26]
INSTRUCTION[25-21]
INSTRUCTION[20-16]
INST[15-11]
BRANCH
REG_DST
REG_WRITE
ALU_SRC
ALU_OP
MEM_READ,MEM_WRITE
MEM_TO_REG
REGISTERS
READ REGISTER 1
READ REGISTER 2
WRITE REGISTER
WRITE DATA
READ DATA 1
READ DATA 2
MUX
1
0
JUMP
<< 2
I[25-0]
JMP ADDRESS [25-0]
PC+4 [31-28]
JMP ADDRESS [31-0]
Single-Cycle Datapath with Support for the Jump Instruction