## Slide 1
CSE 140: Components and Design Techniques for Digital Systems
Lecture 10:
Sequential Networks: Timing and Retiming
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Timing
Motivation
Gate Delay
Flip-Flop Timing Window
Two Timing Constraints: shortest and longest timing paths
Examples
Clock Skews and Retiming
Examples

## Slide 3: Timing: Motivation
Clock specifies a precise time for the next state
  In general, we allocate one clock period for signal propagation between registers. Goldilocks timing.
Too late: Fail to reach for the setup of the next state.
Too early: Race to disturb the holding of the next state.
Analysis: Verify the timing of the system.
Goal: A robust design.

## Slide 4: The Story of Goldilocks and the Three Bears
Once upon a time, there was a little girl named Goldilocks. She went for a walk in the forest. Pretty soon, she came upon a house. She knocked and, when no one answered, she walked right in. At the table in the kitchen, there were three bowls of porridge. Goldilocks was hungry. She tasted the porridge from the first bowl. "This porridge is too hot!" she exclaimed. So, she tasted the porridge from the second bowl.
"This porridge is too cold," she said. So, she tasted the last bowl of porridge. "Ahhh, this porridge is just right," she said happily and
she ate it all up. DLTK's Crafts for Kids

## Slide 5
Motivation: So far ….
Combinational
CLK
Logic-level analysis

## Slide 6
Motivation: This lecture …
When does our (seemingly logically correct) design go wrong?
How can we design a circuit that works under real constraints?
Popular interview question.
Combinational
CLK

## Slide 7
A typical sequential network has combinational circuit between registers (R1 to R2).
The registers are synchronized by clocks (CLK1 to CLK2).
Timing is set between clocks (CLK1 and CLK2).
The beauty of the synchronized design is that we need only to take care of the timing of the regions separated by the registers.
Motivation: Sequential Networks
Combinational
CLK1
CLK2
A
B
C
D
R1
R2

## Slide 8: Timing of the System
For a synchronized digital Moore machine, we need to take care of the timing of the following region(s).
Between every pair of registers.
Between i. input and register, and ii. register and output.
C1
C2
CLK
x(t)
y(t)
S(t)

## Slide 9: Gate Delay: Combinational Logic Timing
Min delay of a gate, also called Contamination delay: tcd
  Minimum time from when an input changes until the output starts to change
Max delay of a gate, also called Propagation delay: tpd
  Maximum time from when an input changes until the output is guaranteed to reach its final value (i.e., stop changing)
A
B
Y

## Slide 10: Gate Delay: Combinational Logic Timing
Different input transition causes different delay at output
00 | 11 | 1/0
01 | 11 | 1/0
10 | 11 | 1/0
11 | 11 | 1/1
00 | 11 | 1/0
01 | 11 | 1/0
10 | 11 | 1/0
11 | 11 | 1/1
A
B
Y

## Slide 11: Combinational Logic Delay
A
B
C
D
Y
  Different path causes different output transition delay.

## Slide 12: Interconnect Delay
Speed of light: C/ cm/s
For 1cm, it takes 0.7
for the light to reach from one end to the other end.
Chain of buffers: 5-40 times of speed of light.
For 5GHz, the clock period is .

## Slide 13: Combinational Logic: Output timing constraints
X1
X2
X4
Contamination delay (shortest): tcd
  Minimum time from when an input changes until any output starts to change
Propagation delay (longest): tpd
  Maximum time from when an input changes until the output or outputs of a combinational circuit are guaranteed to reach their final value (i.e., stop changing)
Combinational
circuit
X3
Y1
Y2
Y4
Y3

## Slide 14: Flip-Flop Timing Window
Timing: Setup Time and Hold Time Constraints
D
Q
Q’
Once a flip flop has been ‘built’ we are stuck with its timing characteristics:
tsetup, thold timing relation between D and CLK
tccq, tpcq timing relation between CLK and Q
No direct timing relation between input D and output Q

## Slide 15: FF Input Constraints: Set up and hold time
Setup time tsetup Time before the clock edge that data must be stable (i.e. not change)
Setup time violation This occurs if the input signal D does not settle (set up) to the stable value at least tsetup before the clock edge.
Hold time thold Time after the clock edge that data must be stable
Hold time violation This occurs if the input signal D does not remain unchanged (hold) for at least thold after the clock edge.
D
Q
Q’

## Slide 16: FF Output Timing Constraints
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)
D
Q
Q’

## Slide 17
Combinational
CLK1
CLK2
A
B
C
tcq + tcomb + tsetup ≤ T
thold < tcq + tcomb
Two Timing Constraints

## Slide 18
Combinational
CLK1
CLK2
A
B
C
Hold time constraint
thold < tcq + tcomb
Setup time constraint
tcq + tcomb + tsetup ≤ T
max(tcq + tcomb + tsetup )≤ T
thold < min(tcq + tcomb)
Longest delay from CLK1 to CLK2
Shortest delay from CLK1 to CLK2
Two Timing Constraints

## Slide 19
tcq + tcomb + tsetup ≤ T
thold < tcq + tcomb
Two Timing Constraints
CLK1
CLK2
Too long
Too short
Just right

## Slide 20: PIQ: The timing of which of the following signals can cause a setup-time violation?
Signal D arrives too early
Signal D arrives too late
Clock CLK arrives too late
Output Q(t) responds too early
None of the above
D
Q
Q’
D(t)
CLK
Q(t)

## Slide 21: PIQ: A hold time violation is likely to occur when
Signal D changes too early
Signal D changes too late
Clock CLK arrives too early
None of the above
D
Q
Q’
D(t)
CLK
Q(t)

## Slide 22: PIQ: A hold time violation is likely to occur when
Signal D changes too late
Clock CLK arrives too early
Clock CLK arrives too late
None of the above
D
Q
Q’
D(t)
CLK
Q(t)

## Slide 23
R1
Combinational
CLK
R2
CLK
D1
Q1
D2
An alternate view of the sequential circuit
Combinational
CLK

## Slide 24
What should happen within a clock cycle for correct functionality?
R1
Combinational
CLK
R2
CLK
D1
Q1
D2

## Slide 25
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements

## Slide 26
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements
2
3
3

## Slide 27
PI Q: Suppose CLK rises at t1, what is the maximum delay (from t1) after which D2 reaches a stable value?
Setup time of R1+ Propagation delay of CL + Propagation delay of R2
Hold time of R1+ Propagation delay of CL + setup time of R1
Propagation delay of R1+ Propagation delay of CL + Propagation delay of R2
Propagation delay of R1+ Propagation delay of CL
Propagation delay of CL + Propagation delay of R2

## Slide 28: Setup Time Constraint
The setup time constraint depends on the maximum delay from register R1 through the combinational logic.
The input to register R2 must be stable at least tsetup before the clock edge.
Maximum delay, tmax
=
Setup Time Constraint:

## Slide 29: Setup Time Constraint
Tc ≥ tpcq + tpd + tsetup
PI Q: As a designer, which of the following parameters would you modify to meet the set up time constraint?
The clock period, Tc
The prop. delay of R1, tpcq
The prop. delay of CL, tpd
The setup time of R2, tsetup
All of the above

## Slide 30: Setup Time Constraint
PI Q: As a designer, which of the following parameters would you modify to meet the set up time constraint?
The clock period, Tc
The prop. delay of R1, tpcq
The prop. delay of CL, tpd
The setup time of R2, tsetup
All of the above
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)

## Slide 31
PI Q: Suppose CLK rises at t1, what is the minimum delay (from t1) after which D2 starts to change?
Setup time of R1+ propagation delay of CL + propagation of R2
Hold time of R1+ propagation time of CL +setup time of R1
Hold time of R1+ Contamination delay of CL + Propagation time of R2
Contamination delay of R1+ Contamination delay of CL
Contamination delay of CL + Contamination delay of R2

## Slide 32: Hold Time Constraint
The hold time constraint depends on the minimum delay from register R1 through the combinational logic.
The input to register R2 must be stable for at least thold after the clock edge.
Minimum delay, tmin
=
Hold Time Constraint:

## Slide 33: Hold Time Constraint
thold < tccq + tcd
tcd > thold - tccq

## Slide 34: Timing Analysis: Example
Timing Characteristics
FFs tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
Gates tpd(g) = 35 ps
tcd(g)= 25 ps
tpd =
tcd =
Setup time constraint:
Tc ≥
fc = 1/Tc =
Hold time constraint:
tccq + tpd > thold ?

## Slide 35: Timing Analysis: Example
FFs tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
Gates tpd(g)= 35 ps
tcd(g)= 25 ps
tpd(com)= 3 x 35 ps = 105 ps
tcd(com)= 25 ps
Setup time constraint:
T ≥ tpcq + tpd(com)+ tsetup
=50 + 105 + 60 = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd(com)> thold ?
(30 + 25) ps > 70 ps ? No!

## Slide 36: Example: Fix Hold Time Violation
Timing Characteristics
FFs tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
Gates tpd(g)= 35 ps
tcd(g)= 25 ps
tpd(com)=
tcd(com)=
Setup time constraint:
T ≥
fc =
Hold time constraint:
tccq + tpd > thold ?
Add buffers to the short paths:

## Slide 37: Example: Fix Hold Time Violation
FFs tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
Gates tpd(g)= 35 ps
tcd(g)= 25 ps
tpd(com)= 3 x 35 = 105 ps
tcd(com)= 2 x 25 = 50 ps
Setup time constraint:
T ≥ 50 + 105 + 60 = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd(com)> thold ?
(30 + 50) ps > 70 ps ? Yes!
Add buffers to the short paths:

## Slide 38: Clock Skew
The clock doesn’t arrive at all registers at the same time. The difference between two clock edges is skew.
Skew as Noise: Caused by process variation, voltage fluctuation, crosstalks (PVC). Examine the worst case to guarantee that the timing is right.
Designated Skew: Make skew by design to improve the performance.

## Slide 39: Time Constraint with Clock Skew (Noise)
In the worst case, the CLK2 is:
Earlier than CLK1 for setup time
Later than CLK1 for hold time.
Tc ≥ tpcq + tpd(com)+ tsetup + tskew
tccq + tcd(com)> thold + tskew

## Slide 40: Timing Analysis with Clock Skew: Example
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tskew = 50 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ 265 ps
fc = 1/Tc =3.77 GHz
Without skew we got fc =4.65 GHz

## Slide 41: Time Constraint with Clock Skew: Example
In the worst case for setup time, CLK2 is later than CLK1
tccq + tcd(com)> thold + tskew

## Slide 42: Clock Skew: Example
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd(g)= 35 ps
tcd(g)= 25 ps
tskew = 50 ps
tpd(com)= 3 x 35 ps = 105 ps
tcd(com)= 2 x 25 ps = 50 ps
Hold time constraint:
tccq + tcd(com)> thold + tskew?
(30 + 50) > (70 +50) ps ?
Add buffers to the short paths:

## Slide 43: Retiming with Designated Skew
T ≥ tpcq + tpd(com)+ tsetup + tskew
tccq + tcd(com)> thold + tskew
Skew as noise (worst case)
Designated skew
T ≥ tpcq + tpd(com)+ tsetup - tskew
tccq + tcd(com)> thold + tskew

## Slide 44: Retiming: Example
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd(g)= 35 ps
tcd(g)= 25 ps
Tc ≥ tpcq + tpd(com)+ tsetup - tskew
tccq + tcd(com) ≥ thold + tskew
Tc ≥ 50 + 105 + 60 - tskew
30 + 50 ≥ 70+ tskew
iClicker: The minimum clock period T can be:
195
205
215
None of the above

## Slide 45: Timing and Retiming
Retiming: Adjust the clock skew so that the clock period can be reduced.
Add a few more examples on timing and retiming.

## Slide 46: Conclusion
Clock to Clock: Range of shortest and longest paths
Design revision and retiming to adjust the constraints
Research: Variation aware designs
Extra materials:
C. Leiserson and J. Saxe, "Retiming Synchronous Circuitry," Algorithmica, pp. 6:5-35, 1991.
L.T. Liu, M. Shih, N.C. Chou, C.K. Cheng, and W. Ku, "Performance-Driven Partitioning Using Retiming and Replication,“ IEEE Int. Conf. on Computer-Aided Design, pp. 296-299, Nov. 1993.