## Slide 1: CS 140 Lecture 15 Sequential Modules
Professor CK Cheng
CSE Dept.
UC San Diego

## Slide 2: Standard Sequential Modules
Serial Adders
Serial Multipliers
Register
Counter

## Slide 3: Motivation for Serial Adders and Multipliers
Tradeoff of silicon area and system performance
  Perform process in a series of time
Utilization of FPGA architecture
  Slice operation bitwise
Metrics of Cost, Speed, and Power
Ad: Cheaper hardware, Fit for FPGA architecture, Pipelining for excellent throughput
Dis: Longer latency

## Slide 4: Serial Adder: Perform serial bit-addition
a0 b0
a3 b3
cin
cout
s0
s3
Serial
Adder
a
b
sum
si
ai
bi
At time i, read ai and bi. Produce si and ci+1
Internal state stores ci. Carry bit c0 is set as cin

## Slide 5
Serial Adder using D F-F
D
Clk
si
ai
bi
C2
C1
D
Q
Q’
Feed ai and bi and generate si at time i.
Where is ci and ci+1?

## Slide 6: Serial Adder using a D Flip-Flop
id | ai | bi | ci | ci+1 | si
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
2 | 0 | 1 | 0 | 0 | 1
3 | 0 | 1 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0 | 1
5 | 1 | 0 | 1 | 1 | 0
6 | 1 | 1 | 0 | 1 | 0
7 | 1 | 1 | 1 | 1 | 1
D=ci+1
Q=ci

## Slide 7
D
Q
Q’
Clk
si
ai
bi
ci
Serial Adder using a D Flip-Flop
Logic Diagram

## Slide 8
Multiplication using Serial Addition
a2 a1 a0
b2 b1 b0
x
a2b0 a1b0 a0b0
a2b1 a1b1 a0b1
a2b2 a1b2 a0b2
+
m5 m4 m3 m2 m1 m0
0 1 1
1 0 1
x
0 1 1
+
0 0 0
0 1 1
0 1 1 1 1
3 X 5 = 15
For m=AxB, set m(0)=0
At time i, perform m(i+1)=m(i)+Abi2i

## Slide 9
Register
LD
D
Q
Q (t+1) = (0, 0, .. , 0) if CLR = 1
= D if LD = 1 and CLR = 0
= Q (t) if LD = 0 and CLR = 0
CLR
Clk

## Slide 10: Counter
Program Counter
Address Keeper: FIFO, LIFO
Clock Divider
Sequential Machine

## Slide 11: Counter
Modulo-n Counter
Modulo Counter (m<n)
Counter (a-to-b)
Counter of an Arbitrary Sequence
Cascade Counter

## Slide 12
Modulo-n Counter
LD
D
Q
TC
Q (t+1) = (0, 0, .. , 0) if CLR = 1
= D if LD = 1 and CLR = 0
= (Q(t)+1)mod n if LD = 0, CNT = 1 and CLR = 0
= Q (t) if LD = 0, CNT = 0 and CLR = 0
CNT
CLR
Clk
TC = 1 if Q (t) = n-1 and CNT = 1
= 0 otherwise

## Slide 13
Modulo-m Counter (m< n)
Given a mod 16 counter, construct
a mod-m counter (0 < m < 16) with AND, OR, NOT gates
m = 6
Q3 Q2 Q1 Q0
3 2 1 0
CLK
CLR
CNT
D3 D2 D1 D0
0 0 0 0
LD
Q2
Q0
X
Set LD = 1 when X = 1 and (Q3Q2Q1Q0) = (0101), ie m-1

## Slide 14
A 5-to-11 Counter
Q3 Q2 Q1 Q0
Clk
CLR
CNT
D3 D2 D1 D0
0 1 0 1 (a)
LD
Q3
Q0
X
Set LD = 1 when X = 1 and (Q3Q2Q1Q0) = b (in this case, 1011)
Counter (a-to-b)
Given a mod 16 counter, construct an a-to-b counter
(0 < a < b < 15)
Q1
(b)

## Slide 15
Given a mod 8 counter, construct
a counter with sequence 0 1 5 6 2 3 7
Q2 Q1 Q0
Clk
CLR
CNT
D2 D1 D0
LD
Q2’
Q0
X
Q2
Q0 Q1 Q0
Q0’
When Q = 1, load D = 5
When Q = 6, load D = 2
When Q = 3, load D = 7
Counter of an Arbitrary Sequence

## Slide 16
LD = Q2’ Q0 + Q2Q0’
D2 = Q0
D1 = Q1
D0 = Q0
K Mapping LD and D,
we get
Id | Q2Q1Q0 | LD | D2 | D1 | D0
0 | 000 | 0 | - | - | -
1 | 001 | 1 | 1 | 0 | 1
2 | 010 | 0 | - | - | -
3 | 011 | 1 | 1 | 1 | 1
4 | 100 | - | - | - | -
5 | 101 | 0 | - | - | -
6 | 110 | 1 | 0 | 1 | 0
7 | 111 | 0 | - | - | -
Given a mod 8 counter, construct
a counter with sequence 0 1 5 6 2 3 7
Counter of an Arbitrary Sequence

## Slide 17
D2 = Q0
D1 = Q1’ + Q0
D0 = Q1’Q0
LD = Q2’ Q1’ + Q2Q0 + Q2 Q1
Through K-map, we derive
Example: Count in sequence 0 2 3 4 5 7 6
LD = 1 D = 2 When Q(t) = 0
LD = 1 D = 7 When Q(t) = 5
LD = 1 D = 6 When Q(t) = 7
LD = 1 D = 0 When Q(t) = 6
Id | Q2Q1Q0 | LD | D2 | D1 | D0
0 | 000 | 1 | 0 | 1 | 0
1 | 001 | - | - | - | -
2 | 010 | 0 | - | - | -
3 | 011 | 0 | - | - | -
4 | 100 | 0 | - | - | -
5 | 101 | 1 | 1 | 1 | 1
6 | 110 | 1 | 0 | 0 | 0
7 | 111 | 1 | 1 | 1 | 0
Counter of an Arbitrary Sequence

## Slide 18
Cascade Counter
CNT
LD
TC
Clk
Q7,Q6,Q5,Q4
D7,D6,D5,D4
CNT
LD
TC
Clk
Q3,Q2,Q1,Q0
D3,D2,D1,D0
X
TC0
A Cascade Modulo 256 Counter
D3D2D1D0
D3D2D1D0
Q3Q2Q1Q0
Q3Q2Q1Q0

## Slide 19
TC = 1 when (Q3,Q2,Q1,Q0 )=(1,1,1,1) and X=1
(Q7 (t+1) Q6 (t+1) Q5 (t+1) Q4 (t+1) ) = (Q7 (t) Q6 (t) Q5 (t) Q4 (t) ) + 1 mod 16
when TC0 = 1
The circuit functions as a modulo 256 counter.
Cascade Counter
Time |  | 0 | 1 | 2 | 3 | … | 13 | 14 | 15 | 16 | 17 | 18 | 19
Q7-4 |  | 0 | 0 | 0 | 0 | … | 0 | 0 | 0 | 1 | 1 | 1 | 1
TC0 |  | 0 | 0 | 0 | 0 | … | 0 | 0 | 1 | 0 | 0 | 0 | 0
Q3-0 |  | 0 | 1 | 2 | 3 | … | 13 | 14 | 15 | 0 | 1 | 2 | 3