## Slide 1
Lecture 4: Four Input K-Maps
CSE 140: Components and Design Techniques for Digital Systems
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Outlines
Boolean Algebra vs. Karnaugh Maps
  Algebra: variables, product terms, minterms, consensus theorem
  Map: planes, rectangles, cells, adjacency
Definitions: implicants, prime implicants, essential prime implicants
Implementation Procedures

## Slide 3: 4-input K-map
An example
id | A | B | C | D | Y
0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 1
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 1
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0

## Slide 4: 4-input K-map
id | A | B | C | D | Y
0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
2 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1
4 | 0 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0 | 1
9 | 1 | 0 | 0 | 1 | 1
10 | 1 | 0 | 1 | 0 | 1
11 | 1 | 0 | 1 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0
14 | 1 | 1 | 1 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0

## Slide 5: 4-input K-map
Arrangement of variables
Adjacency and partition
0 | 4 | 12 | 8
1 | 5 | 13 | 9
3 | 7 | 15 | 11
2 | 6 | 14 | 10

## Slide 6
Boolean Expression | K-Map
Variable and complement | Half planes and
Product term | Rectangle
Each minterm | One element cell
Two adjacent minterms | Two neighboring cells
Each minterm has n adjacent minterms | Each cell has n neighbors
Boolean algebra | Two dimensional tool
? | Don’t Care set handling
Boolean Expression | K-Map
Each minterm | One element cell
Two adjacent minterms | Two neighboring cells
Each minterm has n adjacent minterms | Each cell has n neighbors
Boolean algebra | Two dimensional tool
? | 
K-Map vs. Boolean Expression

## Slide 7: Procedure for finding the minimal function via K-maps (layman terms)
Convert truth table to K-map
Group adjacent ones: In doing so include the largest number of adjacent ones (Prime Implicants)
Create new groups to cover all ones in the map: create a new group only to include at least one cell (of value 1 ) that is not covered by any other group (Essential Prime Impliants)
Select the groups that result in the minimal sum of products (we will formalize this because its not straightforward)

## Slide 8: Reading the reduced K-map
0 | 4 | 12 | 8
1 | 5 | 13 | 9
3 | 7 | 15 | 11
2 | 6 | 14 | 10
∑m(2,3,6,7)
∑m(5,7)
∑m(8,9)
∑m(0,2,8,10)

## Slide 9: Definitions: implicant, prime implicant, essential prime implicant
Implicant: A product term that has non-empty intersection with on-set F and does not intersect with off-set R .
Prime Implicant: An implicant that is not covered by any other implicant.
Essential Prime Implicant: A prime implicant that has an element in on-set F but this element is not covered by any other prime implicants.
Notes: Implicant, Prime, Essential (Check dictionary)

## Slide 10: Examples of Primes and Essential Primes

## Slide 11: Implicant, Prime, Essential Prime
0 | 4 | 12 | 8
1 | 5 | 13 | 9
3 | 7 | 15 | 11
2 | 6 | 14 | 10
Prime
∑m(2,3,6,7)
∑m(5,7)
∑m(8,9)
∑m(0,2,8,10)

## Slide 12: Definition: Prime Implicant
Yes
No
Q: How about this one? Is it a prime implicant?
Implicant: A product term that has non-empty intersection with on-set F and does not intersect with off-set R.
Prime Implicant: An implicant that is not covered by any other implicant.

## Slide 13: Definition: Essential Prime
Essential Prime Implicant: A prime implicant that has an element in on-set F but this element is not covered by any other prime implicants.
Yes
No
Q: Is the blue group an essential prime?

## Slide 14: Definition: Essential Prime
bc’d
d’b’
ac
ab
ad’
Q: Which of the following product term(s) is (are) not an essential prime for the given K-map ?
ab
cd
00
01
00
01
11
10
11
10
1
1
1
1
1
1
1
1
1
1
0 | 4 | 12 | 8
1 | 5 | 13 | 9
3 | 7 | 15 | 11
2 | 6 | 14 | 10
∑m(5,13)
∑m(0,2,8,10)
∑m(10,11,14,15)
∑m(12,13,14,15)
∑m(8,10,12,14)

## Slide 15: Procedure for finding the minimal function via K-maps (formal terms)
Convert truth table to K-map
Include all essential primes
Include non essential primes as needed to completely cover the onset (all cells of value one)

## Slide 16: K-maps with Don’t Cares

## Slide 17: K-maps with Don’t Cares

## Slide 18: K-maps with Don’t Cares

## Slide 19: Reducing Canonical expressions
Given F(a,b,c,d) = Σm (0, 1, 2, 8, 14)
D(a,b,c,d) = Σm (9, 10)
1. Draw K-map
ab
cd
00
01
00
01
11
10
11
10

## Slide 20: Reducing Canonical Expressions
Given F(a,b,c,d) = Σm (0, 1, 2, 8, 14)
D(a,b,c,d) = Σm (9, 10)
1. Draw K-map
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
ab
cd
00
01
00
01
11
10
11
10

## Slide 21: Reducing Canonical Expressions
Given F(a,b,c,d) = Σm (0, 1, 2, 8, 14)
D(a,b,c,d) = Σm (9, 10)
1. Draw K-map
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 0 0 1
1 0 0 X
0 0 0 0
1 0 1 X
ab
cd
00
01
00
01
11
10
11
10

## Slide 22: Reducing Canonical Expressions
Draw K-map
Identify Prime implicants
Identify Essential Primes
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 0 0 1
1 0 0 X
0 0 0 0
1 0 1 X
ab
cd
00
01
00
01
11
10
11
10
PI Q: How many primes (P) and essential primes (EP) are there?
Four (P) and three (EP)
Three (P) and two (EP)
Three (P) and three (EP)
Four (P) and Four (EP)

## Slide 23: Reducing Canonical Expressions
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 0 0 1
1 0 0 X
0 0 0 0
1 0 1 X
ab
cd
00
01
00
01
11
10
11
10
PI Q: Do the E-primes cover the entire on set?
Yes
No
Prime implicants: Σm (0, 1, 8, 9), Σm (0, 2, 8, 10), Σm (10, 14)
Essential Primes: Σm (0, 1, 8, 9), Σm (0, 2, 8, 10), Σm (10, 14)

## Slide 24: Reducing Canonical Expressions
Prime implicants: Σm (0, 1, 8, 9), Σm (0, 2, 8, 10), Σm (10, 14)
Essential Primes: Σm (0, 1, 8, 9), Σm (0, 2, 8, 10), Σm (10, 14)
Min exp: Σ (Essential Primes)=Σm (0, 1, 8, 9) + Σm (0, 2, 8, 10) + Σm (10, 14)
f(a,b,c,d) = ?
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 0 0 1
1 0 0 X
0 0 0 0
1 0 1 X
ab
cd
00
01
00
01
11
10
11
10
PI Q: Do the E-primes cover the entire on set?
Yes
No
Notes: f(a,b,c,d) = b’c’ + b’d’+ acd‘

## Slide 25: Reducing Canonical Expressions
Prime implicants: Σm (0, 1, 8, 9), Σm (0, 2, 8, 10), Σm (10, 14)
Essential Primes: Σm (0, 1, 8, 9), Σm (0, 2, 8, 10), Σm (10, 14)
Min exp: Σ (Essential Primes)=Σm (0, 1, 8, 9) + Σm (0, 2, 8, 10) + Σm (10, 14)
f(a,b,c,d) = b’c’ + b’d’+ acd‘
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 0 0 1
1 0 0 X
0 0 0 0
1 0 1 X
ab
cd
00
01
00
01
11
10
11
10
PI Q: Do the E-primes cover the entire on set?
Yes
No
Notes: f(a,b,c,d) = b’c’ + b’d’+ acd‘

## Slide 26: Another example
Given F(a,b,c,d) = Σm (0, 3, 4, 14, 15)
D(a,b,c,d) = Σm (1, 11, 13)
Draw the K-Map
ab
cd
00
01
00
01
11
10
11
10

## Slide 27: Another example
Given F(a,b,c,d) = Σm (0, 3, 4, 14, 15)
D(a,b,c,d) = Σm (1, 11, 13)
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 1 0 0
X 0 X 0
1 0 1 X
0 0 1 0
ab
cd
00
01
00
01
11
10
11
10

## Slide 28: Reducing Canonical Expressions
Prime implicants: Σm (0, 4), Σm (0, 1), Σm (1, 3), Σm (3, 11), Σm (14, 15), Σm (11, 15), Σm (13, 15)
Essential Primes: Σm (0, 4), Σm (14, 15)
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 1 0 0
X 0 X 0
1 0 1 X
0 0 1 0
ab
cd
00
01
00
01
11
10
11
10

## Slide 29: Reducing Canonical Expressions
Prime implicants: Σm (0, 4), Σm (0, 1), Σm (1, 3), Σm (3, 11), Σm (14, 15), Σm (11, 15), Σm (13, 15)
Essential Primes: Σm (0, 4), Σm (14, 15)
Min exp: Σm (0, 4), Σm (14, 15), (Σm (3, 11) or Σm (1,3) )
f(a,b,c,d) = a’c’d’+ abc+ b’cd (or a’b’d)
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
1 1 0 0
X 0 X 0
1 0 1 X
0 0 1 0
ab
cd
00
01
00
01
11
10
11
10