## Slide 1
Lecture 5: K-Map minimization in larger input dimensions and K-map minimization using max terms
CSE 140: Components and Design Techniques for Digital Systems
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Part I. Combinational Logic
Specification
Implementation
  K-map:
  Sum of products
  Product of sums

## Slide 3
Sum of Products Expression
Implicant: A product term that has non-empty intersection with on-setF and does not intersect with off-set R .
Prime Implicant: An implicant that is not a proper subset of any other implicant.
Essential Prime Implicant: A prime implicant that has an element in on-set F but this element is not covered by any other prime implicants.
Product of Sums Expression
Implicate: A sum term that has non-empty intersection with off-set R and does not intersect with on-set F.
Prime Implicate: An implicate that is not a proper subset of any other implicate.
Essential Prime Implicate: A prime implicate that has an element in off-set R but this element is not covered by any other prime implicates.
Definitions: Sum of Products and Product of Sums Expressions

## Slide 4: K-Map to Minimized Product of Sums
Sometimes it is easier to reduce the K-map by considering the offset
ab
cd
00
01
00
01
11
10
11
10
0 | 0 | 0 | 0
1 | 0 | 1 | 0
0 | 0 | 0 | 0
1 | 0 | 1 | 0
F1=a’b’c’d+abc’d+a’b’cd’+abcd’
F2=(a+b’)(a’+b)(c’+d’)(c+d)
iClicker:
Which function is simpler for a two level logic implementation?
F1
F2
Two are the same

## Slide 5: K-Map to Minimized Product of Sums
Sometimes it is easier to reduce the K-map by considering the offset
ab
cd
00
01
00
01
11
10
11
10
0 | 0 | 0 | 0
1 | 0 | 1 | 0
0 | 0 | 0 | 0
1 | 0 | 1 | 0
F1=a’b’c’d+abc’d+a’b’cd’+abcd’
F2=(a+b’)(a’+b)(c’+d’)(c+d)

## Slide 6: Another min product of sums example
Given R(a,b,c,d) = Σm (3, 11, 12, 13, 14)
D (a,b,c,d)= Σm (4, 8, 10)
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
ab
cd
00
01
11
10
00
01
11
10
K-map

## Slide 7: Another min product of sums example
a
d
1 X 0 X
1 1 0 1
0 1 1 0
1 1 0 X
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
ab
00
01
11
10
cd
00
01
11
10
Given R(a,b,c,d) = Σm (3, 11, 12, 13, 14)
D (a,b,c,d)= Σm (4, 8, 10)

## Slide 8
Prime Implicates:
ΠM(0,8), ΠM(11,15), ΠM(12,13,14,15), ΠM(6,14)
PI Q: Which of the following is a not an essential prime implicate?
ΠM(0,8)
ΠM(11,15)
ΠM(12,13,14,15)
ΠM(6,14)
a
d
0 1 0 X
1 1 0 1
1 1 0 0
1 X 0 1
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
ab
00
01
11
10
cd
00
01
11
10

## Slide 9: Five variable K-map
0 4 12 8
c
d
b
e
1 5 13 9
3 7 15 11
2 6 14 10
16 20 28 24
c
d
b
e
a
17 21 29 25
19 23 31 27
18 22 30 26
Neighbors of m5 are: minterms 1, 4, 7, 13, and 21
Neighbors of m10 are: minterms 2, 8, 11, 14, and 26
a=0
a=1
bc
de
00
01
11
10
00
01
11
10
00
01
11
10

## Slide 10: Reading a Five variable K-map: An example
0 4 12 8
c
d
b
e
1 5 13 9
3 7 15 11
2 6 14 10
16 20 28 24
c
d
b
e
a
17 21 29 25
19 23 31 27
18 22 30 26
a=0
a=1
bc
de
00
01
11
10
00
01
11
10
00
01
11
10
1 1
1 1
1 1
1 1 1
1
1
1 1 1
1 1 1
Notes: 5 EPIs

## Slide 11: Six variable K-map
d
e
c
f
d
e
c
d
e
c
f
48 52 60 56
d
e
c
b
49 53 61 57
51 55 63 59
50 54 62 58
a
32 36 44 40
33 37 45 41
35 39 47 43
34 38 46 42
f
f
0 4 12 8
1 5 13 9
3 7 15 11
2 6 14 10
16 20 28 24
17 21 29 25
19 23 31 27
18 22 30 26