## Slide 1: CSE 140 Lecture 12 Standard Combinational Modules
CK Cheng
CSE Dept.
UC San Diego

## Slide 2: Part III. Standard Modules
Interconnect Modules:
1. Decoder, 2. Encoder
3. Multiplexer, 4. Demultiplexer

## Slide 3: Multiplexer
Definition
Logic Diagram
Application

## Slide 4: Interconnect: Decoder, Encoder, Mux, DeMux
Processors
Decoder: Decode the address to assert the addressed device
Mux: Select the inputs according to the index addressed by the control signals
P1
Memory Bank
Mux
P2
Pk
Demux
Decoder
Mux
Data
Address
Address k
Address 2
Address 1
Data 1
Data k
Arbiter
n
n-m
m
2m

## Slide 5: Multiplexer Definition
A device that interleaves two or more activities
A communications device that combines several signals for transmission over a single medium
A logic circuit that sends one of several inputs out over a single output channel.
The circuit that uses a common communications channel for sending two or more messages or signals.
All of the above

## Slide 6: 3. Mux (Multiplexer) Definition: A digital module that selects one of data inputs according to the binary address of the selector.
Description
If E = 1
y = Di where i = (Sn-1, .. , S0)
Else
y = 0
E
y
D2n-1-D0
(Data input)
Sn-1,0
(Selector or Address)

## Slide 7: Multiplexer (Mux): Definition
Selects between one of N inputs to connect to the output.
log2N-bit select input – control input
E: Enable
y: Output
S: Selector or Address
D0
D1
0
1
Data input

## Slide 8: Multiplexer (Mux): Definition
Selects between one of N inputs to connect to the output.
log2N-bit select input – control input
Example: 2:1 Mux

## Slide 9
What is the output of the following MUX?
0
1
Can’t say
E =1
y
S=1
0
1
0
1

## Slide 10: Multiplexer Definition: 4-input mux
En
y
S1
S0
D0
D1
D2
D3
0
1
2
3
S1 | S0 | y

## Slide 11: Multiplexer: Logic Diagram
Logic gates
  Sum-of-products
Tristates
  For an N-input mux, use N tristates
  Turn on exactly one to select the appropriate input

## Slide 12: Multiplexer Application: universal set {Mux}
We use selector to decompose the function into smaller functions (less number of variables), which follows Shannon’s expansion.
We simplify the decomposed functions using K-map, which follows consensus theorem.

## Slide 13: Multiplexer Application
Mux for a Boolean function with truth table as input
Building blocks of FPGA (Field Programmable Gate Array).
For the logic diagram on left, output Y is
AB
(AB)’
A+B
(A+B)’
None of the above

## Slide 14: Multiplexer Application: universal set {Mux}
Example 1: Given f (a,b,c) = Σm (0,1,7) + Σd(2), implement with an 8-input Mux.
En
y
a
b
c
S2
S1
S0
0
1
2
3
4
5
6
7
id | abc | f
0 | 000 | 1
1 | 001 | 1
2 | 010 | -
3 | 011 | 0
4 | 100 | 0
5 | 101 | 0
6 | 110 | 0
7 | 111 | 1

## Slide 15
E
y
a
b
S1
S0
0
1
2
3
Example 2: Given f (a,b,c) = Σm (0,1,7) + Σd(2), implement with 4-input Muxes.
ab | c=0 | c=1 | D
00 |  |  | D0
01 |  |  | D1
10 |  |  | D2
11 |  |  | D3

## Slide 16
E
0
1
a
y
Example 3: Given f (a,b,c) = Σm (0,1,7) + Σd(2), implement with 2-input Muxes.
a\bc | 00 | 01 | 10 | 11 | D(b,c)
0 | 1 | 1 | - | 0 | D0
1 | 0 | 0 | 0 | 1 | D1

## Slide 17
E
b’
0
1
a
y
D0 (b,c) = b’
D1 (b,c) = bc
Example 3: Given f (a,b,c) = Σm (0,1,7) + Σd(2), implement with 2-input Muxes.
D1 (b,c)
a\bc | 00 | 01 | 10 | 11 | D(b,c)
0 | 1 | 1 | - | 0 | D0
1 | 0 | 0 | 0 | 1 | D1
c=0 | 1 | -
c=1 | 1 | 0
 | b=0 | b=1
c=0 | 0 | 0
c=1 | 0 | 1
 | b=0 | b=1

## Slide 18
D1 (b,c)
E
b’
0
1
a
y
Example 3: Given f (a,b,c) = Σm (0,1,7) + Σd(2), implement with 2-input Muxes.
b\c | 0 | 1 | D
0 | 0 | 0 | D0=
1 | 0 | 1 | D1=

## Slide 19
D1 (b,c)
E
E
b’
0
1
a
b
y
0
1
0
c
Example 3: Given f (a,b,c) = Σm (0,1,7) + Σd(2), implement with 2-input Muxes.
b\c | 0 | 1 | D
0 | 0 | 0 | D0=0
1 | 0 | 1 | D1=c

## Slide 20
Example 4: Given f (a,b,c) = Σm (0,2,4,7) + Σd(3,5), implement with 2-input Muxes.
E
0
1
a
y
D0(b,c)
D1(b,c)
a\bc | 00 | 01 | 10 | 11 | D
0 | 1 | 0 | 1 | - | D0
1 | 1 | - | 0 | 1 | D1

## Slide 21: 4. Demultiplexers
E
x
y2n-1 -y0
S(n-1,0)
Control Input
yi = x if i = (Sn-1, .. , S0) & E=1
yi = 0 otherwise

## Slide 22: Shifters
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb).
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111

## Slide 23: Shifter
Can be implemented with a mux
s
d
yi
E
1
0
3 2 1 0
xi+1
xi-1
xi
s
d
xn
x0
x-1
xn-1
yn-1
y0
E
s / n
l / r
yi = xi-1 if E = 1, s = 1, and d = L
= xi+1 if E = 1, s = 1, and d = R
= xi if E = 1, s = 0
= 0 if E = 0

## Slide 24: Shifter Design

## Slide 25: Barrel Shifter
O or 1 shift
O or 2 shift
O or 4 shift
x
s0
s1
s2
y
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
shift

## Slide 26: Shifters as Multipliers and Dividers
A left shift by N bits multiplies a number by 2N
  Ex: 00001 << 2 = 00100 (1 × 22 = 4)
  Ex: 11101 << 2 = 10100 (-3 × 22 = -12)
The arithmetic right shift by N divides a number by 2N
  Ex: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Ex: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)