## Slide 1: Lecture 1: Introduction to Digital Logic Design
CSE 140: Components and Design Techniques for Digital Systems
Spring 2021
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego
Notes: Digital: 0, 1 or False, True or GND, Vdd
Logic: Reasoning
Design: Theory + Implementation

## Slide 2: Outlines
Staff
  Instructor, TAs, Tutors
Logistics
  Websites, Textbooks, Grading Policy
Motivation
  Moore’s Law, Deep Learning, Quantum Computing
Scope
  Position among CSE courses
  Coverage

## Slide 3: Staff: the Instructor
Instructor: CK Cheng
Education: Ph.D. in EECS UC Berkeley
Industrial Experiences: Engineer of AMD, Mentor Graphics, Bellcore; Consultant for technology companies
Email: ckcheng+140@ucsd.edu
Office: Room 2130 CSE Building
Office hours
  3:00-4:00PM Monday; 2:00-3:00PM Wednesday
Websites
  http://cseweb.ucsd.edu/~kuan
  http://cseweb.ucsd.edu/classes/sp21/cse140-a

## Slide 4: Staff: TAs and Tutors
TAs
Abraham, Elizabeth, email:eabraham@ucsd.edu
Holtz, Chester, email:chholtz@ucsd.edu
Hsu, Po-Ya, email:p8hsu@ucsd.edu
Ravindrakumar, Vaishakh, email:varavind@ucsd.edu
Wu, (Connie) Yen-Yi, email:yew001@ucsd.edu
Tutor(s)
Jang, (Tim) Wonsuk, email:w1jang@ucsd.edu
Serrano, Evan, email:e1serran@ucsd.edu
Office hours will be posted on the course website (piazza)
Notes: Office hours and paper correction

## Slide 5: Logistics: Class Schedule
Lecture: TR 12:30-1:50PM
Discussion: F 3-350PM
5-6 Homework Assignments, 3 Exams
The Third Exam: Due time M 230PM, 6/7/2021

## Slide 6: Logistics: Textbooks
Reserved at library
Digital Design and Computer Architecture by David Money Harris and Sarah L. Harris, Morgan Kaufmann (Reading Activities)
Digital Systems and Hardware/Firmware Algorithms, Milos D. Ercegovac and Tomas Lang (System Designs, pdf file will be released)

## Slide 7: Logistics: Sites for the Class
Class website
  http://cseweb.ucsd.edu/classes/sp21/cse140-a/index.html
  Index: Staff Contacts and Office Hrs
  Syllabus
    Grading policy
    Class notes
    Assignment: Homework and Reading Activities
    Exercises: Solutions and Rubrics
Forum (Piazza): Online Discussion *make sure you have access
Score keepers: Gradescope, Canvas
Notes: Joint website

## Slide 8: Logistic: Class Expectation
Level 1: Concepts and Methods (Lecture and slides)
  Class attendance of video record
Level 2: Hands on Practices (Exercises)
  Homework
Level 3: Command of Materials (Samples of exams)
  Exams: Type 1
Level 4: Extension and Exploration (Content beyond the textbook)
  Exams: Type 2

## Slide 9: Logistics: Grading
Total pts distribution:
Homework: 35pts (grade based on a subset of problems)
Exams: 32.5pts for the each of the best two out of 3 exams
  Exam 1: Week 4
  Exam 2: Week 7
  Exam 3: (due 230PM, Monday 6/7/2021)
Grading: The better choice of the following two categories
  Exact score (100pts)
    A>93, A- >90, B+>87, B>83, B->80, C+>77, C>73
    C- >50.
  The curve (100% of class)
    A+ top x% (< 5)
    (A,A-) top 33±ε%; (B+,B,B-) top 66±2ε%

## Slide 10: Logistic: grading components
  Homework:
    Due Monday night on gradescope
    Group discussion is encouraged. However, we are required to write individually
  Discount 10% loss of credit for each day after the deadline but no credit after the solution is posted.
  Some parts will be graded by completion only
  Standard: Posted solutions and rubrics

## Slide 11: Logistic: 3 Exams
Exams: Asynchronous exam taken within 48 hours
  Open book, notes, free to check websites
  Solution and grading policy will be posted after the exam.
  Exams are not cumulative but requires a good command of the previous exam content
  Two timeframe options for the class to decide
    80 minutes time frame: Finish the exam in 80 minutes after you start the exam.
    48 hours time frame: Deliver the result in 48 hours after the exam is posted.
  Exam schedule
    Weekends
    Weekdays

## Slide 12: Course Problems…Cheating
What is cheating?
  Studying together in groups is not cheating but encouraged
  Turned-in work must be completely your own.
  Copying someone else’s solution on a HW or Exam is cheating
  Both “giver” and “receiver” are equally culpable
We will be better off to work on the problem alone during the exam.
We have to address the issue once the cheating is reported by someone (e.g. TA, Tutor, Student, etc.).

## Slide 13: Motivation
Microelectronic technologies have revolutionized our world: cell phones, internet, rapid advances in medicine, etc.
The semiconductor industry has grown from $21 billions in 1985, $335 billions in 2015, to $478 billions in 2018.

## Slide 14: The Digital Revolution
WWII
Integrated Circuit: Many digital operations on the same material
ENIAC
Moore’s Law
1965
1949
Integrated Circuit
Exponential Growth of Computation
Vacuum tubes
(1.6 x 11.1 mm)
Stored Program
Model
Notes: The stored program model computers and the invention of the transistor and the integrated circuit generated an exponential growth in computing devices and computers – why?
Von neumann architecture – put both data and instructions on the same electronic medium – memory. The whole machine could be constructed from digital logic/circuits.
Digital logic was in turn constructed using electronic circuits – different discrete components vacuum tubes (switches), capacitors, resistors.
But the way digital circuits were constructed underwent a revolution once the transistor came along. The transistor replaced the vacuum tube (both are switches) – given a control signal they either let current pass through them (logic 1) or stop current (logic 0). Discrete circuits were replaced by integrated circuits (everything made from the same silicon material).
The whole computer shrank.

## Slide 15: Building complex circuits
Transistor

## Slide 16: Robert Noyce, 1927 - 1990
Nicknamed “Mayor of Silicon Valley”
Cofounded Fairchild Semiconductor in 1957
Cofounded Intel in 1968
Co-invented the integrated circuit

## Slide 17: Gordon Moore
Cofounded Intel in 1968 with Robert Noyce.
Moore’s Law: the number of transistors on a computer chip doubles every 1.5 years (observed in 1965)

## Slide 18: Technology Trends: Moore’s Law
Since 1975, transistor counts have doubled every two years.
Moore’s law: wider applications: larger market: higher revenue: more R&D

## Slide 19: Introduction: Moore in1965 The complexity for minimum component costs has increased at a rate of roughly a factor of two/yr.
Cheng’s talk: http://cseweb.ucsd.edu/~kuan/talk20/KTC2020_CK_201014.pdf
Notes: Most of you have heard of Moore’s Law. As Gordon Moore proposed it over 50 years ago, it is a law of Value and Cost SCALING. Scaling means cost reduction – again, so that what was impossible before, now becomes possible.
In the industry, we focus on PPAC scaling: power, performance, area, cost. A new technology should be superior in all four of these dimensions.
And Moore’s Law is also about TIME: It means that the semiconductor world advances at roughly One Percent every Week. One week is One percent.

## Slide 20: New Technologies
New materials and fabrication for devices
  Low power devices
  Three dimensional integrated circuits
  Graphene
New architecture
  Machine learning, deep learning
Quantum computing
Understand the principles to explore the future

## Slide 21: Artificial Intelligence
Logic and Reasoning
Boolean Satisfiability (SAT)
  Product of sum clauses
  Diagnosis
States and Sequences
  Sequential Machines
  Reachability
  Controllability
One example of the applications and opportunities

## Slide 22: Scope
The purpose of this course is that we:
Learn the principles of digital design
Learn to systematically debug increasingly complex designs
Design and build digital systems
Learn what’s under the hood of an electronic component
Prepare for the future technology revolution

## Slide 23: Position among CSE Courses
Big idea: Coordination of many levels of abstraction
CSE 140
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
Transistors
Memory
Architecture
Software
Assembler
Dan Garcia
CSE 120
CSE 141
CSE 131
Algos: CSE 100, 101

## Slide 24: Principle of Abstraction
Abstraction: Hiding details when they are not important
CSE 30
CSE 141
CSE 140

## Slide 25: Combinational Logic vs Sequential Network
fi(x,s)
x1
.
.
.
xn
Combinational logic:
yi = fi(x1,..,xn)
CLK
Sequential Networks
1. Memory
2. Time Steps (Clock)
yit = fi (x1t,…,xnt, s1t, …,smt)
sit+1 = gi(x1t,…,xnt, s1t,…,smt)
fi(x)
x1
.
.
.
xn
fi(x)
fi(x)
x1
.
.
.
xn
fi(x)
si

## Slide 26: Scope: Overall Picture of CS140
Sequential machine
Conditions
Control
Mux
Memory File
ALU
Memory Register
Conditions
Input
Pointer
CLK: Synchronizing Clock
Data Path Subsystem
Select
Control Subsystem
BSV: Design specification and modular design methodology

## Slide 27: Scope
Subjects | Building Blocks | Theory
Combinational Logic | AND, OR, NOT, XOR | Boolean Algebra
Sequential Network | AND, OR, NOT, FF | Finite State Machine
Standard Modules | Operators, Interconnects, Memory | Arithmetics, Universal Logic
System Design | Data Paths, Control Paths | Methodologies
Notes: Coverage of Midterm 1, Midterm 2, and Final

## Slide 28: Combinational Logic Basics

## Slide 29: What is a combinational circuit?
No memory
Realizes one or more functions
Inputs and outputs can only have two discrete values
  Physical domain (usually, voltages) (Ground 0V, Vdd 1V)
  Mathematical domain : Boolean variables (True, False)
Differentiate between different representations:
  physical circuit
  schematic diagram
  mathematical expressions

## Slide 30: Binary Digital Logic
Simplest representation is “1” and “0” (base-2).
Choose a physical quantity to represent “1” and “0”
  Usually voltage, but not always (e.g. current, resistance, magnetic polarization, quantum spin, …)
Use a transistor to make the switch (operating as a digital instead of analog device)
  Two states – on / off
  Signals can be high voltage (“1”) or low voltage (“0”)

## Slide 31: Basic CMOS
Complementary Metal Oxide Semiconductor
Invented in the 1960’s, but took over in the 80’s
“on” means low resistance, ”off” means high resistance
Logic “1” and Logic “0” values are arbitrary
  e.g. logic “1” == 1.0 V, logic “0” == 0.0 V
NMOS
PMOS
”on” when gate is high
”on” when gate is low
https://en.wikipedia.org/wiki/CMOS#/media/File:Cmos_impurity_profile.PNG
d
d
s
s
g
g
Planar technology
FINFET technology
By Irene Ringworm, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3833512

## Slide 32: Transistors as Switches

## Slide 33: Transistors as Switches

## Slide 34: The most basic CMOS gate - inverter
When “inp” is “1”, then the nmos is on and the pmos is off – output will be ?
When “inp” is “0”, then the nmos is off and the pmos is on – output will be ?
inp
out
Schematic
in | out
0 | 1
1 | 0
Truth Table
inp
out
Equation
out = in’
out =in

## Slide 35: Basic Gates – (N)AND gate
AND Y = A & B Y = AB
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
NAND Y = (A & B)’ Y = (AB)’
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Y
What kind of gate is this?
AND
NAND
Inverter
None of the above

## Slide 36: Basic Gates – (N)OR gate
OR Y = A + B Y = A | B
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
NOR Y = (A + B)’ Y = (A | B)’
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A
B
Y
Bubble means Invert
NOR is universal gate
A
B
Y

## Slide 37: Boolean Algebra
A branch of algebra in which the values of the variables belong to a set B (e.g. {0, 1}), has two operations {+, .} that satisfy the following four sets of laws.
Associative laws: (a+b)+c= a+(b+c), (a·b)·c =a·(b·c)
Commutative laws: a+b=b+a, a·b=b·a
Distributive laws: a+(b·c)=(a+b)·(a+c),
a·(b+c)=a·b+a·c
Identity laws: a+0=a, a·1=a
Complement laws: a+a’=1, a·a’=0
(x’: the complement element of x)

## Slide 38: Duality
Swap (+, and complement all 0’s and 1’s
If we can prove a statement using laws of Boolean algebra true, then the duality of the statement is also true.
Associative | (a b) c = a (b c) | (a b)c = a(bc)
Commutative | ab = ba | a+b = b+a
Distributive* | a(b+c) = ab + ac | a+(bc)=(a+b)(a+c)
Identity | a1 = a | a+0 = a
Compliment | aa’ = 0 | a + a’ = 1
Associative |  | 
Commutative |  | a+b = b+a
Distributive* |  | 
Identity |  | a+0 = a
Compliment |  | a + a’ = 1
Laws and their duals

## Slide 39: Representations of combinational circuits: The Schematic
A
B
Y
What is the simplest combinational circuit that you know?

## Slide 40: Representations of combinational circuits Truth Table: Enumeration of all combinations
A
B
Y=AB
Example: AND
id | A | B | Y
0 | 0 | 0 | 0
1 | 0 | 1 | 0
2 | 1 | 0 | 0
3 | 1 | 1 | 1

## Slide 41: Boolean Algebra
Similar to regular algebra but defined on sets with only three basic ‘logic’ operations:
  Intersection: AND (2-input); Operator: ∙ ,&
  Union: OR (2-input); Operator: + ,|
  Complement: NOT ( 1-input); Operator: ‘ ,!
“&, |, !” Symbols in BSV

## Slide 42: Some Def’s
Complement : variable with a “BAR” over it or ‘ after it
  A’
Literal : variable or its complement
Implicant: product of literals
  ABC
Implicate: sum of literals
  (A+B+C)
Minterm, maxterm (implicant or implicate that includes all the inputs)
  f(A,B,C,D): ABCD, (A+B+C+D)

## Slide 43: Boolean algebra and switching functions
Two-input AND ( ∙ )
A B Y
0 0 0
0 1 0
1 0 0
1 1 1
AND
A B Y
0 0 0
0 1 1
1 0 1
1 1 1
OR
A Y
0 1
1 0
NOT
For an AND gate,
0 at input blocks the other inputs and dominates the output
1 at input passes signal A
For an OR gate,
1 at input blocks the other inputs and dominates the output
0 at input passes signal A
A
1
1
A
0
A
A
1
A
A
0
0
Two-input OR (+ )
One-input NOT (Complement, ’ )

## Slide 44: Boolean Algebra
For two Boolean variables X and Y with X=1, Y=0, what is function f(X,Y)=X+Y?
f(X,Y)=0
f(X,Y)=1
f(X,Y)=2

## Slide 45: Boolean Algebra
iClicker Q: For two Boolean variables X and Y with X=1, Y=0, what is function f(X,Y)=X+X+Y?
f(X,Y)=0
f(X,Y)=1
f(X,Y)=2

## Slide 46: Boolean Algebra
For two Boolean variables X and Y with X=1, Y=0, what is function f(X,Y)=X+XY?
f(X,Y)=0
f(X,Y)=1
f(X,Y)=2

## Slide 47: Boolean Algebra
For two Boolean variables X and Y with X=1, Y=0, what is function f(X,Y)=(X+Y)Y?
f(X,Y)=0
f(X,Y)=1
f(X,Y)=2

## Slide 48: So, what is the point of representing gates as symbols and Boolean expressions?
ab + cd
a
b
c
d
e
cd
ab
y=e (ab+cd)
Logic circuit vs. Boolean Algebra Expression
Simplify the Boolean expression: Reduce the complexity of the circuit
Given the Boolean expression, we can draw the circuit it represents by cascading gates (and vice versa)

## Slide 49: Switching Expression and Logic Diagrams
Switching Expression –
  Equations - # literals, # variables, # operators
    Literal is a variable or its complement (e.g. a, a’)
    Variables (e.g. x)
    Operator (e.g. +, ·)
  Schematic / Logic Diagram - # of gates, # nets (wires), # of pins
    Gate (and, or, etc) – can be more than 2 inputs (e.g. 3 input AND gate)
    Net – wire that connects gates
    Pin - input or output of a gate.

## Slide 50
Associativity Laws
(A+B) + C = A + (B+C)
(AB)C = A(BC)
C
A
B
A
B
C
C
A
B
A
B
C
Laws and Logic Diagrams
Notes: Logic is the same, but timing may be different.
Which one would be choose of (AB)C or A(BC) if A arrives later than B and C signals.

## Slide 51
Distributive Laws
A ∙(B+C) = A ∙ B + A ∙ C
A+B ∙ C = (A+B) ∙(A+C)
A
B
C
A
C
A
B
A
B
C
A
C
A
B
Laws and Logic Diagrams
Notes: Draw / Count
# literals, # operators
# pins.
Show #pins = # literals + #gates * 2– 1.
Each literal has 1 pin, each gate has 1 pin – out connected to 1 pin in (except for primary output) so times 2 pins.
Except output which has only one pin.

## Slide 52: Switching Expression and Logic
Schematic Diagram:
5 primary inputs
1 primary output
4 components (gates)
9 signal nets
12 pins
a·b + c·d
a
b
c
d
e
c·d
a·b
y=e·(a·b+c·d)
Boolean Algebra:
5 variables
1 expression
4 operators
5 literals

## Slide 53: Switching Expression and Logic
Schematic Diagram:
6 primary inputs
1 primary output
4 gates (3 ANDs, 1 OR)
10 signal nets
11 pins
Nets are wires, Gates ->transistors
a·b + b’·c
a
b
b’
c
d’
b’·c
a·b
y= d’ ·e ·(a·b+b’·c)
Switching Expression:
5 variables
1 expression
4 operators (3 ANDs, 1 OR)
6 literals
Cost: #gates, #nets, #pins
e
Notes: Show how to count # nets
Show eq for pins
# of literals + 2*# of gates -1 (each gate has an output + one input except for output gate)

## Slide 54: Example: f(a, b, c) = ab + a’c + a’b’
# variables | 
# literals | 
# gates | 
Notes: Draw circuit.
Count # literals = 6
Count # variables = 3
Count # gates = 4 gates
Count # pins = 13 pins
Count # nets = 10
Count # operators (gates) = 4

## Slide 55: Which statement is not true in general?
Schematic Diagram:
5 primary inputs
4 components (gates)
9 signal nets
12 pins
a·b + c·d
a
b
c
d
e
c·d
a·b
y=e·(a·b+c·d)
Boolean Algebra: y=e·(a·b+c·d)
5 literals
4 operators
#primary inputs = # literals
#gates = # operators
#nets = #variables + # operators
#pins = # literals + 2 * #operators -1
All of them
Based on CK Cheng – CSE140 Spr18
Notes: # nets = # variables + # operators - for example, replace e with d’ - reduced # of variables, but # of nets is the same.
# nets = # literals + # operators
Discuss D and why it is true :
Every gate has an output which goes to an input (2 pins) except the last gate
All primary inputs (literals) to to a pin.

## Slide 56: Logic Diagram/Schematics
https://commons.wikimedia.org/wiki/File:74181aluschematic.png
Logic circuit vs. Boolean Algebra Expression
Simplify the Boolean expression: Reduce the complexity of the circuit

## Slide 57: Next class
Designing Combinational circuits