## Slide 1
CSE 140: Components and Design Techniques for Digital Systems
Lecture 8:
Sequential Networks and Finite State Machines
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: 3. Implementation
Specification:
  Finite State Machine:
    Behavior, State Diagram, State Table
    Register Transfer Level Description
Design Flow
Excitation Table
Mealy and Moore Machines
Examples

## Slide 3: Specification
Combinational Logic
  Truth Table
  Boolean Expression
  Logic Diagram (No feedback loops)
Sequential Networks: Finite State Machines
  State Diagram, State Assignment, State Table
  Excitation Table and Characteristic Expression
  Register-Transfer Level Description
  Logic Diagram (FFs and feedback loops)

## Slide 4: Finite State Machine: Overview using An example
Not all sequences are created equal: A coin has two faces. A toss of the coin lands either Head or Tail with equal probability. A series of tossing creates a sequence. Given two patterns, say HHH and HTT, the pattern appears first wins.
H
H
H
H
T
H
The two patterns have an equal chance to win
HHH wins more times
HTT wins more times
None of the above

## Slide 5: Finite State Machine: Not all Sequences are created equal
State Diagram of HHH
Different diagrams yield different expectations
H
S
H
H
T/0
T/0
H/1
H/0
H/0
T/0
H
S
T
T
H/0
T/0
H/0
T/1
T/0
H/0
State Diagram of HTT

## Slide 6
Combinational
CLK
CLK
A
B
C
D
Specification: Register-Transfer Level Description
VHDL
Verilog
BVS
S(t)
X
Y
CLK
RTL: Register-Transfer Level Description
Conceptually, we can align all registers into one single column

## Slide 7: Design Flow
Input Output Relation
State Diagram (Transition of states)
State Assignment (Map states into binary code)
  Binary code, Gray encoding, One hot encoding, Coding optimization
State Table (Truth table of states)
Excitation Table (Truth table of FF inputs)
  K Map, Minimal Expression
  Logic Diagram
Verification: Simulation

## Slide 8: Design Flow: Examples
Example 1: a counter from description, state diagram, state table, netlist, to I/O behavior.
Example 2: a pattern recognizer from state diagram to netlist to demonstrate the difference of two machines.

## Slide 9: Example: A Counter
Free running 2 bit Counter
Symbol/ Circuit
Behavior over time
time
CLK
Q0
Q1

## Slide 10: Counter: Input-output relation ⇒ State diagram
2 bit Counter
Symbol/ Circuit
Diagram that depicts behavior over time

## Slide 11: Counter: State diagram ⇒ State assignment
S0
S1
S2
S3
State Diagram
State Table: Binary
Q1(t) | Q0(t) | Q1(t+1) | Q0(t+1)
Current state | Next State
S0 | S1
S1 | S2
S2 | S3
S3 | S0
State | Q1 | Q0
S0 | 0 | 0
S1 | 0 | 1
S2 | 1 | 0
S3 | 1 | 1
State Assignment
State Table: Symbol

## Slide 12: Counter: State assignment ⇒ Excitation table
S0
S1
S2
S3
State Diagram
State Table
Q1(t) | Q0(t) | Q1(t+1) | Q0(t+1)
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
Current state | Next State
S0 | S1
S1 | S2
S2 | S3
S3 | S0

## Slide 13
Counter: Excitation table ⇒ K map ⇒ Logic Diagram
Q1(t) | Q0(t) | Q1(t+1) | Q0(t+1)
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
Q0(t)
Q1(t)
D
Q
Q’
D
Q
Q’
CLK
Circuit with 2 flip flops
Combinational circuit
D0(t) = Q0(t)’
D1(t) = Q0(t) Q1(t)’ + Q0(t)’ Q1(t)

## Slide 14
State Table
Q1(t) | Q0(t) | Q1(t+1) | Q0(t+1)
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
We store the current state using D-flip flops so that:
Inputs to the combinational circuit don’t change while the next output is being computed
The transition to the next state only occurs at the rising edge of the clock
Q0(t)
Q1(t)
D
Q
Q’
D
Q
Q’
CLK
Q0(t+1) = Q0(t)’
Q1(t+1) = Q0(t) Q1(t)’ + Q0(t)’ Q1(t)
Counter: Excitation table ⇒ K map ⇒ Logic Diagram

## Slide 15
Counter: Verification (Simulation)
Time | 0 | 1 | 2 | 3 | 4 | 5
 | 0 |  |  |  |  | 
 | 0 |  |  |  |  | 
Time | 0 | 1 | 2 | 3 | 4 | 5
 | 0 |  |  |  |  | 
 | 0 |  |  |  |  | 
Example: State sequence
Q0(t)
Q1(t)
D
Q
Q’
D
Q
Q’
CLK
Current state | Next State
S0 | S1
S1 | S2
S2 | S3
S3 | S0
Notes: All these forms are equivalent. Given one, we can derive the others.

## Slide 16
Example: Simulation from state table/state diagram
0/0
S0
S1
S3
S2
0/0
1/1
0/1
0, 1/0
1/0
1/0
PS\Input | X=0 | X=1
S0 | S0,0 | S2,0
S1 | S3,0 | S3,0
S2 | S2,0 | S1,0
S3 | S1,1 | S0,1
Time | 0 | 1 | 2 | 3 | 4 | 5
Input | 0 | 1 | 1 | 0 | 1 | -
State | S0 |  |  |  |  | 
Output |  |  |  |  |  | 
Example: Output sequence
Notes: All these forms are equivalent. Given one, we can derive the others.

## Slide 17
Example: Simulation from state table/state diagram
0/0
S0
S1
S3
S2
0/0
1/1
0/1
0, 1/0
1/0
1/0
PS\Input | X=0 | X=1
S0 | S0,0 | S2,0
S1 | S3,0 | S3,0
S2 | S2,0 | S1,0
S3 | S1,1 | S0,1
Time | 0 | 1 | 2 | 3 | 4 | 5
Input | 0 | 1 | 1 | 0 | 1 | -
State | S0 | S0 | S2 | S1 | S3 | S0
Output | 0 | 0 | 0 | 0 | 1 | 0
Example: Output sequence
Notes: All these forms are equivalent. Given one, we can derive the others.

## Slide 18: Example: Life on Mars?
Mars rover has a binary input x. When it receives the input sequence x(t-2, t) = 001 from its life detection sensors, it means that the it has detected life on Mars  and the output y(t) = 1, otherwise y(t) = 0 (no life on Mars ).
Implement the Life-on-Mars Pattern Recognizer!

## Slide 19: Mars Life Recognizer FSM
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0
Which of the following diagrams is a correct Mealy solution for the 001 pattern recognizer on the Mars rover?
A.
S1
S0
0/0
1/0
1/0
0/0
S2
1/1
B.
0/0
C. Both A and B are correct
D. None of the above
Input/output

## Slide 20
Pattern Recognizer ‘001’
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0
C1
C2
CLK
x(t)
y(t)
Mealy Machine
S(t)
What does state table need to show to design controls of C1?
next state S(t+1) vs. input x(t), and present state S(t)
output y(t) vs. input x(t), and present state S(t)
output y(t) vs. present state S(t)
None of the above
Mars Life Recognizer FFs

## Slide 21
State Diagram => State Table with State Assignment
State Assignment
S0: 00
S1: 01
S2: 10
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S0,1
S(t)\x | 0 | 1
00 | 01,0 | 00,0
01 | 10,0 | 00,0
10 | 10,0 | 00,1
Q1(t+1)Q0(t+1), y
C1
C2
CLK
x(t)
y(t)
Mealy Machine
S(t)
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0

## Slide 22: State Diagram => State Table => Excitation Table => Circuit
Q1(t) Q0(t)\x | 0 | 1
00 | 01,0 | 00,0
01 | 10,0 | 00,0
10 | 10,0 | 00,1
id | Q1Q0x | D1 | D0 | y
0 | 000 | 0 | 1 | 0
1 | 001 | 0 | 0 | 0
2 | 010 | 1 | 0 | 0
3 | 011 | 0 | 0 | 0
4 | 100 | 1 | 0 | 0
5 | 101 | 0 | 0 | 1
6 | 110 |  |  | 
7 | 111 |  |  | 
C1
C2
CLK
x(t)
y(t)
Mealy Machine
S(t)

## Slide 23: State Diagram => State Table => Excitation Table => Circuit
Q1(t) Q0(t)\x | 0 | 1
00 | 01,0 | 00,0
01 | 10,0 | 00,0
10 | 10,0 | 00,1
id | Q1Q0x | D1 | D0 | y
0 | 000 | 0 | 1 | 0
1 | 001 | 0 | 0 | 0
2 | 010 | 1 | 0 | 0
3 | 011 | 0 | 0 | 0
4 | 100 | 1 | 0 | 0
5 | 101 | 0 | 0 | 1
6 | 110 |  |  | 
7 | 111 |  |  | 
C1
C2
CLK
x(t)
y(t)
Mealy Machine
S(t)
Example: What to fill in rows 6 and 7 of excitation table?
All 0s
All 1s
All Don’t Cares

## Slide 24
0 2 6 4
1 3 7 5
x(t)
Q1
0 1 X 1
0 0 X 0
Q0
D1(t):
D1(t) = x’Q0 + x’Q1
D0 (t)= Q’1Q’0 x’
y= Q1x
State Diagram => State Table => Excitation Table => Circuit
id | Q1Q0x | D1 | D0 | y
0 | 000 | 0 | 1 | 0
1 | 001 | 0 | 0 | 0
2 | 010 | 1 | 0 | 0
3 | 011 | 0 | 0 | 0
4 | 100 | 1 | 0 | 0
5 | 101 | 0 | 0 | 1
6 | 110 | X | X | X
7 | 111 | X | X | X

## Slide 25
D1(t) = x’Q0 + x’Q1
D0 (t)= Q’1Q’0 x’
y= Q1x
D
Q
Q’
D
Q
Q’
Q1
Q0
D1
D0
Q0
Q1
x’
x
y
Q’1
Q’0
x’
State Diagram => State Table => Excitation Table => Circuit
C1
C2
CLK
x(t)
y(t)
Mealy Machine
S(t)

## Slide 26: Mealy and Moore Machines: Canonical Form
Combinational
Logic
x(t)
y(t)
CLK
C2
C1
y(t)
CLK
x(t)
C1
C2
CLK
x(t)
y(t)

## Slide 27
Mealy Machine: yi(t) = fi(X(t), S(t))
Moore Machine: yi(t) = fi(S(t))
si(t+1) = gi(X(t), S(t))
x(t)
C1
C2
CLK
x(t)
y(t)
Moore Machine
C1
C2
CLK
y(t)
Mealy Machine
S(t)
S(t)
Mealy and Moore Machines: Canonical Form

## Slide 28
Mealy Machine: yi(t) = fi(X(t), S(t))
Moore Machine: yi(t) = fi(S(t))
si(t+1) = gi(X(t), S(t))
Mealy and Moore Machines: Canonical Form
x(t)
C1
C2
CLK
x(t)
y(t)
Moore Machine
C1
C2
CLK
y(t)
Mealy Machine
S(t)
S(t)
 | Input | 
PS | NS | Output
 | Input
PS | NS, output
S
Sj
output
input
Si
output
S
Sj
input/output
Si

## Slide 29: Mealy and Moore Machines: Mars Life Recognizer
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0
Which of the following diagrams is a correct Moore solution to the ‘001’ pattern recognizer?
A.
B.
C. Both A and B are correct
D. None of the above
S1
0
S0
0
1
0
1
S2
0
0
1
S3
1
1
0
input
output
input/output

## Slide 30: Mealy and Moore Machines: Mars Life Recognizer
Pattern Recognizer ‘001’
What does state table need to show to design controls of C2?
(current input x(t), current state S(t) vs. next state, S(t+1))
(current input, current state vs. current output y(t))
(current state vs. current output y(t) and next state)
(current state vs. current output y(t) )
None of the above
C1
C2
CLK
x(t)
y(t)
Moore Machine
S(t)
S1
0
S0
0
1
0
1
S2
0
0
1
S3
1
1
0

## Slide 31: Mealy and Moore Machines: Mars Life Recognizer
Q1Q0\x | 0 | 1
00 | 01,0 | 00,0
01 | 10,0 | 00,0
10 | 10,0 | 11,0
11 | 01,1 | 00,1
Q1(t+1)Q0(t+1), y
ID | Q1Q0x | D1 | D0 | y
0 | 000 | 0 | 1 | 0
1 | 001 | 0 | 0 | 0
2 | 010 | 1 | 0 | 0
3 | 011 | 0 | 0 | 0
4 | 100 | 1 | 0 | 0
5 | 101 | 1 | 1 | 0
6 | 110 | 0 | 1 | 1
7 | 111 | 0 | 0 | 1
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S3,0
S3 | S1,1 | S0,1
S1
0
S0
0
1
0
1
S2
0
0
1
S3
1
1
0

## Slide 32: Mealy and Moore Machines: Mars Life Recognizer
id | Q1Q0x | D1 | D0 | y
0 | 000 | 0 | 1 | 0
1 | 001 | 0 | 0 | 0
2 | 010 | 1 | 0 | 0
3 | 011 | 0 | 0 | 0
4 | 100 | 1 | 0 | 0
5 | 101 | 1 | 1 | 0
6 | 110 | 0 | 1 | 1
7 | 111 | 0 | 0 | 1
0 2 6 4
1 3 7 5
x(t)
Q1
1 0 1 0
0 0 0 1
Q0
D0(t):
0 2 6 4
1 3 7 5
x(t)
Q1
0 1 0 1
0 0 0 1
Q0
D1(t):
0 2 6 4
1 3 7 5
x(t)
Q1
0 0 1 0
0 0 1 0
Q0
y(t):

## Slide 33: Mealy and Moore Machines: Mars Life Recognizer
D
Q
Q’
D
Q
Q’
Q1
Q0
D1
D0
y
State Diagram => State Table => Excitation Table => Circuit
C1
C2
CLK
x(t)
y(t)
Moore Machine
S(t)
D1(t)= Q1(t)Q0(t)’+Q1(t)’Q0(t) x(t)
D0(t)= Q1(t)’Q0(t)’x(t)’+
Q1(t)Q0(t) x(t)’+Q1(t)Q0(t)’ x(t)
y(t)= Q1(t)Q0(t)

## Slide 34: Conversion from Mealy to Moore Machine
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S3,0
S3 | S1,1 | S0,1
S1
0
S0
0
0
1
0
1
S2
0
0
1
S3
1
1
0
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S0,1
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0

## Slide 35: Conversion from Mealy to Moore Machine
S(t)\x | 0 | 1 | y
S0 | S1 | S0 | 0
S1 | S2 | S0 | 0
S2 | S2 | S3 | 0
S3 |  |  | 
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S0,1
Algorithm
1. Identify distinct (NS, y) pair
2. Replace each distinct (NS, y) pair with distinct new states
3. Insert rows of present state = new states

## Slide 36: Conversion from Mealy to Moore Machine
S(t)\x | 0 | 1 | y
S0 | S1 | S0 | 0
S1 | S2 | S0 | 0
S2 | S2 | S3 | 0
S3 |  |  | 
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S0,1
1. Find distinct NS, y
2. Add new states to represent distinct NS, y
iClicker
For the above Moore machine, what are the next states with respect to present state S3?
S2, S3, 1
S2, S0, 1
S1, S0, 1
S1, S0. 0
None of the above.
Mealy
Moore

## Slide 37: Conversion from Mealy to Moore Machine
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S3,0
S3 | S1,1 | S0,1
S1
0
S0
0
0
1
0
1
S2
0
0
1
S3
1
1
0
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S0,1
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
x | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
Smealy | S0 | S1 | S0 | S1 | S2 | S0 | S0 | S1 | S2
ymealy |  |  |  |  |  |  |  |  | 
Smoore | S0 |  |  |  |  |  |  |  | 
ymoore |  |  |  |  |  |  |  |  | 

## Slide 38: Conversion from Mealy to Moore Machine
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S3,0
S3 | S1,1 | S0,1
S1
0
S0
0
0
1
0
1
S2
0
0
1
S3
1
1
0
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S0,1
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
x | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
Smealy | S0 | S1 | S0 | S1 | S2 | S0 | S0 | S1 | S2
ymealy |  |  |  |  |  |  |  |  | 
Smoore | S0 |  |  |  |  |  |  |  | 
ymoore |  |  |  |  |  |  |  |  | 
iClicker Smoore[0-5]
S0,S1,S0,S1,S2,S3
S0,S1,S0,S1,S2,S0
S3,S1,S0,S1,S2,S3
S3,S1,S0,S1,S2,S0
E. None of the above

## Slide 39: Conversion from Mealy to Moore Machine
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S3,0
S3 | S1,1 | S0,1
S1
0
S0
0
0
1
0
1
S2
0
0
1
S3
1
1
0
S(t)\x | 0 | 1
S0 | S1,0 | S0,0
S1 | S2,0 | S0,0
S2 | S2,0 | S0,1
S1
S0
0/0
1/0
0/0
1/1
S2
0/0
1/0
Time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
x | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
Smealy | S0 | S1 | S0 | S1 | S2 | S0 | S0 | S1 | S2
ymealy |  |  |  |  |  |  |  |  | 
Smoore | S0 |  |  |  |  |  |  |  | 
ymoore |  |  |  |  |  |  |  |  | 
iClicker ymoore[0-5]
0,0,0,0,1,0
0,0,0,0,0,1
0,1,0,0,0,0
0,0,0,0,0,0,
None of the above

## Slide 40: Conversion from Mealy to Moore Machine
Algorithm
1. Identify distinct (NS, y) pair
2. Replace each distinct (NS, y) pair with distinct new states
3. Insert rows of present state = new states
4. Append each present state with its output y

## Slide 41: Example: Traffic Light Controller
Traffic sensors: TA, TB (TRUE when there’s traffic)
Lights: LA, LB

## Slide 42: Traffic Light Controller: FSM Black Box
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB

## Slide 43: FSM State Transition Diagram
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs

## Slide 44: FSM State Transition Diagram
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs

## Slide 45: FSM State Transition Table
PS | Inputs |  | NS
 | TA | TB | 
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0

## Slide 46: State Transition Table
PS |  | Inputs |  | NS | 
Q1(t) | Q0(t) | TA | TB | Q1(t +1) | Q0(t +1)
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
Q1(t+1)= Q1(t)Q0(t)
Q0(t+1)= Q’1(t)Q’0(t)T’A + Q1(t)Q’0(t)T’B

## Slide 47: Traffic Light Controller: FSM Output Table
PS |  | Outputs |  |  | 
Q1 | Q0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = Q1
LA0 = Q’1Q0
LB1 = Q’1
LB0 = Q1Q0

## Slide 48: Traffic Light Controller: State Register

## Slide 49: Traffic Light Controller: Logic Diagram

## Slide 50: Traffic Light Controller: Output Logic

## Slide 51: Summary: Implementation
Set up canonical form
  Mealy or Moore machine
Identify the next states
  state diagram ⇨ state table
  state assignment
Derive excitation table
  Inputs of flip flops
Design the combinational logic
  don’t care set utilization