## Slide 1: CSE 140 Lecture 17 System Design II
CK Cheng
CSE Dept.
UC San Diego

## Slide 2: High Level Synthesis
Hierarchical Description
  4-Phase Handshaking
Graph Representation
  Control/Data Flow Graphs
Data Subsystem
  Allocation
  Binding
Scheduling
  Finite State Machine
Reference:
Bluespec System
FPGAs for Software Programmers, D. Koch, F. Hannig, D. Ziener, Springer 2016

## Slide 3: High Level Synthesis
Describe system in programs
Data subsystem
  List data operations
  Map operations to functional blocks
  Add interconnect for data transport
  Input control signals and output conditions
Control Subsystem
  Derive the sequence according to the hardware program
  Create the sequential machine
  Input conditions and output control signals

## Slide 4: Example: Multiplication
Arithmetic
Z=X × Y
M=0
For i=n-1 to 0
  If Yi=1, M=M+X × 2i
Z=M
Input X, Y
Output Z
Variable M, i
M=0
For i=n-1 to 0
  If Yn-1=1, M=M+X
  Shift Y left by one bit
  If i != 0, shift M left by one bit
Z=M

## Slide 6: Implementation: Example
Multiply(X, Y, Z, start, done)
{ Input X[15:0], Y[15:0] type bit-vector, start type Boolean;
Local-Object A[15:0], B[15:0] ,M[31:0], i[4:0] type bit-vector;
Output Z[31:0] type bit-vector, done type Boolean;
S0: If start’ goto S0 || done 1;
S1: A  X || B  Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M  M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done 1|| goto S0;
}

## Slide 7: Step 0: Syntax
Multiply(X, Y, Z, start, done)
{ Input X[15:0], Y[15:0] type bit-vector, start type boolean;
Local-Object A[15:0], B[15:0] ,M[31:0], i[4:0] type bit-vector;
Output Z[31:0] type bit-vector, done type boolean;
S0: If start’ goto S0 || done 1;
S1: A  X || B  Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M  M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done 1|| goto S0;
}

## Slide 8
Z=XY
Data
Subsystem
Control
Subsystem
?
X
Y
start
Z
done
16
16
32
Multiply(X, Y, Z, start, done)
{ Input: X[15:0], Y[15:0] type bit-vector, start type boolean;
Local-Object : A[15:0], B[15:0], M[31:0], i[4:0] type bit-vector;
Output Z[31:0] type bit-vector,
done type boolean;
S0: If start’ goto S0 || done 1;
S1: A  X || B  Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M  M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done 1|| goto S0;
}
Step 1: Identify Input and Output of data and control subsystems
B15,i4

## Slide 9
Step 2: Identify Condition Bits to Control Subsystem
Data
Subsystem
Control
Subsystem
?
B15,, i4
X
Y
start
Z
done
16
16
32
Multiply(X, Y, Z, start, done)
{ Input: X[15:0], Y[15:0] type bit-vector, start type boolean;
Local-Object : A[15:0], B[15:0] ,M[31:0], i[4:0] type bit-vector;
Output Z[31:0] type bit-vector, done type boolean;
S0: If start’ goto S0 || done  1;
S1:AX || B Y || i 0 || M 0 || done0;
S2: If B15 = 0 goto S4 || i i+1;
S3: M  M+A;
S4: if i>= 16, goto S6
S5: M Shift(M,L,1) || B Shift(B,L,1) || goto S2;
S6: Z: M || done 1|| goto S0;
}

## Slide 10
Z=XY
Data
Subsystem
Control
Subsystem
?
B15,i4
X
Y
start
Z
done
16
16
32
Step 3: Identify Data Subsystem Operations
Multiply(X, Y, Z, start, done)
{ Input: X[15:0], Y[15:0] type bit-vector,
start type boolean;
Local-Object : A[15:0], B[15:0] ,M[31:0],
i[4:0] type bit-vector;
Output Z[31:0] type bit-vector,
done type boolean;
S0: If start’ goto S0 || done 1;
S1: A  X || B  Y || i0 || M0 || done  0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M  M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z: M || done 1|| goto S0;
}

## Slide 11
Step 4: Map Data Operations to Implementable functions
Multiply(X, Y, Z, start, done)
{ Input: X[15:0], Y[15:0] type bit-vector,
start type boolean;
Local-Object : A[15:0], B[15:0] ,M[31:0],
i[4:0] type bit-vector;
Output Z[31:0] type bit-vector,
done type boolean;
S0: If start’ goto S0 || done1;
S1: A  X || B  Y || i0 || M0 || done  0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M  M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z: M || done 1|| goto S0;
}
A  X
B Y
M0
i0
ii+ 1
MM+A
MShift(M,L,1)
BShift(B,L,1)
Z:M
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)
Wires

## Slide 12
Step 5: Implement the Data Subsystem from Standard Modules
LD
C
R
D
Registers: If C then R  D
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)

## Slide 13
Storage Component: Registers with control signals
LD
C
R
D
Registers: If C then R  D
Y
LD
B[15]
Register B
D
R
16
X
LD
16
Register A
D
R
A
CLR
32
Register M
D
R
M
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)

## Slide 14
Data Subsystem
Y
LD
B
Register B
D
R
16
X
LD
16
Register A
D
R
A
CLR
32
Register M
D
R
M
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)

## Slide 15
Function Modules: Adder, Shifter
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)
C5
Y
LD
Register B
D
R
B[15]
B
<<
SHL
16
Selector
C2
0
1
C0
X
LD
16
Register A
D
R
A
C3
CLR
32
Register M
D
R
M
Adder
A
B
S
0
1
LD
C1
<<
SHL
C4
Selector
Registers B and M have multiple sources.

## Slide 16
Function Modules: Adder, Shifter, Counter
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)
C5
Y
LD
Register B
D
R
B[15]
B
<<
SHL
16
Selector
C2
0
1
C6
C7
CLR Inc
i[4]
Counter i
D
R
C0
X
LD
16
Register A
D
R
A
C3
CLR
32
Register M
D
R
M
Adder
A
B
S
0
1
LD
C1
<<
SHL
C4
Selector

## Slide 17
Step 6: Map Control Signals to Operations
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)
C5
Y
LD
Register B
D
R
B[15]
B
<<
SHL
16
Selector
C2
0
1
C6
C7
CLR Inc
i[4]
Counter i
D
R
C0
X
LD
16
Register A
D
R
A
C3
CLR
32
Register M
D
R
M
Adder
A
B
S
0
1
LD
C1
<<
SHL
C4
Selector
control
C0=1
C2=0 and C5 =1
C3 =1
C6 =1
C7 =1
C1=0 and C4=1
C1=1 and C4=1
C2=1 and C5 =1

## Slide 18
Z=XY
Data
Subsystem
Control
Subsystem
C0:7
X
Y
start
Z
done
16
16
32
Step 7: Identify Control Path Components
Multiply(X, Y, Z, start, done)
{ Input: X[15:0], Y[15:0] type bit-vector,
start type boolean;
Local-Object : A[15:0], B[15:0] ,M[31:0],
i[4:0] type bit-vector;
Output Z[31:0] type bit-vector,
done type boolean;
S0: If start’ goto S0 || done1;
S1: A X || B Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done1|| goto S0;
}
B[15], i[4]
Control
Unit
B[15]
C0-7
start
done
i[4]

## Slide 19
Data
Subsystem
Control
Subsystem
C0:7
X
Y
start
Z
done
16
16
32
B[15], i[4]

## Slide 20
 | C0 Load A | C1 Feed M | C2 Feed B | C3 Clr M | C4 Load M | C5 Load B | C6 Clr i | C7 Inc i | done
S0 | 0 |  |  | 0 | 0 | 0 | 0 | 0 | 1
S1 | 1 |  |  | 1 | 0 | 1 | 1 | 0 | 0
S2 | 0 |  |  | 0 | 0 | 0 | 0 | 1 | 0
S3 | 0 |  |  | 0 | 1 | 0 | 0 | 0 | 0
S4 | 0 |  |  | 0 | 0 | 0 | 0 | 0 | 0
S5 | 0 |  |  | 0 | 1 | 1 | 0 | 0 | 0
S6 | 0 |  |  | 0 | 0 | 0 | 0 | 0 | 1
Multiply(X, Y, Z, start, done) {
S0: If start’ goto S0 || done1;
S1: A X || B Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done1|| goto S0;}
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)
control
C0=1
C2=0 and C5 =1
C3 =1
C6 =1
C7 =1
C1=0 and C4=1
C1=1 and C4=1
C2=1 and C5 =1

## Slide 21
 | C0 Load A | C1 Feed M | C2 Feed B | C3 Clr M | C4 Load M | C5 Load B | C6 Clr i | C7 Inc i | done
S0 | 0 | X | X | 0 | 0 | 0 | 0 | 0 | 1
S1 | 1 | X | 0 | 1 | 0 | 1 | 1 | 0 | 0
S2 | 0 | X | X | 0 | 0 | 0 | 0 | 1 | 0
S3 | 0 | 0 | X | 0 | 1 | 0 | 0 | 0 | 0
S4 | 0 | X | X | 0 | 0 | 0 | 0 | 0 | 0
S5 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
S6 | 0 | X | X | 0 | 0 | 0 | 0 | 0 | 1
Multiply(X, Y, Z, start, done) {
S0: If start’ goto S0 || done1;
S1: A X || B Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done1|| goto S0;}
operation
A  Load (X)
B  Load (Y)
M Clear(M)
i Clear(i)
i  INC(i)
M Add(M,A)
M  SHL(M)
B  SHL(B)
control
C0=1
C2=0 and C5 =1
C3 =1
C6 =1
C7 =1
C1=0 and C4=1
C1=1 and C4=1
C2=1 and C5 =1

## Slide 22
Design of the Control Subsystem
Multiply(X, Y, Z, start, done)
{
S0: If start’ goto S0 || done1;
S1: A X || B Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done1|| goto S0
}
Control
Subsystem
B[15]
C0-7
start
done
i[4]

## Slide 23
Control Subsystem
S0
S1
S2
S3
S5
S4
B[15]
start’
start
i[4]
B[15]’
i[4]’
S6
Multiply(X, Y, Z, start, done)
{
S0: If start’ goto S0 || done1;
S1: A X || B Y || i0 || M0 || done 0;
S2: If B15 = 0 goto S4 || ii+1;
S3: M M+A;
S4: if i>= 16, goto S6
S5: MShift(M,L,1) || BShift(B,L,1) || goto S2;
S6: Z:M || done1|| goto S0
}

## Slide 24
State Assignment
Binary | b2b1b0
S0 | 000
S1 | 001
S2 | 010
S3 | 011
S4 | 100
S5 | 101
S6 | 110
S7 | 111
Gray | b2b1b0
S0 | 000
S1 | 001
S2 | 011
S3 | 010
S4 | 110
S5 | 111
S6 | 101
S7 | 100
One Hot | b7b6b5b4b3b2b1b0
S0 | 0 0 0 0 0 0 0 1
S1 | 0 0 0 0 0 0 1 0
S2 | 0 0 0 0 0 1 0 0
S3 | 0 0 0 0 1 0 0 0
S4 | 0 0 0 1 0 0 0 0
S5 | 0 0 1 0 0 0 0 0
S6 | 0 1 0 0 0 0 0 0
S7 | 1 0 0 0 0 0 0 0
One Hot Encoding: n bits for n states. Bit i=1 for state i.

## Slide 25
Control Subsystem: One-Hot State Machine Design
Input: State Diagram
Use a flip flop to replace each state.
  Set the flip flop which corresponds to the initial state and reset the rest flip flops.
Use an OR gate to collect all inward edges.
Use a Demux to distribute the outward edges.

## Slide 26
start
start’
S2
S3
B15
B15’
S5
S6
S0
S1
S4
i[4]
i[4]’
One-Hot State Machine
S0
S1
S2
S3
S5
S4
B[15]
start’
start
i[4]
B[15]’
i[4]’
S6

## Slide 27
Control Subsystem: One-Hot State Machine Design
Input: State Diagram
Use a flip flop to replace each state.
  Set the flip flop which corresponds to the initial state and reset the rest flip flops.
Use an OR gate to collect all inward edges.
Use a Demux to distribute the outward edges.

## Slide 28: Implementation: Example
Given a hardware program, implement data path and control subsystems
{ Input X[7:0], Y[7:0] type bit-vector, start type boolean;
Local-Object A[7:0], B[7:0] type bit-vector;
Output Z[7:0] type bit-vector, done type boolean;
Wait: If start’ goto Wait || done1;
S1: A X || B Y|| done 0;
S2: If B >= 0 goto S4;
S3: B -B;
S4: If A >= B goto S6;
S5: A A + 1 || B B-1 || goto S4;
S6: Z 4 * A || done 1 || goto Wait;
}

## Slide 29
Data
Subsystem
Control
Subsystem
?
?
X
Y
start
Z
done
8
8
8
Some_function
{ Input X[7:0], Y[7:0] type bit-vector,
start type boolean;
Local-Object A[7:0], B[7:0] type bit-vector;
Output Z[7:0] type bit-vector,
done type boolean;
Wait: If start’ goto Wait || done1;
S1: A X || B Y|| done 0;
S2: If B >= 0 goto S4;
S3: B -B;
S4: If A >= B goto S6;
S5: A A + 1 || B B-1 || goto S4;
S6: Z 4 * A || done 1 || goto Wait;
}
Step 1: Identify Input and Output of data and control subsystems

## Slide 30
Step 2: Identify Data Subsystem Operations
Some_function
{ Input X[7:0], Y[7:0] type bit-vector,
start type boolean;
Local-Object A[7:0], B[7:0] type bit-vector;
Output Z[7:0] type bit-vector,
done type boolean;
Wait: If start’ goto Wait || done1;
S1: A X || B Y|| done 0;
S2: If B >= 0 goto S4;
S3: B -B;
S4: If A >= B goto S6;
S5: A A + 1 || B B-1 || goto S4;
S6: Z 4 * A || done 1 || goto Wait;
}
Data
Subsystem
Control
Subsystem
?
?
X
Y
start
Z
done
8
8
8
Z =
4 Ceiling[ (X + |Y| )/ 2] if X< |Y|
4X otherwise

## Slide 31
Step 2: Identify Data Subsystem Operations
Some_function
{ Input X[7:0], Y[7:0] type bit-vector,
start type boolean;
Local-Object A[7:0], B[7:0] type bit-vector;
Output Z[7:0] type bit-vector,
done type boolean;
Wait: If start’ goto Wait || done1;
S1: A X || B  Y|| done <= 0;
S2: If B >= 0 goto S4;
S3: B  -B;
S4: If A >= B goto S6;
S5: A  A + 1 || B B-1 || goto S4;
S6: Z  4 * A || done  1 || goto Wait;
}
Data
Subsystem
Control
Subsystem
?
?
X
Y
start
Z
done
8
8
8

## Slide 32
Step 2: Map Data Operations to Implementable functions
{Input X[7:0], Y[7:0] type bit-vector,
start type boolean;
Local-Object A[7:0], B[7:0] type bit-vector;
Output Z[7:0] type bit-vector,
done type boolean;
Wait: If start’ goto Wait || done1;
S1: A X || B Y|| done <= 0;
S2: If B >= 0 goto S4;
S3: B -B;
S4: If A >= B goto S6;
S5: A A + 1 || B  B-1 || goto S4;
S6: Z  4 * A || done  1 || goto Wait;
}
A  X
B  Y
B  -B
A >= B
A  A + 1
B  B – 1
Z  4A
operation
A  Load (X)
B  Load (Y)
B  CS (B)
Comp (A, B)
A  INC (A)
B  DEC (B)
Z  SHL(A)

## Slide 33
Step 3: Tag each Data Operations with a Control Signal
A  X
B  Y
B  -B
A ≥ B
A  A + 1
B  B – 1
Z  4A
operation
A  Load (X)
B  Load (Y)
B  CS (B)
Comp (A, B)
A  INC (A)
B  DEC (B)
Z  SHL(A)
Data
Subsystem
Control
Subsystem
?
X
Y
start
Z
done
8
8
8

## Slide 34
Step 4: Identify Condition Bits to Control Subsystem
{Input X[7:0], Y[7:0] type bit-vector,
start type boolean;
Local-Object A[7:0], B[7:0] type bit-vector;
Output Z[7:0] type bit-vector,
done type boolean;
Wait: If start’ goto Wait || done1;
S1: A  X || B  Y|| done  0;
S2: If B ≥ 0 goto S4;
S3: B  -B;
S4: If A ≥ B goto S6;
S5: A  A + 1 || B  B-1 || goto S4;
S6: Z  4 * A || done 1 || goto Wait;
}
Data
Subsystem
Control
Subsystem
C0:6
B7, A≥B
X
Y
start
Z
done
8
8
8

## Slide 35
C2
Y
LD
B[7]
Register B
D
R
8
C1
X
LD
8
Register A
D
R
A
Step 5: Implement the Data Subsystem from Standard Modules
operation
A  Load (X)
B  Load (Y)
B  CS (B)
Comp (A, B)
A  INC (A)
B  DEC (B)
Z  SHL(A)

## Slide 36
Reg
Reg
C2C3
C5
C1
C4
X
INC
Comp
ShiftReg
Control
Unit
B[7]
C6
C7
CS
DEC
Y
C1
C2
C3
C4
C5
C6
C7
start
done
LD
LD
B
A
Z
S
S1S0
0
1
2
1
0
LD Shift
A≥B

## Slide 37
S0:
S1:
S2:
S3:
S4:
S5:
S6:
S7:
S8:
If start’, goto S0, else goto S1 || done1
A  X || B  Y || done  0 || goto S2
If B’<7> goto S4, else goto S3
B  CS (B) || goto S4
If k goto S6, else goto S5
A  INC (A) || B  DEC (B) || goto S4
Z  A || goto S7
Z  SHL (z) || goto S8
Z  SHL (z) || done  1 ||goto S0
Step 6: Map Control Signals to Operations
Step 7: Identify Control Path Components
S0
S1
S2
S3
S4
S8
S7
S6
S5
k’
k
B[7]
B’[7]
start’
start

## Slide 38
start
start’
S2
S3
B7
B7’
S5
S6
S0
S1
S4
k
k’
S7
S8
One-Hot State Machine
S0
S1
S2
S3
S4
S8
S7
S6
S5
k’
k
B[7]
B’[7]
start’
start

## Slide 39
 | C1 | C2 | C3 | C4 A | C5 B | C6 Z | C7 | done
S0 |  |  |  | 0 | 0 | 0 | 0 | 1
S1 |  |  |  | 1 | 1 | 0 | 0 | 0
S2 |  |  |  | 0 | 0 | 0 | 0 | 0
S3 |  |  |  | 0 | 1 | 0 | 0 | 0
S4 |  |  |  | 0 | 0 | 0 | 0 | 0
S5 |  |  |  | 1 | 1 | 0 | 0 | 0
S6 |  |  |  | 0 | 0 | 1 | 0 | 0
S7 |  |  |  | 0 | 0 | 0 | 1 | 0
S8 |  |  |  | 0 | 0 | 0 | 1 | 1
If start’, goto S0, else goto S1 || done<=1
A  X || B  Y || done  0 || goto S2
If B’<7> goto S4, else goto S3
B  CS (B) ||goto S4
If k goto S6, else goto S5
A  INC (A) || B  DEC (B) || goto S4
Z  A || goto S7
Z  SHL (z) || goto S8
Z  SHL (z) || done<=1 || goto S0
S0:
S1:
S2:
S3:
S4:
S5:
S6:
S7:
S8:
Reg
Reg
C2C3
C5
C1
C4
X
INC
Comp
ShiftReg
Control
Unit
B[7]
C6
C7
CS
DEC
Y
C1
C2
C3
C4
C5
C6
C7
start
done
LD
LD
B
A
Z
S
S1S0
0
1
2
1
0
LD Shift
A≥B

## Slide 40: Summary
Hardware Allocation
  Balance between cost and performance
Resource Sharing and Binding
  Map operations to hardware
Interconnect Synthesis
  Convey signal transports
Operation Scheduling
  Sequence the process

## Slide 41
Remarks:
Implement the control subsystem with one-hot state machine design.
Try to reduce the latency of the whole system.