## Slide 1
CSE 140: Components and Design Techniques for Digital Systems
Lecture 3: Incompletely Specified Functions and K Maps
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Outlines
Definitions
  Minterms and Maxterms
  Incompletely Specified Function
Implementation: Boolean Algebra vs Map
Karnaugh Maps: Two Dimensional Truth Table
  2-Variable Map
  3-Variable Map
  Up to 6-Variable Map

## Slide 3: Definitions
Literals
Product Term
Sum Term
Minterm of n variables: A product of n literals in which every variable appears exactly once.
Maxterm of n variables: A sum of n literals in which every variable appears exactly once.
Adjacency of minterms (maxterms): Two minterms (maxterms) are adjacent if they differ by only one variable.

## Slide 4: Definitions: Examples
Minterm of n variables: A product of n literals in which every variable appears exactly once.
  E.g. For function are minterms, while are not.
Maxterm of n variables: A sum of n literals in which every variable appears exactly once.
Adjacency of minterms: Two minterms are adjacent if they differ by only one variable.
  E.g. abcde and a’bcde are adjacent, while a’b’cde and abc’d’e’ are not

## Slide 5: Examples
For two minterms ab’c’d’ and ab’cd’, are they adjacent?
Yes
No
Adjacency allows us to merge the terms to reduce the Boolean expression.

## Slide 6
Id a b f (a, b)
0 0 0 1
1 0 1 0
2 1 0 1
3 1 1 X (don’t care)
For example:
The input pattern does not happen.
The input pattern happens, but the output is ignored.
Example:
Decimal number 0… 9 uses 4 bits. (1,1,1,1) does not happen.
Situations where the output of a switching function can be either 0 or 1 for a particular combination of inputs
This is specified by a don’t care in the truth table
Incompletely Specified Function

## Slide 7: How to completely specify the truth table in canonical form? We have three types of output which divides the input space into three sets: On-set F: All the input conditions for which the output is 1 Off-set R: All the input conditions for which the output is 0 Don’t care set D: All the input conditions for which the output is a ‘don’t care’
Example: The truth table on right has
F covers input pattern {(a=1,b=0)}
R covers input pattern {(0,0)}
D covers input patterns {(0,1), (1,1)}
The union of F, R, D is the whole set of all input patterns.
Id | a | b | F
0 | 0 | 0 | 0
1 | 0 | 1 | X
2 | 1 | 0 | 1
3 | 1 | 1 | X
Incompletely Specified Function

## Slide 8: Incompletely Specified Function
Example: The truth table on right has
F covers input pattern (a,b)=(1,0)
R covers input pattern (a,b)=(0,0)
D covers input patterns (a,b)=(0,1) (1,1)
Id | a | b | F
0 | 0 | 0 | 0
1 | 0 | 1 | X
2 | 1 | 0 | 1
3 | 1 | 1 | X
We assign values to elements in don’t care set for logic designs.
Id | a | b | F
0 | 0 | 0 | 0
1 | 0 | 1 | 
2 | 1 | 0 | 1
3 | 1 | 1 | 

## Slide 9
Which of the following assignment would result in an implementation with the fewest gates?
Reducing Incompletely Specified Functions
Id | a | b | F(a,b)
0 | 0 | 0 | X
1 | 0 | 1 | 0
2 | 1 | 0 | 1
3 | 1 | 1 | 0
F(0,0)=1
F(0,0)=0
Neither A or B
Both A and B

## Slide 10: Implementation
Specification  Schematic Diagram
Net list,
Switching expression
Obj min cost  Search in solution space
(max performance)
Cost: wires, gates  Literals, product terms,
sum terms
For two level logic (sum of products or product of sums),
we want to minimize # of terms, and # of literals

## Slide 11: Implementation: Specification => Logic Diagram
Flow 1: Boolean Algebra
Specification
Truth table
Sum of products (SOP) or product of sums(POS) canonical form
Reduced expression using Boolean algebra
Schematic diagram of two level logic
Flow 2: K Map
Specification
Truth Table
Karnaugh Map (truth table in two dimensional space)
Reduce using K’Maps
Reduced expression (SOP or POS)
Schematic diagram of two level logic
Karnaugh Map: A 2-dimensional truth table

## Slide 12: Truth Table vs. Karnaugh Map
ID | A | B | f(A,B)
0 | 0 | 0 | f(0,0)
1 | 0 | 1 | f(0,1)
2 | 1 | 0 | f(1,0)
3 | 1 | 1 | f(1,1)
2-variable function, f(A,B)
 | B=0 | B=1
A=0 | f(0,0) | f(0,1)
A=1 | f(1,0) | f(1,1)

## Slide 13: Truth Table
ID | A | B | f(A,B) | minterm
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | A’B
2 | 1 | 0 | 1 | AB’
3 | 1 | 1 | 1 | AB
An example of 2-variable function, f(A,B)

## Slide 14
Function can be represented by sum of minterms:
f(A,B) = A’B+AB’+AB
This is not optimal however!
We want to minimize the number of literals and terms.

## Slide 15
To minimize the number of literals and terms.
We factor out common terms –
A’B+AB’+AB
= A’B+AB’+AB+AB
=(A’+A)B+A(B’+B)=B+A
Hence, we have
f(A,B) = A+B

## Slide 16: How can we guarantee the most reduced expression was reached?
Boolean expressions can be minimized by combining terms
K-maps minimize equations graphically
ID | A | B | f(A,B)
0 | 0 | 0 | f(0,0)
1 | 0 | 1 | f(0,1)
2 | 1 | 0 | f(1,0)
3 | 1 | 1 | f(1,1)
 | B=0 | B=1
A=0 | A’B’ | A’B
A=1 | AB’ | AB

## Slide 17
K-Map: Truth Table in 2 Dimensions
B = 0 B = 1
A = 0
A = 1
0 1
2 3
0 1
1 1
ID | A | B | f(A,B)
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | 1

## Slide 18
K-Map: Truth Table in 2 Dimensions
B = 0 B = 1
A = 0
A = 1
0 1
2 3
0 1
1 1
f(A,B) = A + B
ID | A | B | f(A,B)
0 | 0 | 0 | 0
1 | 0 | 1 | 1
2 | 1 | 0 | 1
3 | 1 | 1 | 1

## Slide 19: Two Variable K-maps
# possible 2-variable functions:
For 2 variables as inputs, we have 4=22 entries. Each entry can be 0 or 1. Thus we have 16=24 possible functions.
f(a,b)
a
b
id | a | b | f (a, b)
0 | 0 | 0 | f (0, 0)
1 | 0 | 1 | f (0, 1)
2 | 1 | 0 | f (1, 0)
3 | 1 | 1 | f (1, 1)

## Slide 20: Representation of k-Variable Func.
Boolean Expression
Truth Table
Cube
K Map
Binary Decision Diagram
And-Inverter Graph
  Ref: R. Brayton and A. Mishchenko, “ABC: an academic industrial-strength verification tool,” ACM Int. Conf. on Computer Aided Verification, pp. 24-40, 2010.
A cube of 4 variables: (A,B,C,D)
(0,1,1,1)
(0,1,1,0)
(0,0,0,0)
(0,0,0,1)
(1,0,0,1)
(1,1,1,1)
(1,1,0,1)
(1,0,0,0)
(0,0,1,0)
(1,1,1,0)
(0,0,1,1)
(1,0,1,1)
(0,1,0,1)
(1,0,1,0)
D
C
B
A

## Slide 21: Corresponding three variable K-map
c = 1
(0,0) (0,1) (1,1) (1,0)
c = 0
Gray code (a,b)
Id a b c f (a,b,c)
0 0 0 0 1
1 0 0 1 0
2 0 1 0 1
3 0 1 1 0
4 1 0 0 1
5 1 0 1 0
6 1 1 0 1
7 1 1 1 0
Truth table

## Slide 22: Karnaugh Maps (K-Maps)
K-maps minimize equations graphically
Note that the label decides the order in the map

## Slide 24: K-map
Circle 1’s in adjacent squares
Find rectangles which correspond to product terms in Boolean expression
y(A,B)=A’B’C’+A’B’C= A’B’(C’+C)=A’B’

## Slide 25: Corresponding K-map
0 2 6 4
1 3 7 5
c = 1
0 1 X 1
0 0 1 1
(0,0) (0,1) (1,1) (1,0)
c = 0
Id a b c f (a,b,c)
0 0 0 0 0
1 0 0 1 0
2 0 1 0 1
3 0 1 1 0
4 1 0 0 1
5 1 0 1 1
6 1 1 0 X
7 1 1 1 1
Another 3-Input truth table

## Slide 26: Corresponding K-map
0 2 6 4
1 3 7 5
b = 1
c = 1
a = 1
0 1 X 1
0 0 1 1
(0,0) (0,1) (1,1) (1,0)
c = 0
f(a,b,c) = a + bc’
Id a b c f (a,b,c)
0 0 0 0 0
1 0 0 1 0
2 0 1 0 1
3 0 1 1 0
4 1 0 0 1
5 1 0 1 1
6 1 1 0 X
7 1 1 1 1
Another 3-Input truth table

## Slide 27: Corresponding K-map
0 2 6 4
1 3 7 5
c = 1
1 X 0 1
1 0 0 1
(0,0) (0,1) (1,1) (1,0)
c = 0
Id a b c f (a,b,c,d)
0 0 0 0 1
1 0 0 1 1
2 0 1 0 X
3 0 1 1 0
4 1 0 0 1
5 1 0 1 1
6 1 1 0 0
7 1 1 1 0
3-input truth table
Q: In the above case the minimal Boolean expression is obtained when the don’t care term is:
Included i.e. Circled in with one or more minterms that evaluate to 1
Excluded when grouping the minterms that evaluate to one
Either approach gives the minimal expression

## Slide 28: Corresponding K-map
0 2 6 4
1 3 7 5
c = 1
1 X 0 1
1 0 0 1
(0,0) (0,1) (1,1) (1,0)
c = 0
Id a b c f (a,b,c,d)
0 0 0 0 1
1 0 0 1 1
2 0 1 0 X
3 0 1 1 0
4 1 0 0 1
5 1 0 1 1
6 1 1 0 0
7 1 1 1 0
3-Input Truth table
Q: In the above case the minimal Boolean expression is obtained when the don’t care term is:
Included i.e. Circled in with one or more minterms that evaluate to 1
Excluded when grouping the minterms that evaluate to one
Either approach gives the minimal expression

## Slide 29: Corresponding K-map
0 2 6 4
1 3 7 5
b = 1
c = 1
a = 1
1 X 0 1
1 0 0 1
(0,0) (0,1) (1,1) (1,0)
c = 0
f(a,b,c) = b’
Id a b c f (a,b,c,d)
0 0 0 0 1
1 0 0 1 1
2 0 1 0 X
3 0 1 1 0
4 1 0 0 1
5 1 0 1 1
6 1 1 0 0
7 1 1 1 0
3-input truth table with Don’t cares

## Slide 30: Consensus Theorem in View of K Maps
Consensus Theorem: A’B+AC+BC=A’B+AC