## Slide 1
CSE 140: Components and Design Techniques for Digital Systems
Lecture 7:
Sequential Networks
CK Cheng
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Part II: Sequential Networks
Introduction
  Sequential Circuits
  Memory Hierarchy
  Basic Mechanism of Memory
Basic Building Blocks
  Latches
  Flip-Flops
  Examples of Memory Modules
Implementation

## Slide 3: 1. Introduction: What is a sequential circuit?
“A circuit whose output depends on current inputs and past outputs”
“A circuit with memory”
Memory: a key parameter is Time
Memory / Time steps
Clock
i
i
i
Notes: A combinational logic cannot have some sort of feedback loop where the output of a logic is also the input of it. A sequential network on the other hand can have this feature.

## Slide 4: 1. Introduction: Sequential Network Key features
Memory: Flip flops
Specification: Finite State Machines
Implementation: Excitation Tables
Main Theme: Timing
Present time = t and next time = t+1
Timing constraints to separate the present and next times.
Memory / Time steps
Clock
xi
yi
si
Notes: A combinational logic cannot have some sort of feedback loop where the output of a logic is also the input of it. A sequential network on the other hand can have this feature.

## Slide 5: 1. Introduction: Sequential Network Key features
Main Theme: Timing
Present time = t and next time = t+1
Timing constraints to separate the present and next times.
St+1
Y
X
Combinational
logic
St
clock
Y
X
Combinational
logic
St
clock
Notes: A combinational logic cannot have some sort of feedback loop where the output of a logic is also the input of it. A sequential network on the other hand can have this feature.

## Slide 6: 1. Introduction: Different Types of Memory/Storage
Typical Computer Memory Hierarchy
Tradeoff between speed (latency) and size
Size relates to
  Storage density (area/bit)
  Power (power/bit)
Registers/Latches
Register File (Static Memory- SRAM)
Cache Memory (Static Memory - SRAM)
Main Memory (Dynamic Memory – DRAM)
NVM Main Memory (Non-Volatile Memory– e.g. Flash)
Disk

## Slide 7: 1. Introduction: Fundamental Memory Mechanism

## Slide 8: 1. Introduction: Memory Mechanism Capacitive Load
Fundamental building block of sequential circuits
Two outputs: Q, Q
There is a feedback loop!
  In a typical combinational logic, there is no feedback loop.
No inputs

## Slide 9: 1. Introduction: Capacitive Loads
Consider the two possible cases:
  Q = 0: then Q’ = 1 and Q = 0 (consistent)
  Q = 1: then Q’ = 0 and Q = 1 (consistent)
  Bistable circuit stores 1 bit of state in the state variable, Q (or Q’ )
  Hold the value due to capacitive charges and feedback loop strengthening
But there are no inputs to control the state

## Slide 10: Example
Q. Given a memory component made of a loop of inverters, the number of inverters in the loop has to be
Even
Odd
No constraints

## Slide 11: 1. Introduction: Memory Storage Mechanism
Word line (WL) to access cell
Read – measure voltage difference between B+ and B-
Write – force values of B+ and B- which may flip the cell
Static Random Access Memory - SRAM
WL
B+
B-
Sense Amp
Write Driver

## Slide 12: 2. Basic Building Blocks
Latches (Level Sensitive)
  SR Latches, D Latches
Flip-Flops (Edge Triggered)
  D FFs, (JK FFs, T FFs)
Examples of Memory Modules
  Registers, Shift Registers, Pattern Recognizers, Counters, FIFOs

## Slide 13: 2. Basic Building Blocks: Flight attendant call button
Flight attendant call button
  Press call: light turns on
    Stays on after button released
  Press cancel: light turns off
  Logic gate circuit to implement this?
a
Bit
Storage
Blue light
Call
button
Cancel
button
1. Call button pressed – light turns on
Bit
Storage
Blue light
Call
button
Cancel
button
2. Call button released – light stays on
Bit
Storage
Blue light
Call
button
Cancel
button
3. Cancel button pressed – light turns off
SR latch implementation
  Call=1 : sets Q to 1 and keeps it at 1
  Cancel=1 : resets Q to 0
R
S
Q
C
all
button
Blue light
Cancel
button

## Slide 14: 2. Basic Building Blocks: SR (Set/Reset) Latch
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1

## Slide 15: 2. Basic Building Blocks: SR Latch Analysis
  S = 1, R = 0: then Q = 1 and Q = 0
  S = 0, R = 1: then Q = 0 and Q = 1

## Slide 16: 2. Basic Building Blocks: SR Latch Analysis
  S = 0, R = 0: then Q = Qprev
  S = 1, R = 1: then Q = 0 and Q = 0

## Slide 17: 2. Basic Building Blocks: SR Latch
Inputs: S, R State: (Q, y)
S
R
y
Q
S
R
y
Q
Q = (R+y)’
y = (S+Q)’

## Slide 18
id | S | R | Qt | yt | Qt | yt | Qt | yt | Qt | yt
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
2 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
5 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
9 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
14 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Truth table of SR latch with incremental steps in time

## Slide 19
“State Table” of SR latch
 | 00 | 01 | 10 | 11
00 | 11 | 01 | 10 | 00
01 | 01 | 01 | 10 | 00
10 | 10 | 01 | 10 | 00
11 | 00 | 01 | 10 | 00
 | 00 | 01 | 10 | 11
00 | 11 | 01 | 10 | 00
01 | 01 | 01 | 10 | 00
10 | 10 | 01 | 10 | 00
11 | 00 | 01 | 10 | 00
id | S | R | Qt | yt | Qt | yt | Qt | yt | Qt | yt
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
2 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
5 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
7 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0
9 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0
10 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
12 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
13 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
14 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 20
CASES:
SR=01: (Q,y) = (0,1)
SR=10: (Q,y) = (1,0)
SR=11: (Q,y) = (0,0)
SR= 00: (Q,y) does not change if (Q,y)=(1,0) or (0,1)
However, when (Q,y) = (0,0) or (1,1), the output keeps changing
Remark: To verify the design, we need to enumerate all combinations.

## Slide 21
01
11
00
10
00
10
10
01
00
00
11
10
01
00
01
11
10
11
01
11
Q y
State
SR
Q y
State
Transition
Present
State
Next
State
State diagram
\SR Qy | 00 | 01 | 10 | 11
00 | 11 | 01 | 10 | 00
01 | 01 | 01 | 10 | 00
10 | 10 | 01 | 10 | 00
11 | 00 | 01 | 10 | 00
State Table and State Diagram
State Table

## Slide 22
CASES:
SR=01: (Q,y) = (0,1)
SR=10: (Q,y) = (1,0)
SR=11: (Q,y) = (0,0)
SR= 00: (Q,y) does not change if (Q,y)=(1,0) or (0,1)
However, when (Q,y) = (0,0) or (1,1), the output keeps changing
Q. Suppose that we can set the initial state (Q,y)=(0,1). To avoid the SR latch output from toggling or behaving in an undefined way which input combinations should be avoided:
(S, R) = (0, 0)
(S, R) = (1, 1)
None of the above

## Slide 23
CASES:
SR=01: (Q,y) = (0,1)
SR=10: (Q,y) = (1,0)
SR=11: (Q,y) = (0,0)
SR= 00: (Q,y) does not change if (Q,y)=(1,0) or (0,1)
However, when (Q,y) = (0,0) or (1,1), the output keeps changing
We set the initial state (Q,y)=(0,1) or (1,0). To avoid the state (Q,y)= (0,0) or (1,1), we block the input SR=11.
Thus, without input SR=11, the state can only be (Q,y)=(0,1) or (1,0).

## Slide 24: SR Latch
01
11
00
10
00
10
10
01
00
00
11
10
01
00
01
11
10
11
01
11
The only way to reach state (Q,y)=(0,0) or (1,1) is via edge labeled SR=11.

## Slide 25: SR Latch
01
11
00
10
00
10
10
01
00
00
11
10
01
00
01
11
10
11
01
11
The only way to reach state (Q,y)=(0,0) or (1,1) is via edge labeled SR=11.

## Slide 26: 2. Basic Building Blocks: SR Latch Analysis
  S = 0, R = 0: then Q = Qprev and Q = Qprev (memory!)
  S = 1, R = 1: then Q = 0 and Q = 0 (invalid state: Q ≠ NOT Q)

## Slide 27
CASES
SR=01: (Q,y) = (0,1)
SR=10: (Q,y) = (1,0)
SR=11: (Q,y) = (0,0)
SR = 00: if (Q,y) = (0,0) or (1,1), the output keeps changing
Solutions: Avoid the case that SR = (1,1).
Characteristic Expression
Q(t+1) = S(t)+R’(t)Q(t)
Q(t+1)
NS (next state)
0 0 0 1 -
1 1 0 1 -
PS
inputs
00 01 10 11
State table
SR
Q(t)
2. Basic Building Blocks: SR Latch

## Slide 28: 2. Basic Building Blocks: SR Latch Symbol
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1 (S = 1, R = 0, Q = 1)
  Reset: Make the output 0 (S = 0, R = 1, Q = 0)
Must do something to avoid
invalid state (when S = R = 1)

## Slide 29: 2. Basic Building Blocks: SR Latch Symbol

## Slide 30: 2. Basic Building Blocks: D Latch
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1, D passes through to Q (the latch is transparent)
  When CLK = 0, Q holds its previous value (the latch is opaque)
Avoids invalid case when Q ≠ NOT Q

## Slide 31: 2. Basic Building Blocks: D Latch Internal Circuit

## Slide 32: 2. Basic Building Blocks: D Latch Internal Circuit

## Slide 33: 2. Basic Building Blocks: D Latch Internal Circuit

## Slide 34: 2. Basic Building Blocks: D Flip-Flop
Two inputs: CLK, D
Function
  The flip-flop “samples” D on the rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on the rising edge of CLK
A flip-flop is called an edge-triggered device because it is activated on the clock edge

## Slide 35: 2. Basic Building Blocks: D FF Internal Circuit

## Slide 36: D Flip-Flop Internal Circuit
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent, L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent, L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q

## Slide 37: D Flip-Flop vs. D Latch

## Slide 38: D Flip-Flop vs. D Latch

## Slide 39: 2. Basic Building Blocks: Latch and FF (two latches)
A latch can be considered as a door
CLK = 0, door is shut
CLK = 1, door is unlocked
A flip-flop is a two-door entrance
CLK = 1
CLK = 0
CLK = 1

## Slide 40: 2. Basic Building Blocks: D Flip-Flop (Delay)
D
CLK
Q
Q’
Id D Q(t) Q(t+1)
0 0 0 0
1 0 1 0
2 1 0 1
3 1 1 1
Characteristic Expression: Q(t+1) = D(t)
0 0 1
1 0 1
PS
D
0 1
State table
NS= Q(t+1)

## Slide 41: 2. Examples
Can D flip-flip serve as a memory component?
Yes
No

## Slide 42: 2. Examples: Rising vs. Falling Edge D FF
D
Q’
Q
Q’
D
Q
Symbol for rising-edge
triggered D flip-flop
Symbol for falling-edge
triggered D flip-flop
Clk
rising edges
Clk
falling edges
Internal design: Just invert servant clock rather than master
The triangle means clock input, edge triggered

## Slide 43
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state
2. Examples: Enabled D-FFs

## Slide 45: 2. Examples: Bit Storage Overview
S
R
D
Q
C
D latch
Only loads D value present at rising clock edge, so values can’t propagate to other flip-flops during same clock cycle.
*Transition happens between two level of flip-flops.
SR can’t be 11 if D is stable before and while C=1, and will be 11 for only a brief glitch even if D changes while C=1.
*Transition may cross many levels of latches.
S1
R1
S
Q
C
R
Level-sensitive SR latch
S and R only have effect when C=1. We can design outside circuit so SR=11 never happens when C=1. Problem: avoiding SR=11 can be a burden.
R (reset)
S (set)
Q
SR latch
S=1 sets Q to 1, R=1 resets Q to 0. Problem: SR=11 yield undefined Q.
D flip-flop
D latch
master
D latch
servant
Dm
Qm
C
m
Ds
D
Clk
Qs’
Cs
Qs
Q
’
Q

## Slide 47: 2. Examples: Shift register
Holds & shifts samples of input
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Time | Input | OUT1 | OUT2 | OUT3 | OUT4
0 | 1 | 0 | 0 | 0 | 0
1 | 0 |  |  |  | 
2 | 1 |  |  |  | 
3 | 1 |  |  |  | 
4 | 0 |  |  |  | 
5 | 0 |  |  |  | 
6 | 0 |  |  |  | 

## Slide 48: 2. Examples: Shift register
Holds & shifts samples of input
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Time | Input | OUT1 | OUT2 | OUT3 | OUT4
0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0
2 | 1 | 0 | 1 | 0 | 0
3 | 1 | 1 | 0 | 1 | 0
4 | 0 | 1 | 1 | 0 | 1
5 | 0 | 0 | 1 | 1 | 0
6 | 0 | 0 | 0 | 1 | 1

## Slide 49: 2. Examples: Pattern Recognizer
Combinational function of input samples
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
OUT

## Slide 50: 2. Examples: Counters
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Counts through : 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
Known as Mobius (or Johnson) counter
Sequences through a fixed set of patterns

## Slide 51: Appendix: slides on BSV Describing Sequential Ckts
State diagrams and next-state tables nor are suitable for describing very large digital designs
  large circuits must be described in a modular fashion -- as a collection of cooperating FSMs
BSV is a modern programming language to describe cooperating FSMs
  We will give various examples of FSMs in BSV

## Slide 52: Modulo-4 counter circuit
Modulo-4
counter
inc
Read the
counter
q0t+1 = ~inc∙q0t + inc∙~q0t
q1t+1 = ~inc∙q1t + inc∙~q1t∙q0t + inc∙q1t∙~q0t
“Optimized” logic
q0t+1 = inc  q0t
q1t+1 = (inc == 1) ? q0t  q1t : q1t
q0
inc
1
0
q1

## Slide 53: Modulo-4 counter circuit
q0t+1 = ~inc∙q0t + inc∙~q0t
q1t+1 = ~inc∙q1t + inc∙~q1t∙q0t + inc∙q1t∙~q0t
“Optimized” logic
q0t+1 =inc  q0t
q1t+1 =(inc == 1) ? q0tq1t:q1t
q0
inc
1
0
q1
PS\input | inc=0 | inc=1
00 | 00 | 01
01 | 01 | 10
10 | 10 | 11
11 | 11 | 00
PS: q1t q0t, NS: q1t+1 q0t+1

## Slide 54: modulo4 counter in BSV
module moduloCounter(Counter);
Reg#(Bit#(2)) cnt <- mkReg(0);
method Action inc;
cnt <={!cnt[1]&cnt[0] | cnt[1]&!cnt[0],
!cnt[0]};
endmethod
method Bit#(2) read;
return cnt;
endmethod
endmodule
~cnt[1]&…
inc.en
read
cnt
An action to specify how the value of the cnt is to be set
State specification
Initial value
Notes: (Andy) ‘r’ and ‘w’ are ‘_read’ and ‘_write’ in BSV, but ‘r’ and ‘w’ are much easier to write on slides.
(Andy) I changed ‘||’ to ‘|’ in the logic because || is the boolean or and | is the bitwise or.

## Slide 55: Interface
Modulo counter has the following interface, i.e., type
An interface can have many different implementations
  For example, the numbers may be represented as Gray code
interface Counter;
method Action inc;
method Bit#(2) read;
endinterface

## Slide 56: Modules
A module in BSV is like a class definition in Java or C++
  It has internal state
  The internal state can only be read and manipulated by the (interface) methods
  An action specifies which state elements are to be modified
  Actions are atomic -- either all the specified state elements are modified or none of them are modified (no partially modified state is visible)

## Slide 57: FIFO Interface
interface Fifo#(numeric type size, type t);
method Bool notFull;
method Bool notEmpty;
method Action enq(t x);
method Action deq;
method t first;
endinterface
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first
- enq should be called only if notFull returns True;
- deq and first should be called only if notEmpty returns True

## Slide 58: One-Element FIFO Implementation
module mkCFFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Bool notFull;
return !v;
endmethod
method Bool notEmpty;
return v;
endmethod
method Action enq(t x);
v <= True; d <= x;
endmethod
method Action deq;
v <= False;
endmethod
method t first;
return d;
endmethod
endmodule
x
en
en
enq
deq
Fifo
module
!full
!emty
first
notFull
notEmpty
first

## Slide 59: FIFO Module: methods with guarded interfaces
Every method has a guard (rdy wire); the value returned by a value method is meaningful only if its guard is true
Every action method has an enable signal (en wire); an action method is invoked (en is set to true) only if the guard is true
Guards make it possible to transfer the responsibility of the correct use of a method from the user to the compiler
Guards are extraordinarily convenient for programming and also enhance modularity of the code
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
interface Fifo#(numeric type size,
type t);
method Action enq(t x);
method Action deq;
method t first;
endinterface

## Slide 60: One-Element FIFO Implementation with guards
module mkCFFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x)
v <= True; d <= x;
endmethod
method Action deq
v <= False;
endmethod
method t first
return d;
endmethod
endmodule
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
if (!v);
if (v);
if (v);