## Slide 1: Lecture 7: Instruction Set Architecture
CSE 30: Computer Organization and Systems Programming
Winter 2014
Diba Mirza
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Outline
Steps in program translation
Hardware/Software Interface Preliminaries
  Instruction Set Architecture
    General ISA Design (Architecture)
    Architecture vs. Micro architecture
    Different types of ISA: RISC vs CISC
  Assembly programmer’s view of the system
    Registers: Special and general purpose
    Assembly and machine code (program translation detail)
    Layout of ARM instructions in memory
  Steps in program execution
  Basic Types of ARM Assembly Instructions

## Slide 3: Steps in program translation
Program in C
Helloworld.c
Code Time
Program:
Text file stored on computers hard disk or some secondary storage
Compile Time
Compiler
Hardware
Executable:
Program in machine code
+Data in binary
1000110001100010000000000000000
1000110011110010000000000000100
1010110011110010000000000000000
1010110001100010000000000000100
Run Time

## Slide 4: Compile time: What does gcc do?
% gcc hello.c
hello.c
gcc
a.out
“Source”
Program in C
#include <stdio.h>
void func1(int a, char *b)
{
if(a > 0)
{ *b = ‘a’; }
}
int main()
{…..
func1();
printf(“\abc”);
}
“Executable”: Equivalent program in machine language
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111

## Slide 5: Steps in gcc
The translation is actually done in a number of steps
hello.c
a.out
gcc
hello.s
Assembler(as)
Linker (ld)
hello.o
Compiler
(cpp)

## Slide 6: Steps in gcc
Ask compiler to show temporary files:
% gcc –S hello.c (gives hello.s – assembly code)
% gcc –c hello.c (gives hello.o – object module)
% gcc –o prog_hello hello.c (gives prog_hello.o - named executable)
hello.c
a.out
gcc
hello.s
as
cpp
cc1
ld
hello.o

## Slide 7: Include code written by others
Code written by others (libraries) can be included
ld (linkage editor) merges one or more object files with the relevant libraries to produce a single executable
hello.c
a.out
gcc
hello.s
as
cpp
cc1
ld
Library files
e.g. math.o: the math library
hello.o

## Slide 8: Assembly Language
Is the binary representation of a program.
A symbolic representation of machine instructions
A set of instructions that the machine can directly execute
Notes: C

## Slide 9: Machine vs Assembly Language
Machine Language: A particular set of instructions that the CPU can directly execute – but these are ones and zeros
Assembly language is a symbolic version of the equivalent machine language
  each statement (called an Instruction), executes exactly one of a short list of simple commands
  Unlike in C (and most other High Level Languages), each line of assembly code contains at most 1 instruction
  Instructions are related to operations (e.g. =, +, -, *) in C or Java

## Slide 10: Steps in program translation
Program in C
Code Time
Compile Time
Compiler
Assembler
Instruction
Set
Architecture
Hardware
What makes programs run fast?
Algorithm
Compiler Translation to Machine code
ISA and hardware implementation

## Slide 11: What is the Instruction Set Architecture?
Agreed-upon interface between all the software that runs on the machine and the hardware that executes it
Primitive set of instructions a particular CPU implements
I/O system
Processor Memory
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Notes: the ISA is the HW/SW interface (book)
it is a useful abstraction in both directions.
More in Chapter 2

## Slide 12: General ISA Design Aspects
  Everything about h/w that is visible to the s/w and can be manipulated by it via basic machine instructions.
  Example: Registers: How many? What size?
  Memory: How to access contents?
  The set of basic machine instructions:
    What they are
    How they change the system state
    How they are encoded in binary
CPU
Bank of registers:
Small and fast storage location
Memory
Notes: the ISA is the HW/SW interface (book)
it is a useful abstraction in both directions.
More in Chapter 2

## Slide 13: Is the ISA different for different CPUs?
Different CPUs implement different sets of instructions.
  Examples: ARM, Intel x86, IBM/Motorola PowerPC (Macintosh), MIPS, Inter IA32 …
Two styles of CPU design:
  RISC (Reduced Instruction Set Computing)
  CISC (Complex Instruction Set Computing)

## Slide 14: RISC versus CISC (Historically)
Complex Instruction Set Computing e.g x86
  Larger instruction set
  More complicated instructions built into hardware
  Variable length
  Multiple clock cycles per instruction
Reduced Instruction Set Computing e.g. ARM
  Small, highly optimized set of instructions
  Memory accesses are specific instructions
  One instruction per clock cycle
  Instructions are of the same size and fixed format

## Slide 15: A = A*B
RISC
LOAD A, eax
LOAD B, ebx
PROD eax, ebx
STORE ebx, A
CISC
MULT B, A

## Slide 16: RISC vs CISC
RISC
More work for compiler
More RAM used to store instructions
Easier to debug: more reliable processors
Easier to optimize
  One clock cycle per instruction
CISC
Less work for compiler
Fewer instructions to store
Harder to maintain and debug

## Slide 17
 | High level Language to Assembly | Assembly to Machine Language
A | One-to-Many | Many-to-Many
B | Many-to-Many | One-to-One
C | One-to-Many | One-to-One
D | One-to-One | One-to-One
For a program written in a high-level-language, the conversion from ____ to _____ will be __________ for different target processors
Notes: C – Question was confusing, specify FOR ONE PROGRAM

## Slide 18: Translations
High-level language program (in C)
  swap (int v[], int k)
  { int temp;
  temp = v[k];
  v[k] = v[k+1];
  v[k+1] = temp;
  }
Assembly language program (for MIPS)
  swap: sll $2, $5, 2
  add $2, $4, $2
  lw $15, 0($2)
  lw $16, 4($2)
  sw $16, 0($2)
  sw $15, 4($2)
  jr $31
Machine (object, binary) code (for MIPS)
  000000 00000 00101 0001000010000000
  000000 00100 00010 0001000000100000
    . . .
C compiler
assembler
one-to-many
one-to-one
Notes: Computer only understands zeros and ones – instructions of 0’s and 1’s
Early programmers found representing machine instructions in a symbolic notation – assembly language
And developed programs that translate from assembler to machine code
Eventually, programmers found working even in assembler too tedious so migrated to higher-level languages and developed compilers that would translate from the higher-level languages to assembler

## Slide 19: Architecture vs Micro-architecture
Architecture:
Parts of processor design needed to write programs in assembly
What is visible to s/w
E.g Number of registers
Micro-Architecture:
Detail of how architecture is implemented
E.g Core frequency of the processor
Aside: Processor Speed:
Intel Core i7: 1.8 GHz
1.8 billion cycles per second
Each instruction takes some number of cycles

## Slide 20: The Assembly Programmer’s View of the machine
Registers: (Very) Small amount of memory inside the CPU
Each ARM register is 32 bits wide
  Groups of 32 bits called a word in ARM
Registers
CPU
Memory
Stack
Address
Data
Instructions
Instructions
Data

## Slide 21: The ARM Register Set
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
General Purpose Registers
Special Purpose Registers
Notes: This animated slide shows the way that the banking of registers works. On the left the currently visible set of registers are shown for a particular mode.
On the right are the registers that are banked out whilst in that mode.
Each key press will switch mode:
user -> FIQ ->user -> IRQ -> user ->SVC -> User -> Undef -> User -> Abort and then back to user.
The following slide then shows this in a more static way that is more useful for reference

## Slide 22: Assembly Variables: Registers
Unlike HLL like C or Java, assembly cannot use variables
  Why not? Keep Hardware Simple
Data is put into a register before it is used for arithmetic, tested, etc.
Manipulated data is then stored back in main memory.
Benefit: Since registers are directly in hardware, they are very fast

## Slide 23: C, Java Variables vs. Registers
In C (and most High Level Languages) variables declared first and given a type
  Example: int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix and match int and char variables).
In Assembly Language, the registers have no type; operation determines how register contents are treated

## Slide 24: Which one of the following is an optimization that is typically done by ARM compilers?
Put the address of frequently used data in registers
Put the value of frequently used data in registers
Put as much data as possible in the registers
Put as few program data in the registers
Registers are not available to the programmer/compiler – they are only used internally by the processor to fetch and decode instructions

## Slide 25: Layout of instructions in memory
  swap (int v[], int k)
  { int temp;
  temp = v[k];
  v[k] = v[k+1];
  v[k+1] = temp;
  }
  0x4000 Swap: mov r2, r5
  0x4004 add r4, r2, #1
  0x4008 ldr r10, [r6,r2]
  0x400c ldr r11, [r6,r4]
  0x4010 mov r1, r10
  0x4014 str r11,[r6,r2]
  0x4018 str r1, [r6,r4]
  0x401c bx lr

## Slide 26: Machine Instructions
Can be thought of as numbers.
Are commands the computer performs.
Were what people originally wrote programs using.
All of the above.
Notes: D

## Slide 27: Machine Instructions
Can be thought of as numbers.
Are commands the computer performs.
Were what people originally wrote programs using.
All of the above.
Notes: D

## Slide 28: Steps in program execution
PC:0x4000
CPU
Memory
Stack
Instructions
Data
  0x4000 Swap: mov r2, r5
  0x4004 add r4, r2, #1
  0x4008 ldr r10, [r6,r2]
  0x400c ldr r11, [r6,r4]
  0x4010 mov r1, r10
  0x4014 str r11,[r6,r2]
  0x4018 str r1, [r6,r4]
  0x401c bx lr

## Slide 29: Assembly Language
Is in binary.
Allows languages to be designed for their specific uses.
Has one line for every machine language instruction.
Notes: C

## Slide 30: Basic Types of Instructions
Arithmetic: Only processor and registers involved
  compute the sum (or difference) of two registers, store the result in a register
  move the contents of one register to another
Data Transfer Instructions: Interacts with memory
  load a word from memory into a register
  store the contents of a register into a memory word
Control Transfer Instructions: Change flow of execution
  jump to another instruction
  conditional jump (e.g., branch if registeri == 0)
  jump to a subroutine

## Slide 31
High Level Language Program
Assembly Language Program
Compiler
Machine Interpretation
Machine Language Program
Assembler
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
How to Speak Computer
Notes: Draw what they cover in this class and where they may see other elements in other classes (compilers, for example). I also draw what we cover in our lab.

## Slide 32: How to Speak Computer
High Level Language Program
Assembly Language Program
Compiler
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
Machine Interpretation
Machine Language Program
Assembler
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
Notes: Draw what they cover in this class and where they may see other elements in other classes (compilers, for example). I also draw what we cover in our lab.

## Slide 33: How to Speak Computer
High Level Language Program
Assembly Language Program
Compiler
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
Machine Interpretation
Machine Language Program
Assembler
1000110001100010000000000000000
1000110011110010000000000000100
1010110011110010000000000000000
1010110001100010000000000000100
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
Notes: Draw what they cover in this class and where they may see other elements in other classes (compilers, for example). I also draw what we cover in our lab.

## Slide 34: How to Speak Computer
High Level Language Program
Assembly Language Program
Compiler
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
Machine Interpretation
Machine Language Program
Assembler
1000110001100010000000000000000
1000110011110010000000000000100
1010110011110010000000000000000
1010110001100010000000000000100
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
Machine does something!
Notes: Draw what they cover in this class and where they may see other elements in other classes (compilers, for example). I also draw what we cover in our lab.