## Slide 1: Single-Cycle Processor Design
CS 3220
Fall 2014
Hadi Esmaeilzadeh
hadi@cc.gatech.edu
Georgia Institute of Technology
Some slides adopted from Prof. Milos Prvulovic
Notes: Color code: 6699CC, 3399CC

## Slide 2: Single-Cycle Approach
Entire instruction done in only one cycle
Data-moving takes only time it really needs (wires)
  E.g. dedicated wire to take reg output to ALU input
Control takes only as much time as it really needs
  Figure out all control signals right after inst read from imem
  Takes only part of one cycle, because one is all we have
All major units get used in every cycle
  Unless the unit is not needed for a specific instruction
But…“enhancements” become “necessities”
  Example: Branch uses ALU to compare, need separate PC+4+4*imm
  Each cycle, need to read two registers read and writte one
  Etc.
And… longest-to-do instruction determines clock
  Usually a load, so all other insts will have slack for memory read

## Slide 3: Single-cycle
Instr
Mem
P
C
RF
+
4
Control
Supported:
ADD

## Slide 4: Look at that register file!
module RegFile(RADDR1,DOUT1,RADDR2,DOUT2,WADDR,DIN,WE,CLK);
parameter DBITS; // Number of data bits
parameter ABITS; // Number of address bits
parameter WORDS = (1<<ABITS);
parameter MFILE = "";
reg [(DBITS-1):0] mem[(WORDS-1):0];
input [(ABITS-1):0] RADDR1,RADDR2,WADDR;
input [(DBITS-1):0] DIN;
output wire [(DBITS-1):0] DOUT1,DOUT2;
input CLK,WE;
always @(posedge CLK)
if(WE)
mem[WADDR]=DIN;
assign DOUT1=mem[RADDR1];
assign DOUT2=mem[RADDR2];
endmodule
Three separate accesses
  Two reads
  One write
Each with it own address!

## Slide 5: Wire it up
wire [3:0] rregno1=rs, rregno2=rt;
wire [(DBITS-1):0] regout1,regout2;
wire [3:0] wregno=rd;
// This comes from decoding logic
// (reg becomes wire in non-edge always block)
reg wrreg;
reg [(DBITS-1):0] wregval;
// Now instantiate the register file module
RegFile #(.DBITS(DBITS),.ABITS(5), regFile(
.RADDR1(rregno1),.DOUT1(regout1),
.RADDR2(rregno2),.DOUT2(regout2),
.WADDR(wregno), .DIN(wregval),
.WE(wrreg),.CLK(clk));

## Slide 6: Wire it up - ALU
// ALU input 1 is always the first source register
wire [(DBITS-1):0] aluin1=regout1;
// ALU input 2 is decided by control logic
// (either regout2 or immediate)
reg [(DBITS-1):0] aluin2;
// Decided by control logic
reg [4:0] alufunc;
// Output of the ALU (becomes wire b/c of always block below)
reg [(DBITS-1):0] aluout;
always @(alufunc or aluin1 or aluin2)
case(alufunc)
OP2_AND: aluout=aluin1&aluin2;
... // Same as in Project 2
... // but uses aluin1 and aluin2 instead of A and B
// Used by control logic for conditional branches
wire cond=aluout[0];

## Slide 7: Control Logic
always @(opcode1 or opcode2 or ry or rz) begin
{aluimm,alufunc,isbranch,isjump,wrmem}=
{ 1'bX, 5'hXX, 1'b0, 1'b0, 1'b0};
{selaluout,selmemout,selpcplus,wrreg}=
{ 1'bX, 1'bX, 1'bX, 1'b0};
case(opcode1)
OP1_ALUR:
{aluimm, alufunc, selaluout,selmemout,selpcplus,wrreg}=
{ 1'b0,{1’b0,op2_i}, 1'b1, 1'b0, 1'b0, 1'b1};
OP1_ALUI:
{aluimm, alufunc, selaluout,selmemout,selpcplus,wrreg}=
{ 1'b1,{1’b0,op2_t}, 1'b1, 1'b0, 1'b0, 1'b1};
…

## Slide 8: Single-cycle
Instr
Mem
P
C
RF
4
Control
Supported:
ADD, ADDI
SE
M
X

## Slide 9: Single-cycle
Instr
Mem
P
C
RF
4
Control
Supported:
All ALUR, ALUI insts
SE
M
X

## Slide 10: Single-cycle
Instr
Mem
P
C
RF
4
Control
Supported:
ALUR, ALUI LW
SE
M
X
Data
Mem
M
X
A

## Slide 11: Single-cycle
Instr
Mem
P
C
RF
4
Control
Supported:
ALUR, ALUI LW, SW
SE
M
X
Data
Mem
M
X
D
A

## Slide 12: Single-cycle
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
4
A
D
Control
Supported:
ALUR, ALUI
LW, SW
BCOND
aluout[0]

## Slide 13: And it’s not done yet!
Instr
Mem
P
C
M
X
RF
Data
Mem
M
X
M
X
SE
4
A
D
Control
Supported:
ALUR, ALUI, LW, SW, BCOND
JAL

## Slide 14: How do we do all this?
The only real “state” is the PC, Regs, and Mem
  The rest is just wires and combinatorial logic
Central control takes opcode, generates all signals for the entire instruction!
But can have other small pieces of control
  E.g. decide if PC+4 or PC+4+Offs loaded into PC on a conditional branch instruction, or to load a register for the JAL instruction